## Slide 1: WF for harmonic issues for EN-DC and NR CA CHTTL
3GPP TSG-RAN WG4 Meeting #88bis R4-1813801 Chengdu, China, 8th – 12th October, 2018

## Slide 2: Backgrounds
Lots of blanks still remain in the current MSD table due to the harmonic exception in TS 38.101-1 and TS 38.101-3
  It is confused what the meaning of the blank is --
    The MSD value is zero
    There will be harmonic issues in the corresponding DL channel bandwidths but the MSD is not specified for some reasons
    The DL channel bandwidth is not supported

## Slide 3: WayForward
Wayforward for the MSD due to harmonic exception for the DL band including EN-DC and NR CA
  For the MSD table due to harmonic exception in TS 38.101-1 Table 7.3A.4-1 and TS 38.101-3 Table 7.3B.2.3.1-1
    For direct hit harmonic exception, the MSD is defined at least up to the DL channel BW with consideration of full overlapping between the UL harmonics and the DL channel bandwidth
      The MSD for larger DL channel bandwidth can be added or at least specified as “N/A” with a note below in the table
        NOTE: No requirements apply when there is at least one individual RE within the uplink transmission bandwidth of the low band for which up to 5th transmitter harmonic is within the downlink transmission bandwidth of the high band. The reference sensitivity is only verified when this is not the case (the requirements specified in TS 38.101-1 clause 7.3.2 apply unless otherwise specified).
    The form remains empty only when the channel BW is not supported in the DL band
MSD due to harmonic exception for the DL band |  |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz
 |  | dB | dB | dB | dB | dB | dB | dB | dB | dB | dB | dB | dB
n3 | n771,2 |  | 23.9 | 22.1 | 20.9 |  |  | 17.9 | 16.9 | 16.1 | FFS | FFS | FFS
 | n773 |  | 1.1 | 0.8 | 0.3 |  |  | 0 | 0 | 0 | 0 | 0 | 0
FFS to be MSD value or N/A |  |  |  |  |  |  |  |  |  |  |  |  | 
The table below is just for example:

## Slide 4: Appendix 1:
MSD due to harmonic exception for the DL band |  |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz
 |  | dB | dB | dB | dB | dB | dB | dB | dB | dB | dB | dB | dB
n3 | n771,2 |  | 23.9 | 22.1 | 20.9 |  |  | 17.9 | 16.9 | 16.1 |  |  | 
 | n773 |  | 1.1 | 0.8 | 0.3 |  |  |  |  |  |  |  | 
n3 | n781,2 |  | 23.9 | 22.1 | 20.9 |  |  | 17.9 | 16.9 | 16.1 |  |  | 
 | n783 |  | 1.1 | 0.8 | 0.3 |  |  |  |  |  |  |  | 
n8 | n784,5 |  | 10.8 | 9.1 | 8.0 |  |  | 5.1 | 4.2 | 3.5 | 2.3 |  | 1.4
n8 | n781,2 |  | 10.8 | 9.1 | 8 |  |  | 3.5 | 2.3 | 1.4 |  |  | 
n8 | n791,2 |  |  |  |  |  |  | [6.8] | 6.2 | [5.6] | 4.9 |  | 4.4
n28 | n751,2 | 28.1 | 25.3 | 24.0 | 22.8 |  |  |  |  |  |  |  | 
 | n781,2 |  | [10.4] | [8.9] | [7.8] |  |  | [4.7] | [3.7] | [3] | [1.7] | [1.2] | [0.7]
Table 7.3A.4-1: Reference sensitivity exceptions due to UL harmonic for NR CA FR1 3GPP TS 38.101-1 V15.3.0 (2018-09)

## Slide 5: Appendix 2:
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm)
1, 3 | n771,2 | 27.1 | 23.9 | 22.1 | 20.9 |  |  | 17.9 |  |  |  |  | 
 | n773 | 1.9 | 1.1 | 0.8 | 0.3 |  |  |  |  |  |  |  | 
2 | n781,2 | 27.1 | 23.9 | 22.1 | 20.9 |  |  | 17.9 |  |  |  |  | 
 | n783 | 1.9 | 1.1 | 0.8 | 0.3 |  |  |  |  |  |  |  | 
3 | n781,2 | 27.1 | 23.9 | 22.1 | 20.9 |  |  | 17.9 |  |  |  |  | 
 | n783 | 1.9 | 1.1 | 0.8 | 0.3 |  |  |  |  |  |  |  | 
8 | n776,7 n786,7 | NA | 10.8 | 9.1 | 8 | 5.1 | 4.2 | 3.5 | 2.3 | 1.4 |  |  | 
8 | n794,5 |  |  |  |  |  |  | 6.8 | 6.2 | 5.6 | 4.9 |  | 4.4
18， 19 | n774,5 |  | 10.4 | 8.9 | 7.8 |  |  | 4.7 | 3.7 | 3 | 1.7 |  | 0.7
28 | n774,5 n784,5 |  | 10.4 | 8.9 | 7.8 |  |  | 4.7 | 3.7 | 3 | 1.7 | 1.2 | 0.7
20 | n776,7 n786,7 |  | 10.8 | 9.1 | 8 |  |  | 6 |  |  |  |  | 
26 | n41 | NA | 10.3 | 8.4 | 7.4 |  |  | 5 | 4.3 | 3.9 | 3.1 | 2.7 | 
26 | n776,7 n786,7 |  | 10.8 | 9.1 | 8 |  |  | 6 |  |  |  |  | 
26 | n774,5 |  | 10.4 | 8.9 | 7.8 |  |  | 4.7 | 3.7 | 3 | 1.7 |  | 0.7
n28 | 18,9,10 | 10.2 | 7.6 | 6.2 | 5.3 |  |  |  |  |  |  |  | 
 | n751,2 | 28.1 | 25.3 | 24.0 | 22.8 |  |  |  |  |  |  |  | 
n71 | 211 | 4.6 | 1.0 | 0.7 | 0.6 |  |  |  |  |  |  |  | 
 | 212 | 1.7 | 1.0 | 0.7 | 0.6 |  |  |  |  |  |  |  | 
66 | n781,2 |  | 23.9 | 22.1 | 20.9 |  |  | 17.9 |  |  |  |  | 
 | n783 |  | 1.1 | 0.8 | 0.3 |  |  |  |  |  |  |  | 
Table 7.3B.2.3.1-1: MSD due to UL harmonic for EN-DC in NR FR1 3GPP TS 38.101-3 V15.3.0 (2018-09)