## Slide 1: WF A-MPR for CA_66B and CA_66C with CA_NS_09
Qualcomm, Inc.
3GPP TSG-RAN WG4#88Bis Meeting R4-1813808
Chengdu, China, 8 – 12 October 2018
Agenda 6.16.1

## Slide 2: Background
It is not good enough to introduce only AMPR only for certain BW class.
The full set of RF requirements must be introduced.
This WF describes what needs to be added along with A-MPR for CA_66B and CA_66C

## Slide 3: WF to add all RF requirements
CR to modify 36.715 TR
CR to modify 36.101 TS
  Add combinations to CA UE Power Class for intra-band contiguous CA
    Table 6.2.2A-1
  Add combinations to reference table for requirements clause and A-MPR
    Table 6.2.4A-1
  Add note in 6.2.4A to indicate exception to setting CA MPR  0dB
    It was shown from simulations and measurement that CA_NS_09 AMPR did not exceed the CA MPR
    Section 6.2.4A – include exception for CA_NS_09
  Add table entries for spurious emission requirements for protected bands
    Table 6.6.3.2A-1
  Add entries for UL REFSENS configuration
    Table 7.3.1A-0 for Class B – add new UL combinations
    Table 7.3.1A-1 for Class C

## Slide 4: Add combinations to CA UE Power Class for intra-band contiguous CA
Table 6.2.2A-1: CA UE Power Class for intraband contiguous CA
E-UTRA CA Configuration | Class 1 (dBm) | Tolerance (dB) | Class 2 (dBm) | Tolerance (dB) | Class 3 (dBm) | Tolerance (dB) | Class 4 (dBm) | Tolerance (dB)
CA_1C |  |  |  |  | 23 | +2/-2 |  | 
CA_3C |  |  |  |  | 23 | +2/-22 |  | 
CA_5B |  |  |  |  | 23 | +2/-22 |  | 
CA_7C |  |  |  |  | 23 | +2/-22 |  | 
CA_8B |  |  |  |  | 23 | +2/-22 |  | 
CA_38C |  |  |  |  | 23 | +2/-2 |  | 
CA_39C |  |  |  |  | 23 | +2/-2 |  | 
CA_40C |  |  |  |  | 23 | +2/-2 |  | 
CA_40D |  |  |  |  | 23 | +2/-2 |  | 
CA_41C |  |  | 26 | +2/-22 | 23 | +2/-22 |  | 
CA_42C |  |  |  |  | 23 | +2/-3 |  | 
CA_66B |  |  |  |  | 23 | +2/-2 |  | 
CA_66C |  |  |  |  | 23 | +2/-2 |  | 
NOTE 1: Void NOTE 2: If all transmitted resource blocks (Figure 5.6A-1) over all component carriers are confined within FUL_low and FUL_low + 4 MHz or/and FUL_high – 4 MHz and FUL_high, the maximum output power requirement is relaxed by reducing the lower tolerance limit by 1.5 dB NOTE 3: PPowerClass is the maximum UE power specified without taking into account the tolerance NOTE 4: For intra-band contiguous carrier aggregation the maximum power requirement should apply to the total transmitted power over all component carriers (per UE). |  |  |  |  |  |  |  | 
Details

## Slide 5: Add combinations to reference table for requirements clause and A-MPR
Table 6.2.4A-1: Additional Maximum Power Reduction (A-MPR) for intra-band contiguous CA
CA Network Signalling value | Requirements (subclause) | Uplink CA Configuration | A-MPR [dB] (subclause)
CA_NS_01 | 6.6.3.3A.1 | CA_1C | 6.2.4A.1
CA_NS_02 | 6.6.3.3A.2 | CA_1C | 6.2.4A.2
CA_NS_03 | 6.6.3.3A.3 | CA_1C | 6.2.4A.3
CA_NS_04 | 6.6.2.2A.1, 6.6.3.3A.8 | CA_41C | 6.2.4A.4
CA_NS_05 | 6.6.3.3A.4 | CA_38C | 6.2.4A.5
CA_NS_06 | 6.6.3.3A.5 | CA_7C | 6.2.4A.6
CA_NS_07 | 6.6.3.3A.6 | CA_39C | 6.2.4A.7
CA_NS_08 | 6.6.3.3A.7 | CA_42C | 6.2.4A.8
CA_NS_09 | TBD | CA_66B,CA_66C | N/A
… |  |  | 
CA_NS_31 | NOTE 1 | Table 5.6A.1-1 (NOTE 1) | N/A
CA_NS_32 | Reserved |  | 
NOTE 1: Applicable for uplink CA configurations listed in Table 5.6A.1-1 for which none of the additional requirements in subclauses 6.6.2.2A or 6.6.3.3A apply. NOTE 2: The index of the sequence CA_NS corresponds to the value of additionalSpectrumEmissionSCell-r10. |  |  | 

## Slide 6: Add note in 6.2.4A to indicate exception to setting CA MPR  0dB
6.2.4A UE maximum output power with additional requirements for CA
Additional ACLR, spectrum emission and spurious emission requirements for carrier aggregation can be signalled by the network to indicate that the UE shall also meet additional requirements in a specific deployment scenario. To meet these additional requirements, Additional Maximum Power Reduction (A-MPR) is allowed for the CA Power Class as specified in Table 6.2.2A-1.
If for intra-band carrier aggregation the UE is configured for transmissions on a single serving cell, then subclauses 6.2.3 and 6.2 4 apply with the Network Signaling value indicated by the field additionalSpectrumEmission.
For intra-band contiguous aggregation with the UE configured for transmissions on two serving cells, the maximum output power reduction specified in Table 6.2.4A-1 is allowed for all serving cells of the applicable uplink CA configurations according to the CA network signalling value indicated by the field additionalSpectrumEmissionSCell-r10. Then clause 6.2.3A does not apply, i.e. the carrier aggregation MPR = 0dB, unless the value indicated is CA_NS_31 and CA_NS_09. For uplink 64 QAM and 256 QAM, the applied maximum output power reduction is obtained by taking the maximum value of MPR requirements specified in Table 6.2.3A-1 and A-MPR requirements specified in Table 6.2.4A-1.

## Slide 7: Add table entries for intra-band CA spurious emission requirements for protected bands
Table 6.6.3.2A-1: Requirements for intra-band carrier aggregation
E-UTRA CA Configuration | Spurious emission |  |  |  |  |  | 
 | Protected band | Frequency range (MHz) |  |  | Maximum Level (dBm) | MBW (MHz) | NOTE
CA_1C | E-UTRA Band 1, 7, 8, 11, 18, 19, 20, 21, 22, 26, 27, 28, 31, 32, 38, 40, 41, 42, 43, 44, 50, 51, 52, 65, 67, 72, 73, 74, 75, 76 | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 3 | FDL_low | - | FDL_high | -50 | 1 | 10
CA_3C | E-UTRA Band 1, 7, 8, 20, 26, 27, 28, 31, 32, 33, 34, 38, 41, 43, 44, 50, 51, 65, 67, 72, 73, 74, 75, 76 | FDL_low | - | FDL_high | -50 | 1 | 
 | E-UTRA Band 3 | FDL_low | - | FDL_high | -50 | 1 | 10
 | E-UTRA Band 22, 42, 52 | FDL_low | - | FDL_high | -50 | 1 | 2
… | …. |  |  |  |  |  | 
CA_66B | E-UTRA Band 1, 2, 3, 4, 5, 8, 10, 12, 13 , 14, 17, 24, 25, 26, 27, 28, 29, 30, 34, 39, 40, 41, 42, 44, 50, 51, 52, 65, 70, 71, 73, 74, 85 | FDL_low | - | FDL_high | -50 | 1 | 
CA_66C | E-UTRA Band 1, 2, 3, 4, 5, 7, 8, 10, 11, 18, 19, 20, 21, 25, 26, 27, 28, 31, 32, 33, 34, 38, 40, 41, 42, 44, 50, 51, 65, 67, 72, 73, 74, 75, 76 | FDL_low | - | FDL_high | -50 | 1 | 

## Slide 8: UL Configurations for REFSENS –BW Class B
Table 7.3.1A-0h: Intra-band contiguous CA uplink configuration for reference sensitivity for Bandwidth Class B
Will add as needed in CR – example below
CA configuration / CC combination / NRB_agg / Duplex mode |  |  |  |  |  |  |  |  | 
Uplink CA configuration | 25RB+25RB |  | 50RB+25RB |  | 50RB+50RB |  | 75RB+25RB |  | Duplex Mode
 | PCC | SCC | PCC | SCC | PCC | SCC | PCC | SCC | 
CA_5B | N/A | N/A | 25 | 0 | 25 | 0 | N/A | N/A | FDD
CA_8B | N/A | N/A | 25 | 0 | 25 | 0 | N/A | N/A | FDD
CA_66B | 25 | 25 | 50 | 25 | 50 | 50 | 75 | 25 | FDD
NOTE 1: The carrier centre frequency of SCC in the UL operating band is configured closer to the DL operating band. NOTE 2: The transmitted power over both PCC and SCC shall be set to PUMAX as defined in subclause 6.2.5A. NOTE 3: The UL resource blocks in both PCC and SCC shall be confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.6-1). NOTE 4: The UL resource blocks in PCC shall be located as close as possible to the downlink operating band, while the UL resource blocks in SCC shall be located as far as possible from the downlink operating band. NOTE 5: In case a CA configuration consists of CC channel bandwidths which are unequal in bandwidth the PCC channel bandwidth shall be the larger one for reference sensitivity test. |  |  |  |  |  |  |  |  | 

## Slide 9: UL Configurations for REFSENS –BW Class C
Table 7.3.1A-1: Intra-band contiguous CA uplink configuration for reference sensitivity for Bandwidth Class C
CA configuration / CC combination / NRB_agg / Duplex mode |  |  |  |  |  |  |  |  |  |  |  |  | 
Uplink CA configuration | 100RB+25RB |  | 100RB+50RB |  | 75RB+75RB |  | 75RB+50RB |  | 100RB+75RB |  | 100RB+100RB |  | Duplex Mode
 | PCC | SCC | PCC | SCC | PCC | SCC | PCC | SCC | PCC | SCC | PCC | SCC | 
CA_1C | N/A | N/A | N/A | N/A | 75 | 54 | N/A | N/A | N/A | N/A | 100 | 30 | FDD
CA_3C | 50 | 0 | 50 | 0 | N/A | N/A | N/A | N/A | 50 | 0 | 50 | 0 | FDD
CA_7C | N/A | N/A | 75 | 0 | 75 | 0 | 75 | 0 | 75 | 0 | 75 | 0 | FDD
CA_38C | N/A | N/A | N/A | N/A | 75 | 75 | N/A | N/A | N/A | N/A | 100 | 100 | TDD
CA_39C | 100 | 25 | 100 | 50 | N/A | N/A | N/A | N/A | 100 | 75 | N/A | N/A | TDD
CA_40C | N/A | N/A | 100 | 50 | 75 | 75 | N/A | N/A | 100 | 75 | 100 | 100 | TDD
CA_41C | 100 | 25 | 100 | 50 | 75 | 75 | 75 | 50 | 100 | 75 | 100 | 100 | TDD
CA_42C | 100 | 25 | 100 | 50 | N/A | N/A | N/A | N/A | 100 | 75 | 100 | 100 | TDD
CA_66C | 100 | 25 | 100 | 50 | 75 | 75 | 75 | 50 | 100 | 75 | 100 | 100 | FDD
NOTE 1: The carrier centre frequency of SCC in the UL operating band is configured closer to the DL operating band. NOTE 2: The transmitted power over both PCC and SCC shall be set to PUMAX as defined in subclause 6.2.5A. NOTE 3: The UL resource blocks in both PCC and SCC shall be confined within the transmission bandwidth configuration for the channel bandwidth (Table 5.6-1). NOTE 4: The UL resource blocks in PCC shall be located as close as possible to the downlink operating band, while the UL resource blocks in SCC shall be located as far as possible from the downlink operating band. NOTE 5: In case a CA configuration consists of CC channel bandwidths which are unequal in bandwidth the PCC channel bandwidth shall be the larger one for reference sensitivity test. NOTE 6: Void. NOTE 7: Void |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: References
R4-18123333, “TP for Rel-15 Intra-band 36.715-00-00 for CA_2DL_ 66B_2UL_66B_BCS0 and CA_2DL_ 66C_2UL_66C_BCS0”, Qualcomm, Inc., 3GPP RSG-RAN WG4 Meeting #88-bis, Chengdu, China, Oct. 8-12, 2018.