## Slide 1: WF on CA_n71B MSD in Rel.16 T-Mobile USA, Skyworks Solutions Inc.,….
3GPP TSG-RAN WG4 Meeting #88bis R4-1813835 Chengdu, China, 8 – 12 October 2018

## Slide 2: Background
CA_n71B is introduced for Release 16 in [1]
It enables up to 25MHz aggregated contiguous spectrum in DL and up to 20MHz aggregated contiguous spectrum in UL with channel arrangements below.
E-UTRA CA configuration / Bandwidth combination set |  |  |  |  | 
NR CA configuration | Uplink CA configurations | Component carriers in order of increasing carrier frequency |  | Aggregated bandwidth (MHz) | Bandwidth combination set
 |  | Channel bandwidths for carrier (MHz) | Channel bandwidths for carrier (MHz) |  | 
CA_n71B | - | 5 | 20 | 25 | 0
 |  | 10 | 15 |  | 
 |  | 15 | 10 |  | 
 |  | 20 | 5 |  | 
Table 5.1.1-1: Supported bandwidth combinations for CA_n71B

## Slide 3: Background
Skyworks flagged the document [1] as it was stating that “There are no REFSENS exceptions for this combination.” which isn't accurate since MSD is anticipated
In fact for band n71, 15MHz and 20MHz channel bandwidths REFSENS already suffer from transmitter excess noise and it can only be further the case if 5MHz extra aggregated bandwidth is added on the side closest to the UL
Although measurements are already available for 25MHz aggregated DL with DC_(n)71AA, these are for different channel arrangements and different UL configurations and cannot apply here.
[1] will be revised to put REFSENS exceptions is FFS and current way forward proposes the test point for further MSD study.

## Slide 4: Proposals
REFSENS exception due to transmit band proximity.
Worst case test point:
  Pcell UL: 20MHz channel DFT-S-OFDM QPSK at 673MHz with 20RB0 allocation
  Pcell DL: 20MHz channel at 627MHz (26MHz away from UL)
  Scell DL: 5MHz DL at 639.5MHz (21MHz away from UL)
  All for 15kHz SCS
  This is the worst case as the 5MHz REFSENS is the lowest thus will show the highest de-sense. Pcell REFSENS should be unchanged compared to n71 20MHz channel BW.
Additional test points with wider DL Scell bandwidths and different SCS are not precluded
Input should be provided to RAN4#89 meeting

## Slide 5: Reference
  [1] R4-1812793, “TP for TR 38.716-01-01: CA_71B”, Ericsson, T-Mobile US, RAN4#88bis