## Slide 1: WF on SDR requirement for NR
NTT DOCOMO, …
3GPP TSG-RAN WG4 Meeting #88bis R4-1813929
Chengdu, China, 8 – 12 October 2018

## Slide 2: Background 1/3 Agreements at RAN4 #88 (R4-1811394)
SDR test methodology
  Use the following procedure for NR SDR testing
    Calculate data rate using equation from TS 38.306 for each CA bandwidth combination from CA bandwidth combinations supported by UE, taking into account channel bandwidth size, SCS and various UE capabilities (i.e. maximum MIMO layers capability, maximum supported modulation order and scaling factor)
    Use CA bandwidth combination which allows achieving maximum data rate for SDR test
    MCS and TBS used for each CC is selected based on test parameters and on indicated UE capabilities including MIMO layers, modulation and scaling factor
      Exact MCS/TBS for SDR testing are FFS and companies encouraged to bring proposals on the MCS selection
        Option 1: Define look up table to derive MCS and TBS parameters based on UE capabilities
        Option 2: Define a procedure to derive MCS and TBS parameters based on UE capabilities
        Other options not precluded

## Slide 3: Background 2/3 Agreements at RAN4 #88 (R4-1811394)
SDR test parameters
  The channel bandwidths for SDR requirements are as follows.
    FR1, 15kHz SCS: 5, 10, 15, 20, 25, 30, 40, 50 MHz
    FR1, 30kHz SCS: 5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 100 MHz
    FR2, 60kHz SCS: 50, 100, 200 MHz
    FR2, 120kHz SCS: 50, 100, 200, [400] MHz
  PDSCH Type A mapping with duration [14] OFDM symbols
  CORESET size in time domain is 1 OFDM symbol.
    FFS: CORESET size in frequency domain and FDM of CORESET and PDSCH
  List of UE MIMO layer capabilities for SDR requirements: {1, 2, 4} for FR1, and {1, 2} for FR2.
  List of supported modulation scheme for DL by the UE for SDR requirements
    FR1: up to 256QAM
    FR2: up to 64QAM
  DMRS configuration
    Option 1: No additional DMRS
    Option 2: with 1 additional DMRS
  Consider FDM of DMRS and PDSCH to increase TBS in a slot.
  PTRS will be configured for FR2,detalied for configuration FFS
  For SDR requirement, for TBS determination is set to 0 for FR1 and [6]for FR2.

## Slide 4: Background 3/3 Agreements at RAN4 #88bis (on Wed.)
DMRS configuration
  1 additional DRMS for SDR test
PTRS configuration
  PTRS configuration for FR2: 1 port, per 2PRB in frequency domain, per symbol in time domain.
SSB configuration
  One SSB is configured in each SSB burst with periodicity 20 ms and slot #0 within period
TDD configuration
  FR1 15kHz: DDDSU
  FR1 30KHz: 7D1S2U
  FR2 60kHz: DDSU
Test metric
  85% relative throughput.
Channel bandwidth
  for simulation campaign for SDR test, we just need to consider one channel bandwidth per SCS per TDD or FDD set.

## Slide 5: Proposals 1/2
MCS/TBS determination
  Adopt the methodology in Section 2.1 of R4-1812165
CSI-RS for tracking (TRS):
  For FR1 and FR2, 20ms periodicity with 2 slot, offset 10ms from SSB slot
CSI-RS for CSI acquisition:
  [For FR1 and FR2, mapping in slots with SSB in OFDM symbols without SSB]
PDSCH scheduling
  No PDSCH scheduling in SSB slots and TRS slots
  No FDM between CORESET and PDSCH
Number of HARQ process
  FFS: 8/4 processes for TDD/FDD soft combining verification test with 16/8 process for TDD/FDD
NR TDD configuration for FR2 120kHz
  Alt.1: DDDSU
  Alt.2: DDSU

## Slide 6: Proposals 2/2
Introduce SDR requirements at least the following scenarios in Rel.15
  Single carrier
  NR CA within only FR1
  NR CA within only FR2
  EN-DC within only FR1
    Maximum archivable data rate for NR side is calculated based on the methodology in Section 2.1 of R4-1812165.
    Maximum archivable data rate for LTE side is calculated based on Section 4.1.2 of TS38.306 (V15.3.0)
  FFS: NR CA including both FR1 and FR2 bands (no testability)
  FFS: EN-DC including both FR1 and FR2 bands (no testability)
RAN4 will introduce two kind of SDR requirements
  1. The highest MCS based on UE capability without any restriction of testable SNR
  2. The highest MCS achieved within testable SNR range in Rel.15
  Note: Only the first is tested if the test is feasible. Only the second one is tested if the test for the first is infeasible.
If RAN4 introduce SDR for EN-DC including FR1 NR carrier, update LTE FRC such that LTE TDD carrier is synchronized with FR1 NR TDD carrier

## Slide 7: Simulation assumption for RAN4 #89 1/5
Simulation cases for single carrier:
Companies are encouraged to provide simulation results with the following two MCS conditions
  The highest MCS based on UE capability without any restriction of testable SNR
  The highest MCS achieved within testable SNR range in Rel.15
Further detailed parameters are described in the next slides
Test case | FR | SCS | Duplex mode | CBW | MIMO config. | Max rank | Max modulation order
Case 1 | FR1 | 15kHz | FDD | 20MHz | 2x2MIMO | Rank 2 | 64QAM
Case 2 | FR1 | 15kHz | FDD | 20MHz | 2x2MIMO | Rank 2 | 256QAM
Case 3 | FR1 | 15kHz | FDD | 20MHz | 4x4MIMO | Rank 4 | 64QAM
Case 4 | FR1 | 15kHz | FDD | 20MHz | 4x4MIMO | Rank 4 | 256QAM
Case 5 | FR1 | 30kHz | TDD | 100MHz | 2x2MIMO | Rank 2 | 64QAM
Case 6 | FR1 | 30kHz | TDD | 100MHz | 2x2MIMO | Rank 2 | 256QAM
Case 7 | FR1 | 30kHz | TDD | 100MHz | 4x4MIMO | Rank 4 | 64QAM
Case 8 | FR1 | 30kHz | TDD | 100MHz | 4x4MIMO | Rank 4 | 256QAM
Case 9 | FR2 | 60kHz | TDD | 100MHz | 2x2MIMO | Rank2 | 64QAM
Case 10 | FR2 | 120kHz | TDD | 100MHz | 2x2MIMO | Rank2 | 64QAM

## Slide 8: Simulation assumption for RAN4 #89 2/5
Note:
For FR2 requirement, testable SNR is scaled down as (aggregated) channel bandwidth is scaled up
  Ex. If maximum testable SNR for 50MHz is XdB, that for 100MHz is (X – 3)dB
For FR2 SDR requirements, (aggregated) channel bandwidth for NR is up to 800MHz in Rel.15
In future release, testable SNR may be improved, and we need to inform to RAN5 what is testable MCS and rank limitation for SDR requirements
For forward compatibility, RAN4 will define MCS to SNR mapping table for all possible MCS and rank combinations.

## Slide 9: Simulation assumption for RAN4 #89 3/5
Parameter |  | Unit | Value
PDSCH transmission scheme |  |  | Transmission scheme 1
EPRE ratio of PTRS to PDSCH |  | dB | N/A
Channel bandwidth |  | MHz | See slide #6
Common serving cell parameters | Physical Cell ID |  | 0
 | SSB position in burst |  | First SSB in Slot #0
 | SSB periodicity | ms | 20
 | First DMRS position for Type A PDSCH mapping |  | 2
Active DL BWP index |  |  | 1
DL BWP configuration #1 | First PRB |  | 0
 | Number of contiguous PRB |  | Full allocation
 | Subcarrier spacing | kHz | See slide #6
 | Cyclic prefix |  | Normal
PDCCH configuration | Slots for PDCCH monitoring |  | Each slot
 | Symbols with PDCCH |  | Symbols #0
 | Number of PRBs in CORESET |  | [TBD]
 | Number of PDCCH candidates and aggregation levels |  | [TBD]
 | DCI format |  | [TBD]
PDSCH configuration | Mapping type |  | Type A
 | k0 |  | 0
 | PDSCH aggregation factor |  | 1
 | PRB bundling type |  | Static
 | PRB bundling size |  | Wideband for FR1 [TBD] for FR2
 | Resource allocation type |  | Type 0
 | VRB-to-PRB mapping type |  | [TBD]
 | VRB-to-PRB mapping interleaver bundle size |  | [TBD]

## Slide 10: Simulation assumption for RAN4 #89 4/5
Parameter |  | Unit | Value
PDSCH DMRS configuration | DMRS Type |  | Type 1
 | Number of additional DMRS |  | 1
 | Length |  | 1
 | Antenna ports indexes |  | {1000} for 1 Layer CCs {1000, 1001} for 2 Layers CCs {1000 - 1003} for 4 Layers CCs
 | Number of PDSCH DMRS CDM group(s) without data |  | 1 for 1 layer and 2 layers CCs 2 for 4 Layers CCs
PTRS configuratioaan |  |  | For FR1: PTRS is not configured For FR2: 1 port, per 2PRB in frequency domain, per symbol in time domain
CSI-RS for tracking | First subcarrier index in the PRB used for CSI-RS (k0) |  | 3
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  | 6
 | Number of CSI-RS ports (X) |  | 1
 | CDM Type |  | No
 | Density (ρ) |  | 3
 | CSI-RS periodicity |  | 20ms
 | CSI-RS offset |  | 10ms from SSB
NZP CSI-RS for CSI acquisition | First subcarrier index in the PRB used for CSI-RS (k0) |  | 4
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  | 13
 | Number of CSI-RS ports (X) |  | Same as Tx ports
 | CDM Type |  | FD-CDM2
 | Density (ρ) |  | 1
 | CSI-RS periodicity |  | 20ms
 | CSI-RS offset |  | 0ms from SSB
Maximum number of code block groups for ACK/NACK feedback |  |  | 1
Maximum number of HARQ transmission |  |  | 4
Redundancy version coding sequence |  |  | {0,2,3,1}
Precoding configuration |  |  | SP Type I, Random per slot with PRB bundling granularity
Symbols for all unused REs |  |  | OCNG Annex A.5
Propagation condition |  |  | Static propagation condition for FR1 [TBD] for FR2

## Slide 11: Simulation assumption for RAN4 #89 5/5
Additional configuration for FDD
Additional configuration for TDD
Parameter |  | Unit | Value
Duplex mode |  |  | FDD
PDSCH configuration | Starting symbol (S) |  | 1
 | Length (L) |  | 13
Number of HARQ Processes |  |  | 4 for simulation purpose
K1 value |  |  | 2
Parameter |  | Unit | Value
Duplex mode |  |  | TDD
PDSCH configuration | Starting symbol (S) |  | 1
 | Length (L) |  | 13
Number of HARQ Processes |  |  | 8 for simulation purpose
K1 value |  |  | TBD
TDD UL-DL pattern |  |  | FR1 15kHz: DDDSU FR1 30KHz: 7D1S2U FR2 60 kHz: DDSU FR2 120 kHz: DDDSU for simulation purpose