## Slide 1: WF for BWP test cases
MediaTek, Nokia, CATT
3GPP TSG-RAN WG4 Meeting #88-Bis
Chengdu, China, 8th – 12th Oct, 2018
Agenda Item: 7.12.5.20
Document for: Approval
R4-1813991

## Slide 2: Background
UE Capability
6-1 | Basic BWP operation with restriction | 1) 1 UE-specific RRC configured DL BWP per carrier 2) 1 UE-specific RRC configured UL BWP per carrier 3) RRC reconfiguration of any parameters related to BWP 4) BW of a UE-specific RRC configured BWP includes BW of the initial DL BWP and SSB for Pcell[/PScell] and BW of the UE-specific RRC configured BWP includes SSB for Scell if there is SSB on Scell
6-2 | Type A BWP adaptation with same numerology | 1) Up to 2 UE-specific RRC configured DL BWPs per carrier 2) Up to 2 UE-specific RRC configured UL BWPs per carrier 3) Active BWP switching by DCI and timer 4) Same numerology for all the UE-specific RRC configured BWPs per carrier 5) BW of a UE-specific RRC configured BWP includes BW of the initial DL BWP and SSB for Pcell[/PScell] and BW of the UE-specific RRC configured BWP includes SSB for Scell if there is SSB on Scell
6-3 | Type B BWP adaptation with same numerology | 1) Up to 4 UE-specific RRC configured DL BWPs per carrier 2) Up to 4 UE-specific RRC configured UL BWPs per carrier 3) Active BWP switching by DCI and timer 4) Same numerology for all the UE-specific RRC configured BWPs per carrier 5) BW of a UE-specific RRC configured BWP includes BW of the initial DL BWP and SSB for Pcell[/PScell] and BW of the UE-specific RRC configured BWP includes SSB for Scell if there is SSB on Scell
6-4 | BWP adaptation with different numerologies | 1) Up to 4 UE-specific RRC configured DL BWPs per carrier 2) Up to 4 UE-specific RRC configured UL BWPs per carrier 3) Active BWP switching by DCI and timer 4) More than one numerologies for the UE-specific RRC configured BWPs per carrier 5) Same numerology between DL and UL per cell except for SUL at a given time 6) BW of a UE-specific RRC configured BWP includes BW of the initial DL BWP and SSB for Pcell[/PScell] and BW of the UE-specific RRC configured BWP includes SSB for Scell if there is SSB on Scell

## Slide 3: Online Agreements
Separate test cases for RRC-based BWP switch and DCI/Timer-based BWP switch
  Test cases for RRC based BWP switch target UE capability 6-1.
    1 single UE-specific BWP configuration
    SSB locates within the bandwidth of BWP
    Same SCS for all BWPs
  Test cases for DCI/Timer-based BWP switch target UE capability 6-2
    Up to 2 UE-specific BWP configurations
    SSB locates within the bandwidth of BWP
    Same SCS for all BWPs
  How to capture delay and interruption test case for RRC-based BWP switch will be addressed in RAN4#89.
BW of a UE-specific RRC configured BWP includes BW of the initial DL BWP
Merge BWP switch delay and interruption test case (under CA)
  Not to introduce Single CC with only BWP switch delay verification
  Specify the separate test metric for different purposes.
  Capture the test cases in 38.133.

## Slide 4: Way forward
Suggested test case list in TS38.133
FFS Test Case
 | # | LTE | PSCell or PCell 1 | SCell | Applicability (Skip other TC) | Company
EN-DC | 1 | FR1 | FR1 | N.A |  | MTK
 | 2 | FR1 | FR1 | FR1 | 1, 5 | Nokia, MTK
 | 3 | FR1 | FR2 | N.A |  | MTK
 | 4 | FR1 | FR2 | FR2 | 3, 6 | Nokia
SA | 5 | N.A | FR1 | FR1 |  | CATT
 | 6 | N.A | FR2 | FR2 |  | CATT
Note 1: PSCell/Pcell is the serving cell for BWP switch |  |  |  |  |  | 
 | # | LTE | PSCell or PCell 1 | SCell | Applicability (Skip other TC) | Company
EN-DC | 7 | FR1 | FR1 | FR2 | 1, 2, 5, 8 | MTK
SA | 8 | N.A | FR1 | FR2 |  | CATT
Note 1: PSCell/Pcell is the serving cell for BWP switch |  |  |  |  |  | 

## Slide 5: Way forward
Suggested test case list in TS38.133
  Capture the test case based on whether has the FR2 serving cell or not
  FFS Test Case
  Different interruption requirements for UE that supports per-FR gao and UE that does not support per-FR gap will be specified in each test case.
# | Section | Test Case
1 | A.4.5.2.1 | E-UTRAN – NR PSCell FR1 DL active BWP switch of PSCell in non-DRX in synchronous EN-DC
2 | A.4.5.2.2 | E-UTRAN – NR PSCell FR1 DL active BWP switch of PSCell with FR1 SCell in non-DRX in synchronous EN-DC
3 | A.5.5.2.1 | E-UTRAN – NR PSCell FR2 DL active BWP switch with non-DRX in synchronous EN-DC
4 | A.5.5.2.2 | E-UTRAN – NR PSCell FR2 DL active BWP switch with FR2 SCell in non-DRX in synchronous EN-DC
5 | A.6.5.2.1 | NR FR1- NR FR1 DL active BWP switch of PCell with non-DRX in SA
6 | A.7.5.2.1 | NR FR2- NR FR2 DL active BWP switch of PCell with non-DRX in SA
# | Section | Test Case
7 | A.5.5.2.3 | E-UTRAN – NR PSCell FR1 DL active BWP switch with FR2 SCell in non-DRX in synchronous EN-DC
8 | A.7.5.2.2 | NR FR1- NR FR2 DL active BWP switch of PCell with non-DRX in SA