## Slide 1
3GPP TSG-RAN WG4 Meeting #88BIS R4-1814065
Chengdu, China , 08 –12 October, 2018
Agenda Item: 7.12.1
WF on inter-frequency measurement accuracy requirements for FR1
CMCC, Samsung, …

## Slide 2: Background
According to the simulation results of SS-SINR measurement accuracy, the measurement performance of inter-frequency SS-SINR measurement is about +-2dB at side condition of -6dB.
SINR (dB) | SCS | Propagation condition | 5%CDF | 50%CDF | 95%CDF | Absolute SS-SINR accuracy | Relative SS-SINR accuracy
-6 | SCS = 15KHz | AWGN | -0.6 | -0.11 | 0.32 | 0.60 | 0.49
 |  | EPA5 | -1.33 | 0.07 | 1.57 | 1.57 | 1.50
 |  | ETU70 | -1.34 | -0.23 | 0.6 | 1.34 | 1.11
 | SCS = 30KHz | AWGN | -0.45 | -0.12 | 0.19 | 0.45 | 0.33
 |  | EPA5 | -1.43 | -0.12 | 0.96 | 1.43 | 1.31
 |  | ETU70 | -1.29 | -0.33 | 0.48 | 1.29 | 0.96
Table 1 simulation results of SS-SINR measurement (R4-1810292)
However, in current TS 38.133, the SS-SINR inter-frequency absolute measurement accuracy is +-[3.5]dB at side condition of >=-[4]Db.

## Slide 3: Background
According to the simulation results of SS-RSRQ measurement accuracy, the measurement performance of inter-frequency SS-RSRQ measurement is about +-2dB at side condition of -6dB.
Table 2 simulation results of SS-RSRQ measurement (R4-1808827)
SINR (dB) | SCS | Propagation condition | 5%CDF | 50%CDF | 95%CDF | Absolute SS-RSRQ accuracy | Relative SS-RSRQ accuracy
-6 | SCS = 15KHz | AWGN | -0.59 | -0.12 | 0.28 | 0.59 | 0.47
 |  | EPA5 | -1.38 | 0.05 | 1.56 | 1.56 | 1.51
 |  | ETU70 | -1.28 | -0.22 | 0.55 | 1.28 | 1.06
 | SCS = 30KHz | AWGN | -0.43 | -0.12 | 0.16 | 0.43 | 0.31
 |  | EPA5 | -1.46 | -0.13 | 0.97 | 1.46 | 1.33
 |  | ETU70 | -1.43 | -0.16 | 0.87 | 1.43 | 1.27
However, in TS 38.133, the SS-RSRQ inter-frequency absolute measurement accuracy is +-[3.5]dB at side condition of >=-[4]dB. The SS-RSRQ inter-frequency relative measurement accuracy is +-[4]dB at side condition of >=-[4]dB.

## Slide 4: Agreements
Option 1: If the side condition is -6dB, the LTE inter-frequency measurement accuracy is reused for NR FR1 inter-frequency measurement.
Option 2: If the side condition is -4dB, the NR FR1 inter-frequency measurement accuracy need to be updated according to the simulation results.
  The simulation assumption is R4-1706551
  Other options are not precluded
  Companies are encouraged to provide discussion on this issue.