## Slide 1: WF for Test Configurations for MSR with NR
Ericsson, Nokia, Nokia Shanghai Bell, […]
R4-1814112
Document for: Approval
3GPP TSG-RAN WG4 RAN#88bis
Chengdu, China, 8 – 12 October, 2018

## Slide 2: Background
The following WFs were approved:
  R4-1811619, Way Forward on Test Configurations for MSR, RAN4#88
Following contributions made proposals on test signal selection and Test Configurations to be specified:
[1] R4-1812580 Further discussion on test configuration for MSR , ZTE
[2] R4-1812761 Open issues when introducing NR in TS 37.141, Ericsson
[3] R4-1812762 CR to TS 37.141: NR introduction - Test Cases and Applicability, Ericsson
[4] R4-1813402 Test configurations for MSR with NR, Nokia, Nokia Shanghai Bell

## Slide 3: Way forward – Test signal
The test signal used to build TCs to test CS16 and CS17 shall selected according following table:
 | Lower edge | Upper edge
CS16 | Typical NR signal | E-UTRA 10MHz with NB-IoT in guard band E-UTRA 5MHz with NB-IoT in-band (Note 1) E-UTRA 5 MHz (Note 2)
CS17 | E-UTRA 10 MHz with NB-IoT in guard band E-UTRA 5MHz with NB-IoT in-band (Note 1) Typical NR signal (Note 2) | NB-IoT standalone
Note 1: if NB-IoT in guard band is not supported Note 2: if NB-IoT in-band and NB-IoT in guard band is not supported Note 3: Typical NR signal is 5MHz CBW and 15kHz SCS. In case 5/10MHz CBW is not supported, the smallest supported CBW is selected. |  | 

## Slide 4: Test Configurations
TCs shall be specified for following operations:
  Contiguous spectrum:
    Considering for CS16:
      NR + E-UTRA
      NR + E-UTRA with NB-IoT in-band
      NR + E-UTRA with NB-IoT in guard band
    Considering for CS17:
      NR + NB-IoT standalone + E-UTRA
      NR + NB-IoT standalone + E-UTRA with NB-IoT in-band
      NR + NB-IoT standalone + E-UTRA with NB-IoT in guard band
  Non-contiguous spectrum:
    Considering for CS16
      NR + E-UTRA
      NR + E-UTRA with NB-IoT in-band
      NR + E-UTRA with NB-IoT in guard band
  Multi-band:
    Considering for CS16
      NR + E-UTRA
      NR + E-UTRA with NB-IoT in-band in one band only
      NR + E-UTRA with NB-IoT in guard band in one band only

## Slide 5: Test Configurations
To specify TCs for following operations, TS 36.104/36.141 shall be updated and related TCs are not considered for the time being:
  Non-contiguous spectrum:
    Considering for CS17
      NR + NB-IoT Standalone + E-UTRA
      NR + NB-IoT Standalone + E-UTRA with NB-IoT in-band
      NR + NB-IoT Standalone + E-UTRA with NB-IoT in guard band
  Multi-band:
    Considering for CS17
      NR + NB-IoT Standalone + E-UTRA
      NR + NB-IoT Standalone + E-UTRA with NB-IoT in-band
      NR + NB-IoT Standalone + E-UTRA with NB-IoT in guard band

## Slide 6: Test Configurations specification
Specify TCs for each CS and each operation type:
  Option 1: One unique TC covering E-UTRA, E-UTRA with NB-IoT in-band, E-UTRA with NB-IoT in guard band (+in-band).
    Not consistent with existing TCs specifications
    Minimize number of new TCs
  Option 2: one TC for E-UTRA, one TC E-UTRA with NB-IoT in-band, one TC for E-UTRA with NB-IoT in guard band (+in-band).
    Keep TC consistency
    Increase number of new TCs (3 times more).
Agreement: Option 1
CR to TS 37.141: RAN4#89
  R4-1813402 would be used as baseline to specify the new Test Configurations.

## Slide 7: Test configuration for MSR AAS
CRs to TS 37.145: RAN4#89.
  Following documents would be used as baseline to specify new Test Configurations with NR for AAS MSR + Test configurations applicability.
    R4-1814124 for CR to TS 37.145-1
    R4-1814125 for CR to TS 37.145-2