## Slide 1: WF on FR2 Temperature Conditions for UE RF Requirements Verification
MediaTek Inc.
3GPP TSG-RAN WG4 #88bis Meeting R4-1814171
ChengDu, Sichuan, China, October 8th – 12th, 2018

## Slide 2: Background
FR2 temperature conditions for UE RF requirements has been discussed in this meeting [1-2], where some concerns were brought up for RF requirements verification under extreme temperature condition.
In current RAN4 and RAN5 specifications, some UE RF requirements have already been specified to be verified only under normal temperature condition which are summarized in the next slide.

## Slide 3: FR2 RF Requirements Tested under Normal Temp.
Rx sensitivity – approved in last RAN5 meeting [3]
 | Spec. | Version | Sub-clause
Power control | 38.101-2 | 15.2.0 | 6.3.4.1
EVM | 38.101-2 | 15.2.0 | 6.4.2.1
EVM equalizer spectrum flatness | 38.101-2 | 15.2.0 | 6.4.2.4
ACLR | 38.521-2 | 1.0.0 | 6.5.2.3.4.1
SEM | 38.521-2 | 1.0.0 | 6.5.2.1.4.1
Occupied bandwidth | 38.521-2 | 1.0.0 | 6.5.1.4.1
ACS | 38.521-2 | 1.0.0 | 7.5.4.1
IBB | 38.521-2 | 1.0.0 | 7.6.2.4.1

## Slide 4: Way Forward
Companies are encouraged to propose a list of RF requirements which need be tested in extreme temperature condition with technical justifications in next meeting (excluding the requirements already defined under normal temperature condition as listed in previous slide).
Upon the discussion outcome in next meeting, RAN4 decides if all UE RF requirements are allowed to be verified only under normal temperature condition and inform RAN5 on RAN4’s decision.

## Slide 5: References
[1] R4-1812323, “FR2 environmental conditions”, MediaTek Inc.
[2] R4-1812721, “Discussion on the extreme conditions in FR2”, OPPO
[3] R5-184366, “Discussion of NR FR2 Test Point for RX RefSens test cases”, Qualcomm Inc., 3GPP TSG-RAN WG5 Meeting #80, Gothenburg, Sweden, August 20th – 24th, 2018