## Slide 1: Way forward on NR UE PDSCH demodulation requirements and General aspects
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8 – 12 October 2018 Agenda Item: 7.13.1.2
R4-1814238

## Slide 2: SA/NSA requirements
For SA/NSA Normal demodulation performance requirements only verified NR carrier requirements, additional EN-DC specific requirements can be further discussed after normal requirements finalized.
NSA SDR requirements
  For EN-DC operation within FR1, both LTE carrier and NR carrier need to be verified
  For interworking operation across FR1 + FR2 (e.g. EN-DC operation with FR2, FR1+FR2 CA), only FR2 carrier requirements can be testable considering test feasibility under Rel-15.
  Applicability for UEs supporting SA/NSA operation
  FFS for test applicability of for the same test cases for UE which supporting both SA/NSA operation
  LTE carrier configurations for normal NSA test cases without LTE requirements
  1 LTE cell
  TDD DL-UL configuration 2 (i.e. alignment between LTE and NR)

## Slide 3: CA/DC requirements
Deprioritize NR CA (normal test cases), NR-NR DC requirements before Dec 2018

## Slide 4: Type A performance requirements
Requirement with 70% test point and 8 HARQ process for FDD and 16 HARQ process for TDD: (FFS whether needed or not)
  Option 1: No tests
  Option 2 (simulation purpose)
    MCS #19 and rank 2 for FR1, FDD and TDD (7D1S2U) for both 2Rx and 4Rx
    MCS #13 and rank 2 (2Rx) for TDD (DDDSU) FR2
  Other options not excluded
  Interested companies are encourage to bring more analysis with simulation results to further decide the necessity of introducing such test cases in next RAN4 meeting.
MCS for QPSK test with 4 Rx: MCS 4
PRB bundling:
  Test cases with 4 and WB bundling
    4 for test FR1, QPSK, Rank 1
    WB for test FR1, 16QAM, Rank 3 and FR2, QPSK, Rank 1
  Other test cases: 2 PRB bundling

## Slide 5: Type B performance requirements
Start symbol (S) 5
Duration (L) 7
1 additional DMRS
MCS: MCS4 for 2Rx and 4 Rx

## Slide 6: LTE-NR co-existence test case
PDSCH Type A
Start symbol (S): 3
Duration (L): [9 or 11]
  Note: Use 11 if RAN1 agreement on changes of additional DMRS position for Type A is confirmed
Number of additional DMRS: 1
Duplex mode: FDD only
FRC: MCS4 Rank 1 for 2Rx and 4 Rx
Overhead for TBS determination: 18

## Slide 7: ZP and NZP CSI-RS configurations
NZP CSI-RS configuration for CSI acquisition
ZP CSI-RS configuration
Applicability
  FR1
    Configuration 1: All tests except tests for Configuration 2
    Configuration 2: MCS #13 and rank 2
  FR2: Use Configuration 1 for all test
RRC configuration | Configuration 1 | Configuration 2
periodicityAndOffset | 20 ms, 0 | 5/0
nrofPorts | 2 or 4 | 2
frequencyDomainAllocation | Other, ‘000001’ | Other, ‘000001’
firstOFDMSymbolInTimeDomain | 12 | 13
cdm-Type | 2 | 2
density | 1 | 1
RRC configuration | Configuration 1 | Configuration 2
periodicityAndOffset | 20 ms, 0 | 5/0
nrofPorts | 4 | 8
frequencyDomainAllocation | Other, ‘000100’ | Other, ‘011110’
firstOFDMSymbolInTimeDomain | 12 | 12
cdm-Type | 2 | 2
density | 1 | 1

## Slide 8: UE RX beam refinement for FR2
FFS whether to configure CSI-RS for UE RX beam refinement
NZP CSI-RS configuration for BM:
  2 ports
  4 resources
  Periodicity 20 ms
  Offset 0
  Repetition ON
  Subcarrier index: 0
  OFDM symbol:
    Resource 1: 8, Resource 2: 9, Resource 3: 10, Resource 4: 11
  Density 1
  CDM2

## Slide 9: TCI state configurations
Only one TCI state configured for NR UE performance test cases in Rel-15( [QCL behavior Type A and TypeD (FR2 only)])
Detailed parameters FFS

## Slide 10: Additional CBW/SCS
  List of CBW/SCS
  FR1 FDD: 30 kHz SCS + 20 MHz CBW
  FR1 TDD:
    30 kHz SCS + 20 MHz CBW
  FR2
    120 kHz SCS + 50 MHz CBW
    120 kHz SCS + 200 MHz CBW
    60 kHz SCS + 50 MHz CBW
    FRC for additional CBW/SCS
  MCS 13 with rank2 for FR2 and MCS 19 rank2 for FR1

## Slide 11: PDSCH requirements for FR2
Define band agnostic requirements for current agreed test cases at least for up to frequency range 40 GHz.
List of FRC:
  QPSK:
    MCS4 Rank 1
    MCS4 Rank 2
  16QAM:
    MCS13 Rank 1
    MCS13 Rank 2
  64QAM:
    MCS18 Rank 1
    MCS17 Rank 2
1 additional DMRS for channel model with 300 Hz Doppler

## Slide 12: Dynamic UL/DL determination
Dynamic UL/DL determination is a mandatory feature for Rel-15.
Forward Compatibility: If no test is defined to test this feature now, network operators will have a risk of breaking some existing NR UEs if they try to configure dynamic TDD configuration now or in any future NR release.
To avoid any extra workload, it can be tested for some existing TDD test case(s) as below:
  Configure all slots as flexible in RRC configuration or do not configure TDD UL-DL configuration through RRC.
  Send DL or UL DCI to indicate D, S and U slot to configure the same TDD UL-DL config as agreed for those test case(s).
The above methodology does not impact simulation results or RMCs but it verifies that UE supports DCI based slot configuration.
Way forward
  Option 1: Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s). [QC, Ericsson, NTT Docomo, AT&T, China Mobile, Intel]
  Option 2: Do not define test ( it’s a functionality test, not in UE demodulation performance scope) (Huawei, MTK)