## Slide 1: Way forward on the remaining open issues for RRM test methods
Intel Corporation, Anritsu…
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 8 – 12 October 2018 Agenda Item: 10.1.1
R4-1814311

## Slide 2: Ad-hoc Agreements (1)
UE beam lock assumptions for RRM Test Methods
  From testability perspective UE beam lock may or may not be applied.
  UE beam lock assumptions can be defined for each RRM test case for 1 AoA
  UE beam lock is not applied for 2 AoA case

## Slide 3: Ad-hoc Agreements (2)
Scenario #1: 1 AoA with signal coming from the RX beam peak direction
  Detailed procedure and SNR for 1 AoA from global UE Rx beam peak direction will be defined in TR 38.810
  Global UE RX beam peak is the RX beam peak defined for the UE RF in TS 38.101-2
    UE RX beam peak direction can be different from the beam peak directions of beams which UE is using for RRM measurements. FFS how to account for this difference.
  Scenario #1 can be used for 2 types of RRM test cases
    Type 1 test cases: RRM test cases which assume that UE is using “fine” UE RX beams (i.e. beams used in UE RF requirements)
      For Type 1, UE demodulation methodology is used to define the Noc levels and SNR range, using parameters for Far-Field setup
    Type 2 test cases: RRM test case which assume that UE is using “rough” UE RX beams (i.e. beams which UE is using for RRM measurements)

## Slide 4: Ad-hoc Agreements (3)
Scenario #1: 1 AoA with signal coming from the RX beam peak direction
Types of side conditions emulation:
  TE emulates artificial noise and target SNR conditions in the reference point
    Noise power level Noc1 is defined close UE noise floor such that SNRRP = SNRBB + [X] dB
      X value
        Option 1: X = 1 dB
        Option 2: other values are not precluded. Companies can bring proposals.
      Noc definition
        Type 1 test cases: UE demodulation methodology is used to define the Noc levels and SNR range
        Type 2 test cases:
          Noc level shall be defined taking into account difference in antenna gains for UE RX beam peak and for [spherical coverage] for the UE RF and RRM requirements.
          Antenna gain difference is FFS. Companies to bring analysis on the values in RAN4 #89 to finalize the Noc definition.
    Whether Noc level Noc2 > Noc1 shall be supported can be discussed in the RRM test cases and not precluded from testability perspective. (Note: feasible SNR range can be smaller than for the case of Noc1)
Next steps:
Further define UE RX beam assumptions for “rough” beams (used for RRM measurements) to identify antenna gain and spherical coverage characteristics (to be provided by UE vendors)
  Note: analysis is applicable to all scenarios
Further discuss the Noc / SNR methodology for the remaining scenarios
  Scenario #2: 1 AoA with signal coming from the non RX beam peak direction
  Scenario #3: 2 AoA

## Slide 5: Background: Tdocs at RAN4#88bis in Noc level and SNR range
Anritsu R4-1812087
  Rx beam peak direction: 18dB max SNR, 100MHz max Ch BW, DFF
  Non-beam-peak direction: 7dB max SNR, 100MHz max Ch BW, DFF
  Based on 11dB spherical coverage ∆
  Noc: -153dBm/Hz beam peak direction, -142dBm/Hz non-beam-peak direction
Qualcomm R4-1813264
  Non-beam-peak direction: 2.4dB max SNR, 100MHz max Ch BW, DFF
  Based on 12.6dB spherical coverage ∆
  Noc: -140.5dBm/Hz non-beam-peak direction
Intel R4-1812208
  Similar principle: “The Noc level for signals coming from the non-beam peak direction.. shall be adjusted to take into account the difference in antenna gains in the beam peak and non beam peak directions”

## Slide 6: Way Forward
UE RX beam types definitions
  “Fine” UE RX beams - beams used to define UE RF requirements (e.g. EIS, EIS spherical coverage)
  “Rough” UE RX beams - beams which UE is using for RRM measurements (e.g. for SSB measurements)
  Note: The beam peak directions, antenna gains and spherical coverage for “fine” and “rough” beams can be different. The number of beams in the respective codebooks can be different.
Beam peak definition
  UE RX beam peak is the RX beam peak defined for the UE RF in TS 38.101-2 (i.e. beam peak corresponding to the “fine” beams)
SNR definition
  SNRRP – OTA reference point SNR
  SNRBB – baseband SNR
The following types of RRM test cases can be supported by the NR Test Methods
  Type 1 RRM test cases: RRM test cases are designed under assumption that UE is using “fine” UE RX beams
  Type 2 RRM test cases: RRM test case are designed under assumption that UE is using “rough” UE RX beams
  Note: It is up to RRM room to identify which test cases are Type 1 or 2

## Slide 7: Way Forward
Scenarios for RRM test cases which can be supported by the NR Test Methods
  Scenario #1: 1 AoA with signal coming from the UE RX beam peak direction
  Scenario #2: 1 AoA with signal coming from the non UE RX beam peak direction
  Scenario #3: 2 AoA
    Signal directions
      Option 1: One signal comes from the UE RX beam peak direction. The other signal comes from the non RX beam peak direction
      Option 2: Both signals come from the non-beam peak directions
      Assumption is that the respective signal and noise levels per AoA at the reference point will be defined in the test description
  Note 1: Type 1 and Type 2 RRM test cases can be used for either scenario
  Note 2: it is up to RRM room to decide whether any of the scenarios can be used for RRM test case definition.

## Slide 8: Way Forward
The following modes of Side condition emulation can be supported by the NR Test Methods
  Mode 1: TE emulates target SNR conditions
    Scenario 1/2: TE transmits desired signal and artificial noise jointly. The noise power is set to reach target SNR conditions in the reference point
    Scenario #3: TE can transmit both desired and noise signals from both directions.
      Option 1: Same noise level can be applied for both tested directions.
      Option 2: Different noise levels can be applied for different directions.
      Assumption is that the respective signal and noise levels per AoA at the reference point will be defined in the test description
  Mode 2: TE emulates desired signal only without artificial noise
  Note: It is up to RRM room to select applicable mode for each test case

## Slide 9: Way Forward
For Scenarios 1&2 and Mode 1 (TE transmits desired signal and artificial noise)
  Noc level is selected such that SNRRP = SNRBB + [X] dB
    Follow the methodology used for UE demodulation to derive the SNR level but with different antenna gain assumptions specific to different scenarios
    X value
      Option 1: X = 1 dB
      Option 2: other values are not precluded. Companies can bring proposals.
    Whether higher Noc level shall be supported can be discussed in the RRM test cases and not precluded from testability perspective. (Note: feasible SNR range can be smaller than for the case of Noc1)
  Noc level definition and SNR range
    Option 1: Use same methodology as the one used for UE demodulation (agreed in R4-1811892)
      The UE antenna gain assumptions shall be changed to account for difference in the antenna gains at UE side for RRM requirements (difference between the antenna gains of fine and rough beams)
        Option 1: Use UE RX antenna gain difference between peak EIS and 50%-ile EIS spherical coverage for PC3
        Option 2: other options not precluded
    Option 2: Use UE RX spherical coverage requirements
      The UE RX spherical coverage requirements are in the process of being agreed for fine beams and can be used directly.
      For rough beams, the same method is used but with values changed to account for difference in the antenna gains at UE side for RRM requirements (difference between the antenna gains of fine and rough beams)

## Slide 10: Way Forward
Option 2 for Noc level definition and SNR range using coverage requirements
  Similar principle to methodology used for UE demodulation
    Based on coverage requirements instead of on UE internal parameters such as noise figure, implementation loss..
    Can be adapted for other UE Power classes
  Example in diagram is for fine beams, non-beam peak

## Slide 11: Way Forward
Further identify assumptions on UE RX beam antenna gain difference relative to the UE RX beam peak antenna gain for Noc definition under assumption of using “rough” beams
  Companies are encouraged to bring comparison of the UE spherical coverage for “rough” and “fine” beams
  Analysis can be done under assumption that UE supports [N] beams codebook for “rough” UE RX beams
    Option 1: N = 4
    Option 2: N = 8
    Other options are not precluded
    Whichever option company chooses it is required to ensure that UE is compliant with RRM requirements
  Notes:
    Based on TR 38.133 section 9.2.5.1
      Mpss/sss_sync_w/o_gaps : For a UE supporting power class 1(fixed wireless access), Mpss/sss_sync=40. For a UE supporting power class 2(vehicle mounted), Mpss/sss_sync_w/o_gaps =[24]. For a UE supporting power class 3(handheld), Mpss/sss_sync_w/o_gaps =[24]. For a UE supporting power class 4, Mpss/sss_sync_w/o_gaps =TBD
      Mmeas_period_w/o_gaps : For a UE supporting power class 1 (fixed wireless access), Mmeas_period_w/o_gaps =40. For a UE supporting power class 2 (vehicle mounted), Mmeas_period_w/o_gaps =[24]. For a UE supporting power class 3 (handheld), Mmeas_period_w/o_gaps =[24]. For a UE supporting power class 4, Mmeas_period_w/o_gaps =TBD.

## Slide 12: Other open issues
Noc level for scenario 3 and Mode 1 (TE transmits desired signal and artificial noise)
How to select the tested direction for Scenario 2 and 3 is FFS