## Slide 1: WF on NR V2X RF operating parameters based on RAN1 incoming LS
LG Electronics, Ericsson, Intel, Huawei, CATT, Qualcomm
3GPP TSG RAN WG4 Meeting #88BIS
Chengdu, China, 08th – 12th October, 2018 Agenda Item: 11
R4-1814322

## Slide 2: Background
In LS from RAN1 [1], RAN4 need study for NR V2X UE RF operating parameters such as AGC set time, Time/Freq. error and IBE requirements for sidelink operation both FR1 and FR2.
In NR V2X SID, there was not request to RAN4 works for NR V2X Study.
NR V2X rapporteur and RAN4 chairman recommend E-mail discussion and offline discussion with interested companies.
  If there is some make consensus, RAN4 treat the papers as e-mail approval at this meeting.
  The deadline is 19th Oct. by RAN4 chairman proposal in e-mail reflector
Provided Tdocs at this meeting
  R4-1813237, "Reply LS to RAN1 NR V2X for discussion," Ericsson
  R4-1813238, "Reply LS to RAN1 NR V2X," Ericsson
  R4-1813452, "On NR V2X RF and RRM characteristics," Intel Corporation

## Slide 3: Summary
Based on offline discussion, RAN4 merged the companies’ view as below
Company | AGC set time | Tx/Rx switching time | Time error | Frequency error | In-band Emission | Others
LG | FR1: 20us (w/o PSD changed), FFS for PSD changed FR2: FFS | FR1: up to 13us, FR2: up to 7us | FR1: 0.4 us regaldress of sync. Source, FR2: FFS | FR1: 0.1 ppm regardless of sync. Sources. FR2: FFS | FR1: reuse LTE V2X IBE. FR2: FFS | Focus on FR1 operating RF parameters
HW | FR1&2: FFS | FR1: 13 us, FR2 : 7us | dependent on sync. Source | FR1 & FR2: 0.1 ppm regardless of sync. Sources | Whether it can be improved need FFS | 
Ericsson | FR1: 20 us w/o PSD change, one OFDM symbol with PSD change for 15kHz SCS, FFS for other SCS. FR2: FFS | FR1: 13 us, FR2: 7 us (Refer to 38.211, table 4.3.2-3) | Up to ±390ns all sync source except syncREF (v2x NR) UE, FFS for syncREF (v2x NR) UE | FR1&FR2: within ±0.1 ppm observed over a period of 1 msec | FR1: reuse/adapt IBE req in 6.4.2.3 in 38.101-1 FR2: reuse/adapt IBE req in 6.4.2.3 in 38.101-2 | Prioritize FR1 over FR2
Intel | FFS | FR1: 13 us, FR2 : 7us | gNB synchronization reference source: Option 1: reuse TS 38.133 section 7.1.2 Option 2: 12*64*Tc for FR1 and 3.5*64*Tc for FR2. GNSS synchronization reference source : 12*64*Tc for FR1 and FFS for FR2 | FR1&FR2: ±0.1 ppm for gNB synchronization reference source FFS for GNSS at FR2 | FR1: Use tightened NR UL IBE model, FR2: FFS | 
CATT | FFS | FR1: up to 13us | FFS | FR1: 0.1 ppm regardless of sync. Sources. | FR1: reuse LTE V2X IBE. | Focus on FR1 operating RF parameters
QC | FFS |  | FFS | FFS | Whether it can be improved need FFS | 
RAN4 baseline assumption | TBD on next meeting | Align with RAN1 | TBD on next meeting | TBD on next meeting | TBD on next meeting | Based on progress, RAN4 send LS on the RF parameters

## Slide 4: WF
TBD part in slide 3 will be evaluated until RAN4 November meeting. Then RAN4 will send LS to RAN1 at RAN4 #89 meeting.
  Information:
    For NR V2X UE synch. case, RAN4 need to wait the RAN1 physical layer design
    SCSs candidates in RAN1 agreement for FR1 and FR2 will be considered:
      FR1: 15 kHz, 30 kHz, 60 kHz
      FR2: 60 kHz, 120 kHz

## Slide 5: WF on FR1 V2X IBE model
Further discuss the IBE model for NR FR1 V2X communication
Option 1: Modified NR UL IBE model
  Companies are encouraged to bring proposals on feasible tightening of the IBE model components comparing to NR UL IBE model defined in TS 38.101-1 (i.e. possible values X1, X2, X3, Y1, Y2, Z1, Z2, Z3 and Z4)
Other options are not precluded
Note: The IBE model in this stage is only for RAN1 evaluation. This initial discussion is not for RAN4 requirements which will be decided in WI stage

## Slide 6: References
[1] R4-1812009, "LS on IBE model for V2X," RAN1, Ericsson
  [2] R4-1813237, "Reply LS to RAN1 NR V2X for discussion," Ericsson
  [3] R4-1813238, "Reply LS to RAN1 NR V2X," Ericsson
  [4] R4-1813452, "On NR V2X RF and RRM characteristics," Intel