## Slide 1: WF on clarification of single UL and dual UL support for DC_3_n3 CHTTL
3GPP TSG-RAN WG4 Meeting #88bis R4-1813120 Chengdu, China, 8th – 12th October, 2018

## Slide 2: Backgrounds
Based on the agreed WF[1] in RAN4#88
  Dual uplink transmission mode is supported in Rel.16
  Two BCS sets will be introduced in Rel.16
    Note that currently only BCS 0 is introduced in Rel.15 with single switch UL only
  Both 2PA/antennas and 1PA/antenna architectures are considered but 2PA architecture is prioritized when defining dual uplink related requirements
Issues to be discussed
  Mandatory/optional support for single UL/dual UL support is still under discussion
  It is beneficial for network to differentiate UE with different capabilities including single uplink/dual uplink support and 1PA/2PA architectures
 |  | E-UTRA – NR configuration / Bandwidth combination set |  |  |  | 
Downlink EN-DC configuration | Uplink EN-DC configurations | Component carriers in order of increasing carrier frequency |  |  | Maximum aggregated bandwidth (MHz) | BCS
 |  | Channel bandwidths for LTE carrier (MHz) | Channel bandwidths NR for carrier (MHz) | Channel bandwidths for LTE carrier (MHz) |  | 
DC_3A_n3A | DC_3A_n3A |  | 5, 10, 15, 20, 25, 30 | 5, 10, 15, 20 | 50 | 0
 |  |  | 5, 10, 15, 20, 25, 30 | 5, 10, 15, 20 | 50 | 1
 |  | 5, 10, 15, 20 | 5, 10, 15, 20, 25, 30 |  |  | 

## Slide 3: Proposals
Wayforward for single uplink and dual uplink support for DC_3_n3
  Option 1 – differentiate single uplink support and dual uplink support by Release
    For Rel.15 UE supporting DC_3_n3, the UE supports single UL switched only
    For Rel.16 onwards UE supporting DC_3_n3, the UE should be able to support dual uplink and meet the related requirements based on the assumption of 2PA architectures
      Note that single UL is also allowed with SUO signalling when the combination meets criteria for SUO allowed (IMD3)
  Option 2 – differentiate single uplink support and dual uplink support by BCS set
    For UE supporting BCS0 only for DC_3_n3, the UE should at least support single UL switched
    For UE supporting BCS1 for DC_3_n3, the UE should be able to support dual uplink and meet the related requirements based on the assumption of 2PA architectures
      Note that single UL is also allowed with SUO signalling when the combination meets criteria for SUO allowed (IMD3)
  Adopt one of the options above

## Slide 4: Reference
  [1] R4-1811500, “WF for DC_3A_n3A in Rel.16”, CHTTL, Skyworks, RAN4#88