## Slide 1: 3GPP TSG-RAN WG4 Meeting #88bis Chengdu, China, 08 - 12 Oct 2018
Ericsson
Way forward on simulation assumption for demodulation performance requirements for network-based CRS interference mitigation
R4-1813450

## Slide 2: WF
Define performance requirements for the UE supporting nw-BasedCRS-InterferenceMitigation-r15 with interference cell CRS based on an on/off pattern changing in time
Define both TM3 and TM9 tests

## Slide 3: Simulation assumptions for TM3 tests
Parameter |  | Unit | Test 1-4 | 
 |  |  | Cell 1 | Cell 2
Downlink power allocation |  | dB | -3 | -3
 |  | dB | -3 (NOTE 1) | -3 (NOTE 1)
 |  | dB | 0 | 0
at antenna port |  | dBm/15kHz | -98 | -98
PDSCH transmission mode |  |  | 3 | 3
CRS transmission |  |  | On | In the subframes which CRS can be muted, 50% subframe is with CRS and 50% is with CRS only on the center six PRBs
nw-BasedCRS-InterferenceMitigation-r15 |  |  | Disabled | Enabled
Correlation matrix and antenna config. |  |  | 2x2 Low | 2x2 Low
Bandwidth |  |  | 10MHz | 10MHz
Channel model |  |  | EVA70 | EVA70
FRC |  |  | R.35 (FDD/TDD) | OCNG
NOTE 1: . NOTE 2: Void. NOTE 3: Void. |  |  |  | 

## Slide 4: Simulation assumptions for TM9 tests
Parameters |  | Unit | Test 1, Test 1a | 
 |  |  | Cell 1 | Cell 2
Downlink power allocation |  | dB | 0 | 0
 |  | dB | 0 (Note 1) | 0 (Note 1)
 |  | dB | -3 | -3
Beamforming model |  |  | Annex B.4.1 | NA
Cell-specific reference signals |  |  | Antenna ports 0,1 | Antenna ports 0,1
CSI reference signals |  |  | Antenna ports 15,…,18 | Antenna ports 15,…,18
CSI-RS periodicity and subframe offset TCSI-RS / ∆CSI-RS |  | Subframes | 5 / 2 | 5 / 2
CSI reference signal configuration |  |  | 0 | 0
csi-RS-ConfigZP-ApList |  |  | N/A | N/A
Zero-power CSI-RS configuration ICSI-RS / ZeroPowerCSI-RS bitmap |  | Subframes / bitmap | 3 / 0001000000000000 | 3 / 0001000000000000
at antenna port |  | dBm/15kHz | -98 | -98
Symbols for unused PRBs |  |  | OCNG | OCNG
Number of allocated resource blocks |  | PRB | 50 | 50
Simultaneous transmission |  |  | No | No
PDSCH transmission mode |  |  | 9 | 9
CRS transmission |  |  | On | In the subframes which CRS can be muted, 50% subframe is with CRS and 50% is without CRS
nw-BasedCRS-InterferenceMitigation-r15 |  |  | Disabled | Enabled
Correlation matrix and antenna config. |  |  | 2x2 Low | 2x2 Low
Bandwidth |  |  | 10MHz | 10MHz
Channel model |  |  | EVA5 | EVA5
FRC |  |  | 64QAM ½ (R.50 FDD/TDD) | OCNG