## Slide 1: A-MPR for intra-band EN-DC
Ericsson, Skyworks, MediaTek, Sprint

## Slide 2: A-MPR for intra-band EN-DC
Ericsson

## Slide 3: Proposed method
The LTE timeline is kept, the LTE power completely determined by the LTE (MCG) alone
Power back-off is applied on the total transmitted signal relative to PEN-DC,total
The A-MPR on the MCG, A-MPRE-UTRA, is determined by the PRB allocation on the MCG alone and the UE determines the Pcmax,c,E-UTRA and the PHRE-UTRA accordingly
The A-MPR of the total transmission power PEN-DC,total, A-MPRtotal, is determined by the PRB allocations on both CGs and the UE determines the resulting PEN-DC,total used for determining if the SCG power should be reduced/dropped
The A-MPR on the SCG, A-MPRNR is set to A-MPRtotal (similar to UL CA for LTE) and the UE determines the Pcmax,c,NR and the PHRNR accordingly
On the SCG: given the PEN-DC,total, the actual UE powers PMCG (known) and PSCG and, the UE reduces the PSCG or drops the SCG

## Slide 4: Timing diagram (same numerology)
PDCCH
PDCCH
PUSCH
PUSCH
n-4
n-1
A-MPR calcuation (MSG and SCG UL SG)
SCG PHR determination
SCG scaling (if needed) based on computed PEN-DC,total
A-MPR calcuation (MSG UL SG)
MCG PHR determination
MCG
SCG
Applies for both intra-band and inter-band EN-DC

## Slide 5: Example, intra-band contiguous, DC_(n)71B
Ppowerclass,EN-DC = 23 dBm, DFTS-OFDM, 10 + 10 MHz
Suppose PL estimate the same on both and both PC loops work out required UL power 0 dBm/PRB
10 PRB on LTE and 20 PRB on NR => A-MPRtotal = 7 dB (MPR = 0 dB)
  A-MPRtotal = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 7 dB
  PEN-DC, total = Ppowerclass,EN-DC - A-MPRtotal = 16dBm, PMCG = 10 dBm, PSCG = 13 dBm
  No scaling since PMCG + PSCG = 14.7 dBm < PEN-DC, total
10 PRB on LTE and 50 PRB on NR => A-MPRtotal = 5 dB
  A-MPRtotal = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 5 dB
  PEN-DC, total = 18 dBm, PMCG = 10 dBm, PSCG = 17 dBm
  No scaling since PMCG + PSCG = 17,8 dBm < PEN-DC, total
10 PRB on LTE and 50 PRB on NR but with 3 dBm/PRB on NR => A-MPRtotal = 5 dB
  A-MPRtotal = 1 dB (by 36.101 for B71), A-MPRNR = A-MPRtotal = 5 dB
  PEN-DC, total = 18 dBm, PMCG = 10 dBm, PSCG = 18 dBm (23 - A-MPRNR reduced from 20 dBm = 3 dBm/PRB + 17)
  NR reduction since PMCG + PSCG = 18.5 dBm > PEN-DC, total , NR reduced to PSCG = PEN-DC, total - PMCG = 17.2 dBm
All computations above internally in the UE
A-MPR table

## Slide 6: How NR can compensate for missing or excessive back-off on LTE side for Intra-band EN-DC A-MPR
Skyworks Solutions, Inc.

## Slide 7: Disclaimer
This proposal is only describing the high level concept:
  It doesn't use true system variables
  It does not use 3GPP notation
  It does not consider ranges
  Numerical example use arbitrary AMPR values
It will need to be translated in equations that uses 3GPP variable and naming and account for ranges where is applies.
This would require verification with measurements for Reverse IMD

## Slide 8: Problem statement
A-MPR for intra band EN-DC have been studied and agreed assuming equal LTE and NR back-off and equal PSD
It was assumed that for Type 1 UEs LTE and NR side would be fully aware of both RAT allocation and power.
  Combinations: DC_(n)71AA, DC_(n)41XA, DC_41_n41
Problem: given that LTE side cannot account for NR allocation and power how can we still use the specified A-MPR and avoid unnecessary NR back-off that would too often result in NR being dropped ?

## Slide 9: IMD behavior assumption
To be on the safe side for meeting emission requirements it is proposed to take a conservative approach to IMD behavior with varying only one of the signal
This is justified because:
  the 2dB/dB best case for IMD3 only applies for class A fixed supply , forward IMD and one sideband.
  Reverse IMD has been shown to behave differently – cf R4-1802985
  APT or class AB PAs do not have the ideal linear IMD behavior over a large range of power. Departing from this would cause significant power consumption increase,
Assumption (R4-1813289)
  Worst case IMD3 has 1dB/dB and IMD5 has 2dB/dB slope
  Best case IMD3 has 2dB/dB and IMD5 has 3dB/dB slope

## Slide 10: definitions
LTE input variables:
LTE UL allocation, PCMAX_LTE
PLTE_req: calculated Pout based on TPC commands,
NR input variables:
LTE UL RB allocation, NR UL RB allocation,
PNR_req: calculated Pout based on up commands,
PLTE_act: Pmax_NRscal: maximum NR Pout after power LTE/NR power sharing,
Xscale: removed from input variables in this document revision.
LTE variables:
Pmax_LTE: maximum LTE output power after stand alone LTE MPR/AMPR backoff,
PLTE_act: actual LTE Pout applied on LTE TX chain
NR variables:
Pmax_NRscal: maximum NR Pout after power LTE/NR power sharing,
BOeq: equal LTE/NR back-off based on EN-DC AMPR,
DBOLTE: missing (>0) or excess (<0) back-off on LTE side,
  IF IMD3: case where IMD3 related AMPR dominates,
  IF IMD5: case where IMD5 related AMPR dominates ,
BONR: NR back-off after LTE Back-off compensation,
Pmax_NRampr: maximum NR Pout after ENDC AMPR and LTE back-off compensation,
Pmax_NR: lowest Pmax from AMPR and power scaling processes,
PNR_act: actual NR Pout applied on NR TX chain after AMPR and power sharing if within Xterm range

## Slide 11: Proposed A-MPR Type 1 UE mechanism with NR compensation (incl. Power scaling)
LTE UL RB
allocation
Calculate LTE Back-off based on LTE SA MPR/AMPR*
PLTEreq
(LTE TPC)
Pmax_LTE
PLTE_act=Pmax_LTE
PLTE_act=PLTE_req
Y
N
Apply PLTE_act
Calculate LTE and NR equal Back-off (BOeq) based on EN-DC AMPR**
NR UL RB
allocation
PLTE_act
Pmax_NRscal = PCMAX_ENDC – PLTE_act
LTE power control
BOeq
DBOLTE=
BOeq - (Pmax_LTE - PLTE_act)
Y
N
IF IMD3: BONR=BOeq+DBOLTE
IF IMD5: BONR=BOeq+DBOLTE /2
IF IMD3: BONR=BOeq+DBOLTE /2
IF IMD5: BONR=BOeq+DBOLTE /3
Pmax_NRampr=PCMAX_NR-BONR
BONR
Pmax_NR = Min(Pmax_NRscal ,Pmax_NRampr)
NR AMPR & NR power sharing
PNRreq
(NR TPC)
N
Y
PNR_act=PNR_req
Drop NR
Apply PNRact
NR PC Xterm scaling
* Note that UE has its own AMPR equation that is better or equal to 36.101
** Note that UE has its own AMPR equation that is better or equal to 38.101-3
!!! Equations in italic uses linear power
NR power sharing
PLTE_req >
Pmax_LTE ?
NR AMPR
PNR_req > Pmax_NR?
DBOLTE>0?

## Slide 12: Numerical examples
PCMAX_LTE = PCMAX_NR = PCMAX_ENDC = 26dBm, Xscale ignored for sake of simplicity – can be taken into account in subsequent revision of this document.
LTE A-MPR from LTE UL RB allocation = 5dB,
Boeq = 10 dB dominated by IMD3 issue (ENDC equal Back-off AMPR from LTE & NR UL allocations)
Case1 PLTE_req = 22 dBm (LTE TPC request)
Pmax_LTE = 21 dBm [PCMAX_LTE – (LTE AMPR)]
PLTE_req= 22dBm > Pmax_LTE  PLTE_act = 21dBm
Pmax_NRscal = 24.3dBm, [Pmax_NRscal = PCMAX_ENDC – PLTE_act]
DBOLTE=10 - (26 - 21) = 5 dB [DBOLTE= BOeq - (Pmax_LTE - PLTE_act)]
For IMD3 compensation NR AMPR needs 5dB more 
  BONR = 15 dB [BONR=BOeq+DBOLTE] for IMD3 and DBOLTE > 0.
  Pmax_NRampr= 11 dBm [Pmax_Nrampr = PCMAX_NR - BONR]
  Pmax_NR = 11 dBm [Pmax_NR = Min (Pmax_NRscal ,Pmax_NRampr)]
  Case1b: PNR_req = 5 dBm < Pmax_NR  PNRact = 5dBm is applied
  Case1c: PNRr_eq = 16 dBm > Pmax_NR  Requested power is 5dB higher than Pmax_NR and is > Xterm  NR is dropped.
Case2 PLTE_req = 15 dBm
PLTE_req = 15 dBm < Pmax_LTE PLTE_act = 15dBm
Pmax_Nrscal = 25.6dBm,
DBOLTE=10 - (26 - 15)= -1dB, for IMD3 compensation NR AMPR needs 0.5dB less 
  BONR = 9.5dB [BONR=BOeq+DBOLTE /2] for IMD3 and DBOLTE < 0.
  Pmax_Nrampr = 16.5dBm
  Pmax_NR = 16.5dBm
  Case1b: PNR_req=15dBm < Pmax_NR  PNR_act=15dBm is applied
  Case1c: PNR_req=22dBm > Pmax_NR  delta 5.5dB > Xterm  NR dropped

## Slide 13: Intra-band ENDC Power Control Design
Mediatek
3GPP TSG RAN WG4 Meeting #88-bis
ChengDu, China, 8-12 October 2018

## Slide 14: Flow Chart of Power Control Design with Existing AMPR equations
Calculate LTE&NR Tx power
PCMAX_ENDC_total
PCMAX_NR_ENDC
PCMAX_LTE_ENDC
Check for fit
Is
a. Ptotal_ENDC ≤ PCMAX_ENDC_total?
b. Ptotal_ENDC_total-D≤ PCMAX_ENDC_total?
Allow dropping NR
Scaling is infeasible to specify
38.101-3 A-MPR
Check capable UE
Is UE capable singaling = true?
Transmit LTE/NR
Ptx_NR_ENDC
Ptx_LTE_ENDC
Transmit LTE/NR
Ptx_LTE_ENDC-D
Ptx_NR_ENDC-D
36.101 A-MPR
Solution is under discussion
a=true
a=false
b=true
a=false
b=false
Capable

## Slide 15
PCMAX_ENDC_total, PCMAX_NR_ENDC, PCMAX_LTE_ENDC are derived from existing A-MPR equaions
. Ptotal_ENDC, P_NR_ENDC, P_LTE_ENDC are required target power per CG from gNB/eNB
Ptx_NR_ENDC, Ptx_LTE_ENDC are real transmission power of NR/LTE after power control flow
All in DFT-S-OFDM
RB of LTE = NR = 10 RB
AMPR_ENDC=7.8dB  P_max_ENDC = 15.2dBm (allowable)
D = 4dB
Example 1: 0dBm/RB P_LTE=10dBm, P_NR=10dBm, P_total_ENDC=13dBm
Example 2: 5dBm/RB P_LTE=15dBm, P_NR=15dBm, P_total_ENDC=18dBm, Backoff = 2.8dB on both carrier
Example 2: 10dBm/RB P_LTE=20dBm, P_NR=20dBm, P_total_ENDC=23dBm, Backoff = 7.8dB on both carrier  drop NR

## Slide 16
Benefit
Remaining Issue
The “D” delta number is to be determined
TPC: If the LTE has higher priority, NR need to follow required LTE PSD to maintain equal PSD. With the assumption of NR is using normal slot, capable UE can re-calculate LTE and NR power before UL starts.

## Slide 17: Sprint intra-band EN-DC A-MPR input
If we go with NR-only A-MPR without any “fast LTE” or “delayed NR” we need to ensure the actual LTE power is used so in the A-MPR calcualtions, so that when LTE power is low, NR power can be increased, not just from a power sharing perspective but for minimizing A-MPR.
We believe that that it would be beneficial to use the 2:1 ratio for Near/far RIMDs, but we think this approach should be studied carefully vs. the 1:1 approach proposed by Skyworks. 1:1 may be conservative in some situations, but can be aggressive in other situations depending on where the RIMD is and if the A-MPR is being increased or decreased.
Performance of “all-NR” A-MPR vs. equal PSD A-MPR should be studied, and maybe included in Rel-16 if not in Rel-15.