## Slide 1: Way forward on NR PDCCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #88bis
Chengdu, China, 08 – 12 Oct, 2018
R4-1813928

## Slide 2: Agreements made from adhoc
Using parameters of test case 12 with AL=4 for 2Rx and 4Rx
Using parameters of test case 13 with (further offline)
  Option 1: AL =4 for 2Rx and 4Rx
  Option 2: AL= 8 for 2Rx and AL =4 for 4Rx
  How about test case 13??
Power allocation
  Assume EPRE ratio of PDCCH_DMRS to SSS is 0dB, and EPRE ratio of the PDCCH to PDCCH_DMRS is 0dB.

## Slide 3: AL 16
Options
  Option 1: Introduced test case(s) for AL 16 for both 2RX and 4RX: China Telecom, CMCC, NTT DoCoMo, Ericsson
  Option 2: Introduced test case(s) for AL 16 for 2RX only: Intel, QC, MTK
Agreements:
  Introduce AL =16 for 2 Rx
  For 4Rx part (further offline):
    Option1:
      Introduce AL=16 for 2Rx
      FFS for AL=16 for 4Rx, companies are encouraged to bring simulation results possible parameters to achieve reasonable SNR levels
    Option 2: we will introduce both 2Rx and 4Rx, meanwhile for 4Rx , detailed parameters FFS for 4Rx
Notes: China Telecom: prefer treat as 2Rx and 4Rx as package
China Mobile: we ok this proposal, first has 2Rx, 4rx can be further discussed
Ericson: If we can get proper SNR levels for 4Rx, then we have nothing, that’s the risk if we cannot agreed at least for 2Rx.
China Telecom: we will introduce both 2Rx and 4Rx, meanwhile for 4Rx , detailed parameters FFS
Intel: not clear for FFS, how we can run simulation for 4Rx
China Telecom: for BS, we have some test cases target for next year June.
Intel: We cannot just make decision for this manner, it’s ran decision. OK to further discuss. For NR performance timeline should be discussed in RAN level.

## Slide 4: Test cases with 4Rx with interleaved CCE-to-REG mapping
  Options: Test case 8, Bundle size =6 with interleave size as 3
  Option 1: Test case 6, 7 with REG bundle size =2, CORESET BW = 96 for both 2Rx and 4Rx (QC, Ericsson, NTT DoCoMo))
  Option 2: For 4Rx, test cases with interleaved (cases 6,7), using REG bundle size =6 (Intel)
Possible agreements
  Take Option 1 as baseline if no technical issues are identified
  Further evaluted above two options for case 6,7 and decided in RAN4#89 meeting.

## Slide 5: Time duration for one of test cases 6, 7 and 8
Options
  Option 1: Revise from 1 to 2 (NTT DoCoMo)
  Option 2: Keep previous agreement by using 1
Possible agreements
  Change test case 6 or 7 with Option 1 (2 symbols) to ensure testable SNR
  Keep test case 7, 8 with Option 2 (1 symbols)
Keep previous agreement as 1 for TDD

## Slide 6: Summary of simulation assumption
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | CORESET-interleaver-size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
1 | 15 | 1_0 | 24 | 39 | 2 | 2 | Non-interleaved | 6 | 2 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
2 | 15 | 1_0 | 24 | 39 | 2 | 4 | Non-interleaved | 6 | 2 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
3 | 15 | 1_1 | 24 | 50 | 2 | 2 | Non-interleaved | 6 | 2 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
4 | 15 | 1_1 | 48 | 50 | 2 | 4 | Non-interleaved | 6 | 2 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
5 | 15 | 1_1 | 48 | 50 | 2 | 8 | Non-interleaved | 6 | 2 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
6 | 30 | 1_0 | Option 1: 102 Option 2: 96 | 41 | 1 | 2 | Interleaved | Option 1: 2 Option 2: 6 | 2 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
7 | 30 | 1_1 | Option 1: 102 Option 2: 96 | 52 | 1 | 4 | Interleaved | Option 1: 2 Option 2: 6 | 2 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
8 | 30 | 1_1 | 90 | 52 | 1 | 8 | Interleaved | 6 | 3 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
9 | 120 | 1_0 | 60 | 40 | 1 | 2 | Interleaved | 2 | 2 | [TDL-A, 30ns, 75Hz] | 1x2 Low | NA
10 | 120 | 1_1 | 60 | 51 | 1 | 4 | Interleaved | 6 | 2 | [TDL-A, 30ns, 300Hz] | 1x2 Low | NA
11 | 120 | 1_1 | 60 | 51 | 1 | 8 | Interleaved | 2 | 2 | [TDL-A, 30ns, 75Hz] | 2x2 Low | NA

## Slide 7: Simulation assumption for 1 symbol PDCCH test case
Companies are encouraged to provide the simulation results in RAN4#88bis to decide the parameters
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
12 | 15 | 1_0 | 48 | 39 | 1 | 4 | Non-interleaved | 6 | [TDL-A, 30ns, 10Hz] | 1x2 Low | 1x4 Low
13 | 15 | 1_1 | 48 | 50 | 1 | Option 1: 8 for 2Rx and 4 for 4Rx Option 2: 4 | Non-interleaved | 6 | [TDL-A, 30ns, 10Hz] | 2x2 Low | 2x4 Low

## Slide 8: Simulation assumption for PDCCH AL16
Companies are encouraged to provide the simulation results in RAN4#88bis to discuss whether or not to introduce PDCCH AL16 requirements with 4Rx.
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
14 | 15 | 1_0 | 48 | 39 | 2 | 16 | Non-interleaved | 6 | [TDL-A, 30ns, 10Hz] | 1x2 Low | FFS
15 | 30 | 1_0 | 48 | 41 | 2 | 16 | Non-interleaved | 6 | [TDL-C, 300ns, 100Hz] | 1x2 Low | FFS
16 | 120 | 1_0 | 60 | 40 | 2 | 16 | Interleaved | 2 | [TDL-A, 30ns, 75Hz] | 2x2 Low | NA