## Slide 1: Transient period for SRS antenna switching
Qualcomm, Ericsson, Huawei, Vivo
3GPP TSG-RAN WG4#88bis Meeting R4-1814160
Chengdu, CN, October 8th ‒ 12th, 2018

## Slide 2: Background
In current version of 38.101-1 there are no specifications for transient period for SRS antenna switching.
This WF is to address the same.

## Slide 3: Proposal-1
10µs
Transient period
N+1 slot (Ant ‘x’)
SRS (Ant ‘x’)
N0 slot (Ant ‘x’)
10µs
10µs
Transient period
10µs
Transient period
Start of N+2 power PUSCH/PUCCH
End of N+1 power PUSCH/PUCCH
Start of N+1 power PUSCH/PUCCH
N+2 slot (Ant ‘x’)
Figure 6.3.3.7-1: PUCCH/PUSCH/SRS time mask when there is a transmission before or after or both before and after SRS when all physical channels use the same antenna port (Ant ‘x’)
N+2 slot (Ant ‘x’)
10µs
Transient period
  N+1 slot (Ant ‘x’)
SRS (Ant ‘y’)
N0 slot (Ant ‘x’)
10µs
15µs
Transient period
15µs
Transient period
Start of N+2 power PUSCH/PUCCH
End of N+1 power PUSCH/PUCCH
Start of N+1 power PUSCH/PUCCH
Figure 6.3.3.7-2: PUCCH/PUSCH/SRS time mask when there is a transmission before or after or both before and after SRS when SRS is sounded on a antenna port (Ant ‘y’) other than the one (Ant ‘x’) used by other physical channels before or after SRS

## Slide 4: Proposal-2
Figure 6.3.3.6-5: FR1 Time mask for 15kHz and 30kHz SCS for the case when consecutive SRS switching usage is between antenna switching & other sets
In the figure, ‘Other set’ belongs to a set in {beamManagement, codebook, nonCodebook}
SRS (other set)
End of OFF power requirement
Start of OFF power requirement
SRS ON power requirement
10µs
Transient period
10µs
Transient period
SRS (ant switch)
SRS (other sets)
SRS
10µs
Transient period
SRS ON power requirement
SRS ON power requirement
SRS ON power requirement
10µs
5µs
5µs
10µs
Note: reasoning for asymmetry in transient period is to make sure that the transient period is 5 usec on either side of SRS which has is a power change. This will be similar to other SRS power change cases in the current standard.

## Slide 5: Proposal-3
Proposal: UE RF requirements do not apply in the transient period for SRS switching for Figure 6.3.3.7-2 and Figure 6.3.3.6-5

## Slide 6: Proposal-4
Proposal: In case of inter-band CA, UE transmit performance requirements to apply only to the physical channels on each CC which are not affected by the SRS switching on any of the other CCs.
This proposal should be reflected in 38.133

## Slide 7: Agreements
Following proposals have been agreed and CR will be submitted in the next meeting:
  Proposal 1
  Proposal 2
  Proposal 3
  Proposal 4