## Slide 1: 3GPP TSG-RAN WG4 Meeting #88Bis Chengdu, China, 8th – 12th Oct, 2018
Huawei, HiSilicon, …
Way forward on 8Rx demodulation and CSI tests
R4-1814230

## Slide 2: Applicability rule - Control Channel
Scenario1: All test cases specified in 8.2 to 8.8 for control channel with 2Rx
  For UE with supported 2Rx RF bands: UE is tested on any of the 2Rx supported RF band, requirements specified with 2Rx should be applied.
  For UE without any 2Rx supported RF bands or 4Rx supported RF bands : UE is tested on any of the 8Rx supported RF bands, requirements specified with 2Rx by tightening 1.5dB should be applied
  For UE without 2Rx supported RF bands but with 4Rx supported RF bands
    Option 1: UE is tested on any of the 8Rx supported RF bands, requirements specified with 2Rx by tightening 1.5dB should be applied
    Option 2: UE is tested on any of the 4Rx supported RF bands, requirements specified with 2Rx by tightening 1.5dB should be applied
Scenario2: All test cases specified in 8.10 for control channel with 4Rx
  For UE with 4Rx supported bands: UE is tested on any of the 4Rx supported RF bands, requirements specified with 4Rx should be applied
  For UE without 4Rx supported bands: UE is tested on any of the 8Rx supported RF bands, requirements specified with 4Rx should be applied.

## Slide 3: CA test
Issues need to be considered for CA
  Simulations for single carrier demodulation performance for other bandwidths other than 10MHz are needed
  Test applicability rule and antenna connection for CA test

## Slide 4: SDR tests applicability rule
Option1: Follow the 4Rx approach with the consideration of a scaling factor; e.g.
Other options not precluded