## Slide 1: Way forward on demodulation and CSI requirements for high capacity stationary wireless link and 1024QAM
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #88Bis R4-1814231
Chengdu, China, 08 - 12 October 2018
Agenda Item: 6.6.4

## Slide 2: Background
Parameters | Value
Bandwidth | 10MHz
Channel model | EPA5
CFI (OFDM symbol for control channel) | 1
Duplex mode | FDD, TDD
For 1024QAM demodulation requirements, the following test cases are agreed to be defined for both FDD and TDD:
No. | TM | PMI feedback (pre-coding) | MIMO layer | MCS | Antenna config.
1 | TM4 | Wideband PMI Feedback (PUSCH 3-1, Reporting interval =1) | 1-layer | MCS#23 (with 52752 bits) | 4x2 Low
2 | TM4 | Wideband PMI feedback (PUSCH 3-1, Reporting interval =1) | 2-layer | MCS#23 (with 52752 bits) | 4x4 Low
3 | TM9 (Note 1) | Per-PRG Random Precoder | 1-layer | MCS#23 (with 52752 bits) | 4x2 Low
4 | TM9 | Wideband PMI feedback | 2-layer | MCS#23 (with 52752 bits) | 4x4 Low
Note 1: For TM9, configure 4Tx with 2 CRS ports

## Slide 3: SDR test
Not define 8-layer + 1024QAM SDR test in Rel-15
SDR test applicability
  Option 1: Do not consider mixed modulation order, only test on those band or band combinations that support 1024QAM, follow 4Rx SDR structure
  Option 2: Consider mixed modulation order, the possible combinations: [64QAM, 1024QAM], [256QAM,1024QAM],[1024QAM]

## Slide 4: CQI reporting test
Agreed test:
  Minimum requirement PUCCH 1-0 (Cell-Specific Reference Symbols): CRS based TM single codeword with TM1 under static channel in Annex B.1
    Bandwidth:
      FDD: 10MHz
      TDD: 20MHz
SNR point: Choose [28dB] and [29dB] for FDD and TDD respectively