## Slide 1
3GPP TSG-RAN WG5 #3-5G-NR Adhoc R5-185838 Jaipur, India, 08th – 12th October 2018
Source: Anritsu
Title: Calibration methods for multiple-cell signalling tests in FR2
Agenda item: 6.1.18
Document for: Agreement

## Slide 2: 0. Background
In RAN5#80, OTA signalling test setups were discussed mainly focusing on single-cell test cases and it has been agreed as the following regarding single-cell signalling test cases. [2][3]
The working assumption is that the DFF or IFF based OTA test methodologies defined in clause 5.2.1 and 5.2.3 respectively of TR 38.810 should be used for Signalling test, although the switches can be removed to reduce the system complexity.
  This implicitly specifies that the same calibration method used in UE RF measurements outlined in 5.2.1.3.1 and 5.2.3.3.1 of TR 38.810 shall be used for single-cell test cases as a working assumption.
Note: For single cell test cases, which is the current scope for FR2 testing, usage of NF test methodology is not precluded
And we have also got the conclusion that the minimum number of distinguishable power levels required for FR2 SIG test cases to be further analyzed and proposed at the next meeting. [1]
1. Overview
In this slide, having multiple-cell signalling test cases in mind, we think about the test-system dynamic range required to firmly trigger the measurement reporting event A1 to A6 under the condition that each of two calibration methods explained in section 2 is used. And the pros and cons of the two calibration methods are also discussed.

## Slide 3: 2. Calibration methods for signaling tests
In this slide, the following two calibration methods are compared.
The same calibration method as the one used in UE RF measurements (hereafter : UE-RF CAL) : See section 3
  The calibration method is specified in 5.2.1.3.1 and 5.2.3.3.1 of TR38.810.
The calibration method using RSRP measurement reporting (hereafter : RSRP reporting CAL) : See section 4
  In signaling tests, we don’t need to care about an actual absolute physical power. What we need to care about is only whether we can make the DUT recognize a power according to a test scenario. The RSRP-measurement-reporting trigger should be based on RSRP-measurement results. So if we use an RSRP-measurement-reported level as a reference, we can adjust the DL-signal power so that the DUT recognize the signal level as a target level.
  For example, we think about a situation where the DUT recognize a signal power as -50dBm(=Xref) when output power setting is 0dBm(=Xset0) at the gNB emulator. In such a case, if a scenario specifies to output a signal level to be recognized as -60dBm(=Xt), we should know that outputting -10dBm(Xt_set = Xset0 + Xt – Xref) from the gNB emulator should make the DUT recognize the signal power level as about -60dBm(= Xt). In this case, the uncertainty would be mainly determined by the linearity and variable uncertainties.

## Slide 4: 3. UE-RF CAL
SS
measurement antenna
DUT
array antenna
RF
Baseband
RSRP measurement point
EIS uncertainty
Antenna gain and beamforming gain uncertainty
RSRP absolute uncertainty
Calibration procedure :
Calibration is performed by using a calibration antenna with known gain values, following the same method used in UE RF measurements. (Refer to 5.2.1.3.1 and 5.2.3.3.1. of TR38.810 [5].)
Figure 3.1 RSRP uncertainty in UE-RF CAL
RSRP uncertainty in UE-RF CAL
In signalling tests, as the measurement events take place in a DUT referring to RSRP absolute levels, the uncertainty we need to care about is the uncertainty of RSRP absolute level recognized by the DUT. Since UE-RS CAL adjusts the absolute power levels, the RSRP uncertainty when using UE-RF CAL can be estimated as the summation of the following absolute uncertainties.
EIS uncertainty
Antenna gain and beamforming gain uncertainty
RSRP absolute uncertainty
If we assume the minimum and the maximum UE-antenna gain as shown in Table 3.1, the RSRP uncertainty when using UE-RF CAL can be estimated as shown in Table 3.2. Here, as the “Antenna gain and beamforming gain uncertainty” and “RSRP absolute uncertainty” are not 95%-confidence-level uncertainty but the specified ranges, the total uncertainty in Table 3.2 is calculated by simple summation (not by RSS).

## Slide 5: 3. UE-RF CAL (Cont’d)
 | Minimum UE-antenna gain condition | Maximum UE-antenna gain condition
Array size | 4x1 | 8x2
Array gain | 6.0 dB (=10*log10(4x1) ) | 12.0 dB (= 10*log10(8x2) )
Element gain | 1.0 dBi | 5.0 dBi
Total UE-antenna gain | 7.0 dBi | 17.0 dBi
Uncertainty | DFF | IFF | Note
EIS uncertainty [dB] | [6.66] | [6.49] | See Table B.1.1.3-2 and Table B.1.3.3-2 of [5].
Antenna gain and beamforming gain uncertainty [dB] | ±[5] | ±[5] | See Table 3.1. Could be bigger as much as beamforming gain uncertainty.
RSRP absolute uncertainty [dB] | ±[6] | ±[6] | See Table 10.1.3.1.1-1 and Table 10.1.5.1.1-1 of [4].
Total RSRP uncertainty () [dB] | [17.66] | [17.49] | Simple summation (not RSS) of uncertainty elements
Minimum required dynamic range [dB] | [35.32] | [34.98] | See section 6.
Uncertainty | DFF | IFF | Note
EIS uncertainty [dB] | [6.66] | [6.49] | See Table B.1.1.3-2 and Table B.1.3.3-2 of [5].
Antenna gain and beamforming gain uncertainty [dB] | ±[5] | ±[5] | See Table 3.1. Could be bigger as much as beamforming gain uncertainty.
RSRP absolute uncertainty [dB] | ±[6] | ±[6] | See Table 10.1.3.1.1-1 and Table 10.1.5.1.1-1 of [4].
 | [17.66] | [17.49] | Simple summation (not RSS) of uncertainty elements
Minimum required dynamic range [dB] | [35.32] | [34.98] | See section 6.
Table 3.2 RSRP uncertainty estimation in UE-RF CAL
Table 3.1 Assumed Minimum and Maximum UE-antenna gain
Uncertainty: +/-5dB
= (17.0-7.0)/2

## Slide 6: 4. RSRP reporting CAL
SS
measurement antenna
DUT
array antenna
RF
Baseband
RSRP measurement point
stable uncertainty + variable uncertainty
Calibration procedure :
Establish connection between SS and DUT.
Adjust angle between measurement antenna and DUT to have Rx-beam peak.
Get an RSRP measurement report from DUT, where the reported level is denoted as Xref [dBm], while transmitting DL-signal with the power setting Xset0 [dBm] from SS.
Calibrated signal transmission:
When the target RSRP level is Xt [dBm], transmit DL-signal with the power setting Xset_t [dBm] from SS.
  Xset_t = Xset0 + (Xt – Xref) (1)
The level uncertainties between SS and DUT can be categorized into stable and variable uncertainties.
Figure 4.1 RSRP uncertainty in RSRP reporting CAL
RSRP uncertainty in RSRP reporting CAL
The calibration procedure is shown in Figure 4.1. Although the original uncertainty elements when using RSRP reporting CAL are the same as the ones when using UE-RF CAL, it is convenient to categorize those uncertainty elements into stable and variable uncertainties.

## Slide 7: 4. RSRP reporting CAL (Cont’d)
Uncertainty analysis :
Xref = Xset0 + GMEASant – Lpathloss + GUEant + Estable + Elinearity1 + Evar1 (2)
Xt_act = Xset_t + GMEASant – Lpathloss + GUEant + Estable + Elinearity2 + Evar2 (3)
Here,
  Xt_act : actual RSRP level when target is Xt
  Estable : stable uncertainty
  Evar1, Evar2 : variable uncertainty
  Elinearity1, Elinearity2 : linearity uncertainty of the devises composing the test system and a DUT
The following equation derived by subtracting (2) from (3).
Xt_act – Xref = Xset_t – Xset0 + Elinearity2 – Elinearity1 + Evar2 – Evar1 (4)
Substituting (1) into (4) makes the following equation.
Xt_act = Xt + Elinearity2 – Elinearity1 + Evar2 – Evar1 = Xt + (5)
Elinearity1 + Evar1 (6)
Elinearity2 + Evar2 (7)
In short, the uncertainty in a target RSRP measurement level shall be determined by variable uncertainties and linearity error.
Figure 4.2 RSRP uncertainty analysis in RSRP reporting CAL
As shown in Figure 4.2, when using UE-RF CAL, the uncertainty of RSRP recognized by a DUT shall be determined only by the variable uncertainty and linearity uncertainty. As it is likely that most of the uncertainties are stable and the linearity uncertainty would be much smaller than the absolute-level uncertainties discussed in section 3, the uncertainty when using RSRP reporting CAL () would be much smaller than the one when using UE-RF CAL ().

## Slide 8: 4. RSRP reporting CAL (Cont’d)
The most of variable uncertainty is likely to come from “beamforming gain uncertainty”. As the beamforming in an NR-UE would be controlled digitally, which means that the beam direction should have some finite resolution step, there should be at least two possible beamforming controls at border angles. This could be an unstable uncertainty source. So if RAN4 determines the “beamforming gain uncertainty”, we can estimate the variable uncertainty () as an uncertainty equal to or smaller than “beamforming gain uncertainty”.
If RAN4 specifies “RSRP linearity uncertainty”, which is the linearity uncertainty in UE side, by summing it up with the linearity uncertainty in the test system side, the linearity uncertainty would be estimated as below.
Referring to (5) in Figure 4.2, the uncertainty in using “RSRP reporting CAL” can be estimated as the following.
Here, uncertainties are summed up by simple summation for the meantime. It would be necessary to consider which of “simple summation” and “RSS” is better for uncertainty calculations.
Although the actual variable uncertainties and the linearity uncertainties could be dependent on various conditions, such as signal levels, the relative level uncertainty () is assumed to be estimated as the worst case.
DUT
Test antenna
Figure 4.3 Instability of “beamforming gain uncertainty”
At an angle around the border of beamforming-control-resolution steps, there could be multiple possible beamforming controls, which could be an unstable uncertainty source.

## Slide 9: 4. RSRP reporting CAL (Cont’d)
Measurement point of signal power
Referring to 6.2.2.2 in the current TS38.508-1[6], the signal levels are specified as the power at Rx-antennas of a DUT. However, once we adopt “RSRP reporting CAL” for multiple-cell test cases, the signal levels would be specified as the power at RSRP measurement point (UE baseband). For further discussions on the definition of measurement point or the selection of calibration methods, please refer to section 8.
Black-box approach
The uncertainty originating from Black-box approach, which is the path-loss and measurement-antenna-directivity uncertainty, shall be mostly stable. So, those uncertainties can be cancelled out by RSRP reporting CAL as shown in Figure 4.2.
When the DFF setup for UE RF measurements is commonly used for signaling tests, as the DUT antenna size gets bigger in DUT-antenna configuration 1/2 or the range where antenna panels exist gets bigger in DUT-antenna configuration 3, the measurement distance could be in the range of near-field. In the near-field, the radiation pattern of the DUT and the measurement antenna could be changed from the one in far-field. However, as long as the gain deviation is stable, the uncertainty should be cancelled out by RSRP reporting CAL as shown in Figure 4.2.
  The near-field could also be used as long as wide enough dynamic range and small enough variable uncertainties are secured, if we adopt “RSRP reporting CAL”.
  We need to think of measurement-distance conditions under which we can secure wide enough dynamic range and small enough variable uncertainties.
    Dynamic range could be smaller when UE-beam-steering pointing error gets bigger in near field.
    Random uncertainties could be bigger when the distance between a UE and the measurement antenna gets too small to keep the UE-beamforming stable.
An example of RSRP reporting CAL
Refer to Appendix B.

## Slide 10: 5. Number of distinguishable levels required to trigger measurement-reporting events
Event Type | Event meaning | Level allocation at T1 | Level allocation at T2 | Note
Event A1 | Serving cell becomes better than threshold | #3: N/A #2: threshold #1: Serving cell level | #3: Serving cell level #2: threshold #1: N/A | 
Event A2 | Serving cell becomes worse than threshold | #3: Serving cell level #2: threshold #1: N/A | #3: N/A #2: threshold #1: Serving cell level | 
Event A3 | Neighbour becomes offset better than SpCell | #2: Serving cell level #1: Neighbour cell level | #2: Neighbour cell level #1: Serving cell level | Offset = 0
Event A4 | Neighbour becomes better than threshold | #3: N/A #2: threshold #1: Neighbour cell level | #3: Neighbour cell level #2: threshold #1: N/A | 
Event A5 | SpCell becomes worse than threshold1 and neighbour becomes better than threshold2 | #3: SpCell level #2: threshold1 #1: N/A #3’: N/A #2’: threshold2 #1’: Neighbour cell level | #3: N/A #2: threshold1 #1: SpCell level #3’: Neighbour cell level #2’: threshold2 #1’: N/A | 
Event A6 | Neighbour becomes offset better than SCell | #2: SCell level #1: Neighbour cell level | #2: Neighbour cell level #1: SCell | Offset = 0
Table 5.1 Level transition to trigger measurement-reporting events
Note) Here, the level relationship is assumed to be : Level#3 > Level#2 > Level#1.
Copied from : <http://www.sharetechnote.com/html/Handbook_LTE_MultiCell_Measurement_LTE.html>
Figure 5.1 Measurement-reporting event triggering
The signal level transition which triggers the measurement-reporting events are shown in Table 5.1. Assuming that one test scenario only triggers one measurement-reporting event, the minimum required number of distinguishable levels shall be three.

## Slide 11: 6. Dynamic range of measurement system required to firmly trigger measurement-reporting events
Threshold
(Level#2)
Level#3
Level#1
Level#2
Level#1
Level#2
Level#1
Threshold
(Level#2)
Level#3
Level#1
Dynamic range in UE-RF CAL
Dynamic range in RSRP reporting CAL
When we think about relative uncertainty, the threshold level should also have uncertainty.
Figure 6.1 Required minimum dynamic range in UE-RF CAL and RSRP reporting CAL
Figure 6.1 and Table 6.1 show the minimum dynamic ranges at an RSRP-measurement point required to firmly compare two signal levels with a threshold or to firmly compare two signal levels each other for each cases of using UE-RF CAL and RSRP reporting CAL.
When using UE-RF CAL, the estimated dynamic range may not be attained even with a high-power amplifier.
When using RSRP reporting CAL, the required dynamic range would be small enough.

## Slide 12: 6. Dynamic range of measurement system required to firmly trigger measurement-reporting events (Cont’d)
Calibration method | comparison with threshold | comparison between two levels | Note
UE-RS CAL | [34.98] (in IFF) | [35.32] (in DFF) [34.98] (in IFF) | See Table 3.2. Even with a high power amplifier, the estimated dynamic range may not be attained. ( See Appendix A.)
RSRP reporting CAL | ( smaller than 10dB?) | ( smaller than 5dB?) | 
Calibration method | comparison with threshold | comparison between two levels | Note
UE-RS CAL |  |  | See Table 3.2. Even with a high power amplifier, the estimated dynamic range may not be attained. ( See Appendix A.)
RSRP reporting CAL |  |  | 
Table 6.1 Required dynamic range to firmly trigger the RSRP measurement report
Here, it may be necessary to think about whether uncertainty in signalling tests can be calculated with 95% confidence level, because the 5%-probability of not triggering an event may not be low enough.

## Slide 13: 7. Pros and Cons for each of the calibration methods
 | Pros | Cons
UE-RF CAL | Calibration measurement results can be used commonly for signaling tests with any DUTs. (As long as RSRP reporting is used for Rx-beam-peak search, this merit over RSRP reporting CAL is very limited.) | Required dynamic range would be too big to realize in multiple-cell test cases.
RSRP reporting CAL | Required dynamic range would be small enough. Absolute level calibration using a reference antenna whose gain is known is not necessarily required. The DFF setup for UE RF measurements could be used for signaling tests in Black-box approach. Uncertainty for near-field measurements could be small, although the condition of allowable measurement-distance range may need to be clarified. | Calibration procedure needs to be performed for each DUT.
Refer to Table 7.1 about the Pros and Cons for each of the calibration methods ( UE-RF CAL and RSRP reporting CAL ).
Table 7.1 Pros and Cons for each of the calibration methods

## Slide 14: 8. Calibration method selection
test cases | Measurement point of default powers | Calibration method
single-cell test cases | Rx-antennas of a DUT or RSRP measurement point in a DUT | UE-RF CAL or RSRP reporting CAL
multiple-cell test cases | RSRP measurement point in a DUT | RSRP reporting CAL
Table 8.1 Measurement point and calibration method of default FR2 NR powers
Referring to the current TS38.508-1[6], it only specifies test conditions for single-cell test cases in FR2 NR, where UE-RF CAL is used.
As explained here, however, it would be difficult to use UE-RF CAL in multiple-cell test cases considering the dynamic range requirement.
We propose to define as in Table 8.1 the measurement point and calibration method for FR2 default powers in 6.2.2.2 of TS38.508-1. In Table 8.1, the new condition of using RSRP reporting CAL has been added, while the original calibration method UE-RF CAL is kept as one of the selections for single-cell test cases.

## Slide 15: 9. Conclusions
Observations
  The uncertainty when using RSRP reporting CAL () would be much smaller than the one when using UE-RF CAL ().
  If RAN4 determines the “beamforming uncertainty” and “RSRP linearity uncertainty”, we can estimate the uncertainty when using RSRP reporting CAL ().
  Once we adopt “RSRP reporting CAL” for multiple-cell test cases, the signal levels would be specified as the power at RSRP measurement point (UE baseband).
  The near-field could also be used as long as wide enough dynamic range and small enough variable uncertainties are secured, if we adopt “RSRP reporting CAL”.
  We need to think of measurement-distance conditions under which we can secure wide enough dynamic range and small enough variable uncertainties.
  Assuming that one test scenario only triggers one measurement-reporting event, the minimum required number of distinguishable levels shall be three.
  When using UE-RF CAL, the estimated dynamic range may not be attained even with a high-power amplifier.
  When using RSRP reporting CAL, the required dynamic range would be small enough.
  It may be necessary to think about whether uncertainty in signalling tests can be calculated with 95% confidence level, because the 5%-probability of not triggering an event may not be low enough.
Proposals
  We propose to adopt “RSRP reporting CAL” for FR2 multiple-cell signalling test cases and to add a new option of using “RSRP reporting CAL” in FR2 single-cell signalling test cases.
  It is proposed to ask RAN4 to determine the “beamforming uncertainty” and “RSRP linearity uncertainty” to make it possible to estimate the uncertainty when using RSRP reporting CAL.

## Slide 16: References
[1] R5-185131, “Reuse of demodulation setup for signalling tests in FR2”, Anritsu
[2] R5-185132, “OTA Chamber requirements for 5G NR Signalling test cases”, Keysight Technologies UK
[3] R5-185168, “Introduction of OTA signalling test environment”, Keysight Technologies UK Ltd, Anritsu Ltd
[4] R4-1811913, “CR to TS38.133: Implementation of endorsed draft CRs from RAN4-AH-1807 and RAN4 #88”, Intel
[5] TR38.810 v16.0.0, “Study on test methods”, RAN4, 2018-09
[6] TS38.508-1 v15.1.0, “Part 1: Common test environment”, RAN5, 2018-09

## Slide 17: Appendix A : Dynamic range of measurement system
 | 24GHz | 43GHz | 
UE Antenna Gain | 7 | 8 | dBi
NF(F_UE) | 10 | 12 | dB
Implementation loss | -10 | -11 | dB
Nktb | -174 | -174 | dBm/Hz
Table A-1: Assumed UE parameters
(copied from Table B.3.1.1-1 in TR38.810)
 | 24GHz | 43GHz | 
P1dB amplifier power | +23 | +23 | dBm
Backoff from P1dB | -13 | -13 | dB
Cable loss | -4 | -7 | dB
Probe antenna gain | 12 | 12 | dB
Power from Test antenna | +18 | +15 | dBm
Transmission bandwidth | 100M, 200M, 400M, 800M, 1G |  | Hz
Table A-2: Assumed Test system parameters
(copied from Table B.3.1.1-2 in TR38.810)
 | 24GHz | 43GHz | 
@0.5m separation | -54.0 | -59.1 | dB
@0.7m separation | -57.0 | -62.0 | dB
@1.0m separation | -60.1 | -65.1 | dB
Table A-3: Free Space path loss
(copied from Table B.3.1.1-3 in TR38.810)
 | Signal | Noise | 
Power from Test antenna | +15 |  | dBm/400MHz
Free space path loss @0.7m, 43GHz | -62.0 |  | dB
Scale power 400MHz to 1Hz | -86 |  | dB
Maximum allocated RE ratio (100%) | 0 |  | dB
UE Antenna Gain | +8 |  | dB
UE Implementation loss | -11 |  | dB
Wanted powers | -136 |  | dBm/1Hz
Thermal Noise |  | -174 | dBm/1Hz
UE Noise figure |  | +12 | dB
UE Noise |  | -162 | dBm/1Hz
Table A-4: Example signal level calculation
for 400MHz BW, 43GHz, 0.7m, allocation not-limited
The assumed maximum power in the table would require high power amplifier.
Dynamic range:
If the value of the minimum required SNR to perform signalling testing is assumed tentatively to be “ [dB]”, the typical dynamic range ( ) can be calculated as below. Here, “typical” means the value derived without taking account of uncertainties.
( with high power amplifier )
If we use a moderate output power amplifier, the maximum signal level would be around 10dB lower than the above case.
( without high power amplifier )

## Slide 18: Appendix B : An example of RSRP reporting CAL
Here is an example of how to trigger an Event A using RSRP reporting CAL.
  2.5[dB]
Calibration Procedure :
Place a UE at the angle identified as the Rx-beampeak direction.
Transmit downlink signal with the power setting “-30dBm/SCS” from the serving cell. (Xset0 = -30dBm/SCS)
Get an RSRP report from the UE. The reported value here is assumed to be “-70dBm/SCS”. (Xref = -70dBm/SCS)
Scenario Execution :
We assume to perform a scenario where Event A1 needs to be triggered with the power settings below.
Transmit downlink signal during the T1 time-frame with the power setting “-45dBm/SCS (=Xset_t)” from the serving cell, aiming to make the UE recognize the downlink power as “-85dBm/SCS (=Xt)”.
  Xset_t = Xset0 + (Xt – Xref) = -30 + (-85 + 70) = -45 [dBm/SCS]
At the start timing of the T2 time-frame, transmit downlink signal with the power setting “-35dBm/SCS (=Xset_t)” from the serving cell, aiming to make the UE recognize the downlink power as “-75dBm/SCS (=Xt)”.
  Xset_t = Xset0 + (Xt – Xref) = -30 + (-75 + 70) = -35 [dBm/SCS]
We can expect that the UE should detect the Event-A1 trigger at the transition timing between the T1 and T2 time-frames.
Event Type | Event meaning | Level allocation at T1 | Level allocation at T2
Event A1 | Serving cell becomes better than threshold | #3: N/A #2: threshold (= -80dBm/SCS) #1: Serving cell level (= -85dBm/SCS) | #3: Serving cell level (= -75dBm/SCS) #2: threshold (= -80dBm/SCS) #1: N/A