## Slide 1: WF on NR MIMO OTA
CAICT, Spirent, Keysight Technologies, Qualcomm, ETS-Lindgren, MVG
3GPP TSG-RAN WG4 Meeting #89 R4-1815933
Spokane, USA, 12 – 16 November 2018
Agenda item: 10.4.1
Document for: Approval

## Slide 2: Scenarios for NR MIMO OTA
  FR1 scenarios
    For 2x2: Urban Macro
    For 4x4: Urban Micro
  FR2 static
    Urban Micro street canyon, Indoor

## Slide 3: BS Antenna Assumptions
For FR1 and FR2, directive BS antennas need to be considered
Working Assumption:
  For FR1 bands with frequency higher than 2.5GHz: BS antenna is 8×8 with uniform rectangular array (URA) with half wavelength inter-element spacing
  For FR1 bands with frequency lower than 2.5GHz: BS antenna has 32 elements (assume 4x8 is a typical configuration) with uniform rectangular array (URA) with half wavelength inter-element spacing
  For FR2: BS antenna is 8x16 with uniform rectangular array (URA) with half wavelength inter-element spacing

## Slide 4: Framework on adjusting CDLs to map the scenario
  The CDL-A, CDL-B and CDL-C models in TR38.901 are the baseline for channel model scaling
  Scaling the following parameters for the scenarios defined in Page 2
    rms DS target, AS scaling, angle rotation
    translate and scale ray angles if needed
  CE vendors to provide proposals next RAN4 meeting

## Slide 5: FR1 Performance metric
  Both UE noise-limited condition and interference-limited condition will be studied for FR1 MIMO OTA
    Further down-selection is needed based on the feedback from UE vendors and operators
  For interference-limited condition, how to control the DL signal and noise is FFS
    AWGN or Directional noise
    Fixed noise level or DL power

## Slide 6: Test methods for FR1
MPAC shall be considered reference methodology:
  The optimized probe locations and number of probes need to be studied based on the scenarios, the CDL models, and BS antenna assumptions
  Backward capability with LTE MIMO OTA is desirable
RTS shall be considered a harmonized methodology for NR FR1

## Slide 7: Test methods for FR2
3D MPAC methodology shall be studied as the starting point for FR2 MIMO OTA
  The optimized probe locations and number of probes need to be studied based on the scenarios, the CDL models, and BS antenna assumptions
  Far-field criteria and test zone should be studied