## Slide 1: WF on TDD configuration for UE Tx test
Ericsson
3GPP TSG-RAN WG4 Meeting #89
Spokane, WA, USA, 12 – 16 November, 2018
R4-1816610

## Slide 2: Background
RAN4 received the LS from RAN5 on the issue for UE Tx test for simultaneous LTE and NR transmissions in EN-DC [1][2]
  Issue 1
    As a fundamental issue regardless of test cases and EN-DC types, it is not clear from TS 38.101-3 v15.3.0 whether the each TRx requirment should be tested with synchrous EN-DC or asynchrnous EN-DC. In case simultansous EN-DC shall apply, UL RMC of LTE and NR, measurement period and time offset between LTE and NR should be harmonizedly specified.
  Issue 2
    Even if the TRx requirements are tested with synchronous EN-DC, it is observed simultaneous transmission of LTE and NR is not ensured for SCS 15kHz and SCS 30kHz as analyzed above.
  Issue 3
    For TDD-TDD intra-band LTE-NR EN-DC case, current NR UL RMC and LTE UL RMC do not avoid DL/UL interference.
[1] R4-1814414, “LS to RAN4 on simultaneous LTE and NR transmissions in EN-DC”, RAN5

## Slide 3: Background
Additionally RAN5 pointed out [2]:
  the measurement period UE maximum output power, Transmit OFF power, and frequency error, shall be at least one sub frame (1ms) according to TS38.101-1 and TS38.101-2.
[2] R4-1814415, “LS on RAN4-RAN5 5G-NR RF pending issues during RAN5#3-5G-NR Adhoc
TC | Title | Items pending on RAN4 | R4 part | R5 target
6.2.1 6.3.2 6.4.1 | UE maximum output power Transmit OFF power Frequency error | “Confirm measurement period for MOP, transmit off power and frequency error: - On one hand minimum time unit that can be scheduled in NR is one slot - If 1ms is the measurement period for these requirements, there will be discontinuous measurements in time to collect 1ms according to current UL RMC definition for certain SCS.” | RF, Demod | RAN5#81 (Nov-18)

## Slide 4: Additional RMC table in TS 38.101-1/2/3
TS38.101-3 introduces new LTE RMC (assuming LTE TDD configuration 2 and special subframe configuration 7) to ensure the synchronous operation for intra-band LTE-NR TDD-TDD EN-DC.
TS38.101-1 revises UL RMC for SCS=60kHz to ensure 1ms UL transmission period. DL RMC is also revised accordingly to align to UL.
TS38.101-2 introduces new UL RMC for both SCS=60kHz and SCS=120kHz to ensure 1ms UL transmission period. This new table is only applicable for 1) UE maximum output power, 2) Transmit OFF power, and 3) Frequency error.

## Slide 5: Proposal of TDD configuration for UE RF RMC
NR UE FR | NR UE SCS | NR DL TDD config | NR UL TDD config | LTE TDD config | Necessary changes
NR FR1 | 15kHz | DDDSU | DDDSU | Config 2/SSF7 | LTE RMC configuration in TS38.101-3 (QC)
NR FR1 | 30kHz | 7D1S2U | 7D1S2U | Config 2/SSF7 | LTE RMC configuration in TS38.101-3 (QC)
NR FR1 | 60kHz | 14D2S4U, S1={12D,2G}, S2={6G,8U} | 14D2S4U, S1={12D,2G}, S2={6G,8U} | Config 2/SSF7 | NR UL and DL RMC configuration in TS38.101-1 (E///) LTE RMC configuration in TS38.101-3 (QC)
NR FR2 | 60kHz | DDDSU | 1: DDDSU 2: 3D1S4U, S={4D,6G,4U} | Config 2/SSF7 | NR UL RMC configuration in TS38.101-2 (E///) LTE RMC configuration in TS38.101-3 (QC) New NR UL RMC configuration (2) is applicable for MOP, Tx power off, and freq error
NR FR2 | 120kHz | DDDSU | 1: DDDSU 2: 7D1S8U, S={12D,2G} | Config 2/SSF7 | NR UL RMC configuration in TS38.101-2 (E///) LTE RMC configuration in TS38.101-3 (QC) New NR UL RMC configuration (2) is applicable for MOP, Tx power off, and freq error
Red: New RMC in RAN4#89

## Slide 6: FR1 (for information)
1ms UL

## Slide 7: FR2 (for information)
1ms UL