## Slide 1: WF n41 – B40 Coexistence
Qualcomm, Inc., Huawei, Skyworks, […]
3GPP TSG-RAN WG4#89 Meeting R4-1816614
Spokane, USA, 12 – 16 November 2018
Agenda 7.6.9.5

## Slide 2: Background
UE has to coexist with WIFI (ISM band) and E-UTRA band 40 at the same time
Due to UE FE complexity and multi-mode operation it can be a challenge to filter both bands at the same time due to filter size.
Filter response creeps up in E-UTRA band 40, while trying to reject the ISM band.
NR has larger BW (50MHz – 100MHz) than LTE BW class C (40MHz)
For contiguous RB allocations, composite 5th order distortion can become an issue.
For non-contiguous RB allocations as in EN-DC, 3rd order distortion will become an issue.
MPR is only designed to help meet the general spurious emission requirement of -30dBm/MHz

## Slide 3: Background (2/2)
As discussed in the RAN4#89 in Spokane, synchronous operation does not have to be discussed and focus on asynchronous operation.
For asynchronous operation, it was discussed in [1] [2] to restrict RB start as a function of offset frequency and bandwidth from the low band edge of NR band n41.
Operators are concerned about restricting RB allocations.

## Slide 4: WF details
RAN4 will study following options in next meeting for B40-n41 co-existence assuming asynchronous operation for contiguous RB allocations.
RAN4 will also study A-MPR in next meeting for B40 – DC_41A-n41A EN-DC co-existence assuming asynchronous operation for non-contiguous RB allocations.
Option 1: Restrict RB region with no A-MPR
Option 2: Define A-MPR as a function of RB region and define offset frequency from low band edge for no A-MPR
Assumptions:
  Define RB region in terms of RB_start frequency and TX allocation BW (12*SCS*LCRB).
  For non-contiguous resource allocations, determine A-MPR as a function of TX allocation BW.
  Simulation and measurement assumptions:
    Choose the middle [9.5] dB filter rejection
    LO leakage = -28dBc
    Image = -28dBc
    Choose CIM3 = -60dBc
    Choose CIM5 = -65dBc
    For EN-DC, we measure with 2PA option

## Slide 5: References
R4-1816229, “n41 – B40 Coexistence”, Qualcomm, Inc., 3GPP RSG-RAN WG4 Meeting #89, Spokane, USA, Nov. 12-16, 2018.
R4-1816230, “Draft CR for n41 – B40 Coexistence”, Qualcomm, Inc., 3GPP RSG-RAN WG4 Meeting #89, Spokane, USA, Nov. 12-16, 2018.