## Slide 1: Way forward on the range of Qrxlevmin and Qqualmin
Ericsson
3GPP TSG-RAN WG4 Meeting # 89
Spokane, WA, USA, November 12-16, 2018
Agenda: 7.12.2
R4-1816717

## Slide 2: Background
The following parameters are used by the UE to verify whether the UE meets cell selection criterion S as described in section 5.2.3.2 of TS 38.304:
  Qrxlevmin: Minimum required RX level in the cell (dBm).
  Qqualmin: Minimum required quality level in the cell (dB).
The values of the above parameters are signaled by the network to the UE in RRC idle/inactive state.
RAN2 needs to specify the ranges of Qrxlevmin and Qqualmin, which are currently tentative (See Annex A).
In RRC connected state the SS-RSRP and SS-RSRQ ranges are defined:
  SS-RSRP: from -44 dBm down to -156 dBm
  SS-RSRQ: from 20 dB down to -43 dB

## Slide 3: Way Forward on Qrxlevmin and Qqualmin
Recommended ranges for Qrxlevmin:
  Qrxlevmin range should be similar to SS-RSRP.
  SS-RSRP and current LTE RSRP ranges are similar: between -44 dBm to -156 dBm.
    In LTE, RSRP below -140 dBm (down to -156 dBm) was introduced to support enhanced coverage.
  The recommended Qrxlevmin range is as follows:
    Minimum Qrxlevmin = -140 dBm
    Maximum Qrxlevmin = -44 dBm
Recommended ranges for Qqualmin:
  Compared to LTE RSRQ, the NR SS-RSRQ can be quite low due to different types of NR carrier RSSI measurement schemes for SS-RSRQ in NR (see Table 5.1.3-1 in TS 38.215).
    Therefore at least the lowest value of Qqualmin should be the same as the lowest reportable SS-RSRQ in RRC connected state.
    However the upper value of Qqualmin can be smaller than the largest SS-RSRQ in RRC connected state because Qqualmin is the minimum quality level.
  The recommended Qqualmin range is as follows:
    Minimum Qqualmin = -43 dB
    Maximum Qqualmin = -12 dB

## Slide 4: Annex A: Qqualmin and Qrxlevmin in Section 6.3.2 of TS 38.331
– Q-QualMin
The IE Q-QualMin is used to indicate for cell selection/ re-selection the required minimum received RSRQ level in the (NR) cell. Corresponds to parameter Qqualmin in TS 38.304 [4]. Actual value Qqualmin = field value [dB].
Q-QualMin information element
Q-QualMin ::= INTEGER (-34..-3) -- FFS range
– Q-RxLevMin
The IE Q-RxLevMin is used to indicate for cell selection/ re-selection the required minimum received RSRP level in the (NR) cell. Corresponds to parameter Qrxlevmin in TS 38.304 [4]. Actual value Qrxlevmin = field value * 2 [dBm].
Q-RxLevMin information element
Q-RxLevMin ::= INTEGER (-70..-22) -- FFS range