## Slide 1: 3GPP TSG-RAN WG4 Meeting #90 Athens, Greece, 25th February – 1st March 2019
Huawei, HiSilicon
Way forward on L1-RSRP test
R4-1901185

## Slide 2: Test case list for accuracy test
Test case number | Test purpose | Remark
1 | L1-RSRP measurement accuracy based on SSB in FR1 | Periodic report is used for verdict.
2 | L1-RSRP measurement accuracy based on SSB in FR2 | UE is assumed to use rough Rx beam. Periodic report is used for verdict.
3 | L1-RSRP measurement accuracy based on CSI-RS in FR1 | Periodic CSI-RS resource set with repetition off. Periodic report is used for verdict.
4 | L1-RSRP measurement accuracy based on CSI-RS in FR2 | Periodic CSI-RS resource set with repetition off; TCI is configured and referring to SSB. UE is assumed to use rough Rx beam. Periodic report is used for verdict.
5 | L1-RSRP measurement accuracy based on CSI-RS in FR2 | Aperiodic CSI-RS resource set with repetition on; TCI is configured and referring to SSB. UE is assumed to use fine Rx beam. Aperiodic report is used for verdict.
Note: Test cases should be defined separately for EN-DC and SA. |  | 

## Slide 3: Test case list for delay test
Test case number | Test purpose | Remark
1 | L1-RSRP measurement delay based on SSB in FR1 | One SSB is transmitted through the whole test time; Another SSB is transmitted only in T2. Periodic report after T2 is used for verdict.
2 | L1-RSRP measurement delay based on SSB in FR2 | One SSB is transmitted through the whole test time; Another SSB is transmitted only in T2. UE is assumed to use rough Rx beam. Periodic report after T2 is used for verdict.
3 | L1-RSRP measurement delay based on CSI-RS in FR1 | Aperiodic CSI-RS resource set with repetition off and TCI referring to SSB is transmitted in T2. Aperiodic report after T2 is used for verdict.
4 | L1-RSRP measurement accuracy based on CSI-RS in FR2 | Aperiodic CSI-RS resource set with repetition off and TCI referring to SSB is transmitted in T2. UE is assumed to use rough Rx beam. Aperiodic report after T2 is used for verdict.
Note: Test cases should be defined separately for EN-DC and SA. Note: Test cases should be defined separately for DRX and no-DRX. Note: Test cases should be defined without measurement gap configured. |  | 

## Slide 4: Rx antenna gain assumption
For test cases where UE is assumed to use fine Rx beam, the test requirements or setup should consider the uncertainty of the Rx beam gain
  Rx beam gain is assumed to be in the range of 7-17dB
For test cases where UE is assumed to use rough Rx beam, the test requirements or setup should further consider the uncertainty introduced by the gain difference between rough beam and fine beam
  Rx beam gain is assumed to be in the range of 0-17dB