## Slide 1: WF on SCell Activation in FR2
Qualcomm Inc
R4-1902082

## Slide 2: TCI States and Spatial Relations
Number of TCI States configure for PDCCH/PDSCH via RRC when SCell is added
  By what procedure will active state be selected as part of cell activation: RRC, MAC-CE/DCI
Number of spatialrelations configured for PUCCH/PUSCH via RRC when SCell is added
  By what procedure will active state be selected as part of cell activation : RRC, MAC-CE/DCI

## Slide 3: Activation Procedure
Consider the following options for the activation procedure for the first SCell in an FR2 band
  Option 1: activation of TCI states for PDCCH/PDSCH is part of SCell activation
    Case 1: SCell activation command comes before MAC-CE command for TCI state activation
    Case 2: SCell activation and TCI state activation are bundled in the same command
    Other possibilities are not precluded
    Study if RAN4 needs to define requirements for each of the cases or just in one case
    Time required for processing and application of each of these commands
    If TCI state activation happens after MAC-CE for Scell activation does the UE need to provide a L1-RSRP report before network can select active TCI state
  Option 2: activation of TCI states for PDCCH/PDSCH is not part of SCell activation
    UE assumes PDCCH/PDSCH is QCL-ed with a UE reported beam before receiving the activation command of PDCCH/PDSCH TCI states
    UE assumes CSI-RS for CQI is QCL-ed with a UE reported beam before receiving the configuration of TCI states for CSI-RS for CQI
    FFS if L3 measurement report before SCell activation can be used for the QCL assumption, or L1-RSRP measurement and report are needed during Scell activation process
  Other options are not precluded

## Slide 4: Potential Known Cell Definition
RAN4 to study if UE can do beam management on deactivated cell
  FFS if L3-RSRP reporting via RRC is sufficient for this purpose
  FFS if UE can report L1-RSRP via PUSCH on an already active carrier
    FFS if there is a restriction that beam management can only be done on active BWP or if some default BWP may be used