## Slide 1: WF on ACLR for intra-band non-contiguous ENDC
Skyworks Solutions Inc., ….
3GPP TSG-RAN WG4 Meeting 90
Athens, Greece,
25th February – 1st March 2019
R4-1902171

## Slide 2: Background
For Intra-band ENDC ACLR is valid in gap if gap BW is sufficient
At the time we discussed AMPR for DC-41_n41 specific AMPR for in gap ACLR was added
But this was based on equal back-off assumption
In our measurement campaign for DC_41_n41 [1, 2] and for DC_3_n3 in [4] where we exercised the whole PLTE and PNR range we found that some more cases would fail for the lower power carrier if the sum of the two carriers power is not used as reference

## Slide 3: Proposal for NC intra band ENDC
The individual ACLR is failed for the lower power carrier even though its own regrowth is OK
It was agreed by companies in [3] that this is not the desired behaviour
Can be further clarified 6.5B.2.2.3 Adjacent channel leakage ratio by using the sum of the carrier powers as the reference for ACLR
CR is brought in this meeting

## Slide 4: Observations and proposal for Contiguous intra-band ENDC
In [5] it was found that release 15 38.101-3 spec only has PC3 ACLR value (left table) and is corrected with PC3 and PC2 values (right table) for release 16
PC2 ACLR value in table Table 6.5B.2.1.3-1 needs to be added in release 15 with a CR in this meeting
Parameter | Unit | Value
EN-DCACLR (power class 3) | dBc | 30
EN-DCACLR (power class 2) | dBc | 31
Measurement bandwidth of EN-DC channel |  | 1.00*ENBW
Measurement bandwidth of adjacent channel |  | 0.95*ENBW
Frequency offset of adjacent channel |  | ENBW / -ENBW
NOTE 1: ENBW is the aggregated bandwidth in MHz as defined in sub-clause 5.3B. NOTE 2: The frequency offset is that in between the centre frequencies of the measurement filters |  | 
Table 2.3-1 ACLR for intra-band EN-DC
(contiguous sub-blocks)
Parameter | Unit | Value
EN-DCACLR | dBc | 30
Measurement bandwidth of EN-DC channel |  | 1.00*ENBW
Measurement bandwidth of adjacent channel |  | 0.95*ENBW
Frequency offset of adjacent channel |  | ENBW / -ENBW
NOTE 1: ENBW is the aggregated bandwidth in MHz as defined in sub-clause 5.3B. NOTE 2: The frequency offset is that in between the centre frequencies of the measurement filters |  | 
Table 6.5B.2.1.3-1: ACLR for intra-band EN-DC
(contiguous sub-blocks)

## Slide 5: References
[1] R4-1900897 Intra-band 41 ENDC AMPR verification, Skyworks Solutions Inc. , RAN4#90
[2] R4-1900919 Full Set of Intra-band 41 ENDC Measurement Results, Skyworks Solutions Inc. , RAN4#90
[3] R4-1902162 Minutes for intra-band EN-DC ad-hoc v1.doc, Qualcomm Inc., RAN4#90
[4] R4-1901357 preliminary MPR measurements for DC_3_n3, Skyworks Solutions Inc. , RAN4#90
[5] R4-1900532, Power class 2 UE for TDD-TDD EN-DC, MediaTek Inc.

## Slide 6: Background: LTE20+G20+NR60 example 1
Worst case both in gap and other side ACLR are failed
LTE
Adj
LTE
Wan
LTE
Adj
NR
Wan
NR
Adj
NR spectral regrowth
LTE spectral regrowth
31dBc
31dBc
31dBc
31dBc
LTE gap ACLR is failed although both NR and LTE regrowth are OK
LTE ACLR is failed although both NR and LTE regrowth are OK
11dB
~25dBc
~25dBc
60MHz
60MHz
60MHz
20MHz
20MHz
20MHz

## Slide 7: Background: LTE20+G20+NR60 example 2
Worst case both in gap and other side ACLR are failed
LTE
Adj
LTE
Wan
LTE
Adj
NR
Wan
NR
Adj
NR spectral regrowth
31dBc
31dBc
LTE gap ACLR is failed although both NR and LTE regrowth are OK
LTE ACLR is failed although both NR and LTE regrowth are OK
11dB
~25dBc
~25dBc
In this case LTE does not have any spectrum regrowth in ACLR region but would fail!
60MHz
60MHz
60MHz
20MHz
20MHz
20MHz

## Slide 8: Background: LTE20+G20+NR60 example 3
Worst case both in gap ACLR is failed even if NR ACLR has margin
LTE
Adj
LTE
Wan
LTE
Adj
NR
Wan
NR
Adj
NR spectral regrowth
>>31dBc
34dBc
LTE gap ACLR is failed although both NR and LTE regrowth are OK
11dB
~25dBc
60MHz
60MHz
60MHz
20MHz
20MHz
20MHz
In this case LTE does not have any spectrum regrowth in ACLR region but would fail!