## Slide 1: WF on UE RF spec scope in Rel-15
Qualcomm
3GPP RAN4 WG Meeting #90 R4-1902216 Athens, Greece, February 25 – March 1, 2019

## Slide 2: Background
Scope of this WF is to clarify the unclear items for the scope of Rel-15 specification
Release independent aspect for some features is clarified

## Slide 3: WF on release independence handling
Requirements for a feature can be written in Rel-16 specification but it can be supported by Rel-15 in release independent manner. This means a UE declaring itself as Rel-15 UE can support this feature by satisfying Rel-16 requirements for this feature
For a feature to be supported by an earlier release (Rel-15) in release independent manner, impact to other WG requirements need to be checked
If other WG requirements support the new feature from Rel-15, decision from which release is RAN4 internal
For every feature not written in to Rel-15 specifications, the company bringing the CR to introduce requirements to later release (Rel-16) for the feature shall check other WG specification support and clarify situation to RAN4 and propose from which release feature should be release independent from

## Slide 4: Scope of Rel-15 TS 38.101-1
Intra-band DL CA for bands < 3300 MHz
  Not supported
  Band n41 will be supported by Rel-15 specification [4]
Intra-band NC CA
  Not supported
Intra-band UL CA (contiguous and non-contigous)
  Not supported

## Slide 5: Scope of TS 38.101-2
UL continuous CA in conjunction with NC DL CA [1]
  Supported
UL non- continuous CA
  Not supported
NC RB Allocations within single CC
  Not supported
DL CA for cumulative aggregated bandwidth larger than 1400 MHz
  Not supported
  Maximum aggregated bandwidths for affected configurations will be changed in Rel-15 TS
Beam correspondence requirements and capability (2-20) for PC3
  Supported
  FFS for PC1/2/4

## Slide 6: Scope of TS 38.101-3
Intra-band contiguous EN-DC
  Supported configurations: DC_(n)71 and DC_(n)41
  FFS for General MPR (ongoing discussion in RAN4 #90) to be added to rel-15 TS
Intra-band non-contiguous EN-DC
  Supported configurations: DC_3_n3 (SUO only), DC_41_n41
  FFS for General MPR (ongoing discussion in RAN4 #90) to be added to rel-15 TS
Generic requirements, including switching time, for PA capability (dualpA-Architecture) for intra-band EN-DC single switch uplink operation (SUO) will be defined in Rel-15 TS [5]
  Generic requirements for PA capability (dualpA-Architecture) for intra-band EN-DC without SUO mode will not be defined in Rel-15 TS

## Slide 7: References
[1] R4-1900674, Draft CR to 38.101-2: UL config for DL NC CA, Qualcomm Incorporated
[2] R4-1901802, NR requirement work continuation in Rel-16, Nokia
[3] R4-1902256, Ad-hoc meeting mintues for beam correspondence, Samsung
[4] R4-1902194, [41 DL]Draft CR for 38.101-1 adding DL intra-band CA requirements for frequency less than 2700MHz, Huawei
[5] R4-1901609, Draft CR for TS 38.101-3: Switching time for intra-band EN-DC upon dual PA UE capability, Huawei