## Slide 1: WF on SDR requirement
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting RAN4#90 R4-1902402
Athens, Greece, February 25 – March 1, 2019

## Slide 2: Number of HARQ process
Previous agreements
  Option 1：If normal PDSCH demodulation requirement with 16 (TDD)/8 (FDD) HARQ processes targeting for higher Rank/MCS are introduced, the number of HARQ process for SDR test is 8 (TDD) / 4 (FDD)； Otherwise, 16 (TDD) / 8 (FDD) processes
  Option 2: 8 for TDD and 4 for FDD
Current options:
  Option 1: 4 for FDD and 8 TDD
  Option 2: 8 for FDD and 16 for TDD
  Option 3: [6] for FDD and [12] for TDD
Proposal:
  Option 3: 6 for FDD and 12 for TDD

## Slide 3: MCS level and table for FR1 1/2
Previous agreements
  Single upper bound applicable for all CHBW and SCS
Current options:
  Option 1: single upper bound (Intel, QC)
  Option 2: per CHBW /SCS combination (NTT DoCoMo)
Proposal:
  Option 1
    Upper bound MCS is summarized in the next slide
    FFS: practical MCS
  Modulation format 2 and 4 can be used only for CA case according to UE capability signaling, i.e. only modulation format 6 or 8 are used for single carrier case

## Slide 4: MCS level and table for FR1 2/2
UE capability index |  |  |  |  | 
1 | 1 | 8 | 1 | 26 | [26]
2 | 1 | 8 | 0.8 | 21 | 
3 | 1 | 8 | 0.75 | 20 | 
4 | 1 | 8 | 0.4 | 11 | 
5 | 1 | 6 | 1 | 27 | [27]
6 | 1 | 6 | 0.8 | 23 | 
7 | 1 | 6 | 0.75 | 22 | 
8 | 1 | 6 | 0.4 | 14 | 
9 | 1 | 4 | 1 | 16 | [16]
10 | 1 | 4 | 0.8 | 16 | 
11 | 1 | 4 | 0.75 | 16 | 
12 | 1 | 4 | 0.4 | 10 | 
13 | 1 | 2 | 1 | 9 | [9]
14 | 1 | 2 | 0.8 | 9 | 
15 | 1 | 2 | 0.75 | 9 | 
16 | 1 | 2 | 0.4 | 4 | 
17 | 2 | 8 | 1 | 26 | [26]
18 | 2 | 8 | 0.8 | 21 | 
19 | 2 | 8 | 0.75 | 20 | 
20 | 2 | 8 | 0.4 | 11 | 
21 | 2 | 6 | 1 | 27 | [27]
22 | 2 | 6 | 0.8 | 23 | 
23 | 2 | 6 | 0.75 | 22 | 
24 | 2 | 6 | 0.4 | 14 | 
25 | 2 | 4 | 1 | 16 | [16]
26 | 2 | 4 | 0.8 | 16 | 
27 | 2 | 4 | 0.75 | 16 | 
28 | 2 | 4 | 0.4 | 10 | 
29 | 2 | 2 | 1 | 9 | [9]
30 | 2 | 2 | 0.8 | 9 | 
31 | 2 | 2 | 0.75 | 9 | 
32 | 2 | 2 | 0.4 | 4 | 
UE capability index |  |  |  |  | 
33 | 4 | 8 | 1 | 27 | [26]
34 | 4 | 8 | 0.8 | 23 | 
35 | 4 | 8 | 0.75 | 22 | 
36 | 4 | 8 | 0.4 | 12 | 
37 | 4 | 6 | 1 | 28 | [27]
38 | 4 | 6 | 0.8 | 24 | 
39 | 4 | 6 | 0.75 | 23 | 
40 | 4 | 6 | 0.4 | 14 | 
41 | 4 | 4 | 1 | 16 | [16]
42 | 4 | 4 | 0.8 | 16 | 
43 | 4 | 4 | 0.75 | 16 | 
44 | 4 | 4 | 0.4 | 11 | 
45 | 4 | 2 | 1 | 9 | [9]
46 | 4 | 2 | 0.8 | 9 | 
47 | 4 | 2 | 0.75 | 9 | 
48 | 4 | 2 | 0.4 | 5 | 
Note: MCS level used in test is min( , )

## Slide 5: Methodology for FR2 SDR requirements 1/2
Previous agreements
  Adopt the following procedure for FR2 SDR test cases: (baseline)
    Use general procedure to select CA bandwidth for testing
    Derive for each CC based on UE capability by the previous slide (j is CC index)
    Identify testable SNR value for particular test configuration based on test equipment characteristics
    Use “SNR to MCS+Rank” table to find for each CC (Detail of “SNR to MCS+Rank” table is FFS)
    Conduct SDR test with for each CC
  Other options not excluded
Current options:
  Option 1: Keep the exiting procedure (Baseline)
  Option 2: New procedure proposed in R4-1900048 (Next slide)
Proposal:
  Further evaluation and comparison among these two options in next RAN4 meeting, if no difference for test channel bandwidth combinations among Op1 and Op2 ; then using option1

## Slide 6: Methodology for FR2 SDR requirements 2/2
New procedure proposed in R4-1900048
  Step 1: For all supported CA configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities:
    Use the table defining the MCS to determine the MCS (=MCS1) achieving the largest data rate [TS 38.306 [14, Section 4.1.2]] based on UE capabilities.
    Use the table defining the mapping between MCS and SNR required to achieve that MCS to determine the largest MCS (=MCS2) requiring SNR below test equipment maximum achievable SNR for each CC in that CA configuration.
    Compute the aggregate throughput for CA configuration using the MCS = min(MCS1,MCS2) for each CC in CA bandwidth combination.
  Step 2: Choose the CA bandwidth combination among all supported CA configurations that achieves maximum aggregate throughput in step 1 among all UE capabilities.
    Set of per CC UE capabilities includes channel bandwidth, subcarrier spacing, number of PDSCH MIMO layers, modulation format and scaling factor [TS 38.306 [14, Section 4.1.2]].
    When there are multiple sets of CA bandwidth combinations and UE capabilities (channel bandwidth, subcarrier spacing, number of MIMO layer, modulation format, scaling factor) with same aggregate throughput, select TBD
  Step 3: For each CC in chosen CA bandwidth combination, use determined MCS for each CC in step 1 for that CA configuration based on test parameters and indicated UE capabilities.
Notes: O

## Slide 7: MCS level and table for FR2
UE capability index |  |  |  | 
1 | 1 | 6 | 1 | 27
2 | 1 | 6 | 0.8 | 23
3 | 1 | 6 | 0.75 | 22
4 | 1 | 6 | 0.4 | 14
5 | 1 | 4 | 1 | 16
6 | 1 | 4 | 0.8 | 16
7 | 1 | 4 | 0.75 | 16
8 | 1 | 4 | 0.4 | 10
9 | 1 | 2 | 1 | 9
10 | 1 | 2 | 0.8 | 9
11 | 1 | 2 | 0.75 | 9
12 | 1 | 2 | 0.4 | 4
13 | 2 | 6 | 1 | 27
14 | 2 | 6 | 0.8 | 23
15 | 2 | 6 | 0.75 | 22
16 | 2 | 6 | 0.4 | 14
17 | 2 | 4 | 1 | 16
18 | 2 | 4 | 0.8 | 16
19 | 2 | 4 | 0.75 | 16
20 | 2 | 4 | 0.4 | 10
21 | 2 | 2 | 1 | 9
22 | 2 | 2 | 0.8 | 9
23 | 2 | 2 | 0.75 | 9
24 | 2 | 2 | 0.4 | 4
Proposal:
  The following MCS are agreed as upper bound MCS (or MCS1)
  Modulation format 2 and 4 can be used only for CA case according to UE capability signaling, i.e. only modulation format 6 is used for single carrier case

## Slide 8: Other issues on SDR test
Precoder matrix for FR2 Rank2 SDR test
  Only configure ½*[1, 1; 1, -1] for proper phase noise estimation
Maximum achievable SNR for FR2
  FFS
MCS range down-selection for evaluation for FR2:
  MCS 13 - 27
Whether we need to define RMC for SDR test
  RAN4 plans not to introduce RMC table in RAN4 specification and asking RAN5 feedback
  Send LS to RAN5 (drafted by intel)

## Slide 9: Methodology for EN-DC SDR test
Proposed methodology in R4-1900364
  Step 1: Select one EN-DC bandwidth combination among all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities that provides the largest data rate [TS 38.306 [14, Section 4.1.2]].
    Set of per NR CC UE capabilities includes channel bandwidth, subcarrier spacing, number of PDSCH MIMO layers, modulation format and scaling factor [TS 38.306 [14, Section 4.1.2]].
    Set of per EUTRA CC UE capabilities includes channel bandwidth, number of PDSCH MIMO layers and modulation format [TS 38.306 [14, Section 4.1.2]].
  Step 2: For each NR CC in EN-DC bandwidth combination, use MCSs from FR1 or FR2 SA SDR requirements depending on EN-DC scenario. For each EUTRA CC in EN-DC bandwidth combination, reuse LTE SDR FRCs [TS 36.101, Sections 8.7].
Proposal
  Further evaluated above methodology in next RAN4 meeting
  Other options not excluded

## Slide 10: (Information) Simulation assumption for RAN4 #90bis 1/5
Reuse the previous agreements at RAN4 #88bis [R4-1813929] with some updates (in red) as summarized below
Simulation cases for single carrier:
Companies are encouraged to provide simulation results with the following two MCS conditions
  The highest MCS based on UE capability without any restriction of testable SNR
  The highest MCS achieved within testable SNR range in Rel.15
Further detailed parameters are described in the next slides
Test case | FR | SCS | Duplex mode | CBW | MIMO config. | Max rank | Max modulation order
Case 1 | FR1 | 15kHz | FDD | 20MHz | 2x2MIMO | Rank 2 | 64QAM
Case 2 | FR1 | 15kHz | FDD | 20MHz | 2x2MIMO | Rank 2 | 256QAM
Case 3 | FR1 | 15kHz | FDD | 20MHz | 4x4MIMO | Rank 4 | 64QAM
Case 4 | FR1 | 15kHz | FDD | 20MHz | 4x4MIMO | Rank 4 | 256QAM
Case 5 | FR1 | 30kHz | TDD | 100MHz | 2x2MIMO | Rank 2 | 64QAM
Case 6 | FR1 | 30kHz | TDD | 100MHz | 2x2MIMO | Rank 2 | 256QAM
Case 7 | FR1 | 30kHz | TDD | 100MHz | 4x4MIMO | Rank 4 | 64QAM
Case 8 | FR1 | 30kHz | TDD | 100MHz | 4x4MIMO | Rank 4 | 256QAM
Case 9 | FR2 | 60kHz | TDD | 100MHz | 2x2MIMO | Rank2 | 64QAM
Case 10 | FR2 | 120kHz | TDD | 100MHz | 2x2MIMO | Rank2 | 64QAM

## Slide 11: (Information) Simulation assumption for RAN4 #90bis 2/5
Note:
For FR2 requirement, testable SNR is scaled down as (aggregated) channel bandwidth is scaled up
  Ex. If maximum testable SNR for 50MHz is XdB, that for 100MHz is (X – 3)dB
For FR2 SDR requirements, (aggregated) channel bandwidth for NR is up to 800MHz in Rel.15
In future release, testable SNR may be improved, and we need to inform to RAN5 what is testable MCS and rank limitation for SDR requirements
For forward compatibility, RAN4 will define MCS to SNR mapping table for all possible MCS and rank combinations.

## Slide 12: (Information) Simulation assumption for RAN4 #90bis 3/5
Parameter |  | Unit | Value
PDSCH transmission scheme |  |  | Transmission scheme 1
EPRE ratio of PTRS to PDSCH |  | dB | N/A
Channel bandwidth |  | MHz | See slide #11
Common serving cell parameters | Physical Cell ID |  | 0
 | SSB position in burst |  | First SSB in Slot #0
 | SSB periodicity | ms | 20
 | First DMRS position for Type A PDSCH mapping |  | 2
Active DL BWP index |  |  | 1
DL BWP configuration #1 | First PRB |  | 0
 | Number of contiguous PRB |  | Full allocation
 | Subcarrier spacing | kHz | See slide #11
 | Cyclic prefix |  | Normal
PDCCH configuration | Slots for PDCCH monitoring |  | Each slot
 | Symbols with PDCCH |  | Symbols #0
 | Number of PRBs in CORESET |  | [TBD]
 | Number of PDCCH candidates and aggregation levels |  | [TBD]
 | DCI format |  | [TBD]
PDSCH configuration | Mapping type |  | Type A
 | k0 |  | 0
 | PDSCH aggregation factor |  | 1
 | PRB bundling type |  | Static
 | PRB bundling size |  | Wideband for FR1 and FR2
 | Resource allocation type |  | Type 0
 | VRB-to-PRB mapping type |  | Non-interleaved
 | VRB-to-PRB mapping interleaver bundle size |  | N/A

## Slide 13: (Information) Simulation assumption for RAN4 #90bis 4/5
Parameter |  | Unit | Value
PDSCH DMRS configuration | DMRS Type |  | Type 1
 | Number of additional DMRS |  | 1
 | Length |  | 1
 | Antenna ports indexes |  | {1000} for 1 Layer CCs {1000, 1001} for 2 Layers CCs {1000 - 1003} for 4 Layers CCs
 | Number of PDSCH DMRS CDM group(s) without data |  | 1 for 1 layer and 2 layers CCs 2 for 4 Layers CCs
PTRS configuratioaan |  |  | For FR1: PTRS is not configured For FR2: 1 port, per 2PRB in frequency domain, per symbol in time domain
CSI-RS for tracking | First subcarrier index in the PRB used for CSI-RS (k0) |  | 3
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  | 6 for CSI-RS resource 1 and 3 10 for CSI-RS resource 2 and 4
 | Number of CSI-RS ports (X) |  | 1
 | CDM Type |  | No
 | Density (ρ) |  | 3
 | CSI-RS periodicity |  | 20ms
 | CSI-RS offset |  | 10ms from SSB
NZP CSI-RS for CSI acquisition | First subcarrier index in the PRB used for CSI-RS (k0) |  | 4
 | First OFDM symbol in the PRB used for CSI-RS (l0) |  | 13
 | Number of CSI-RS ports (X) |  | Same as Tx ports
 | CDM Type |  | FD-CDM2
 | Density (ρ) |  | 1
 | CSI-RS periodicity |  | 20ms
 | CSI-RS offset |  | 0ms from SSB
Maximum number of code block groups for ACK/NACK feedback |  |  | 1
Maximum number of HARQ transmission |  |  | 4
HARQ ACK/NACK bundling |  |  | Multiplexed
Redundancy version coding sequence |  |  | {0,2,3,1}
Precoding configuration |  |  | SP Type I, Random per slot with PRB bundling granularity
Symbols for all unused REs |  |  | OCNG Annex A.5
Propagation condition |  |  | Static propagation condition for FR1 and FR2

## Slide 14: (Information) Simulation assumption for RAN4 #90bis 5/5
Additional configuration for FDD
Additional configuration for TDD
Parameter |  | Unit | Value
Duplex mode |  |  | FDD
PDSCH configuration | Starting symbol (S) |  | 1
 | Length (L) |  | 13
Number of HARQ Processes |  |  | 4 for simulation purpose
Parameter |  | Unit | Value
Duplex mode |  |  | TDD
PDSCH configuration | Starting symbol (S) |  | 1
 | Length (L) |  | 13
Number of HARQ Processes |  |  | 8 for simulation purpose
TDD UL-DL pattern |  |  | FR1 15kHz: DDDSU FR1 30KHz: 7D1S2U FR2 60 kHz: DDSU FR2 120 kHz: DDDSU