## Slide 1: Way forward on NR UE PDSCH demodulation requirements and General aspects
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #90
Athens, Greece, 25 February – 1 March 2018 Agenda Item: 6.14.1.2
R4-1902403

## Slide 2: Rel-15 work scope
No new UE demodulation or CSI requirement, which was not discussed in the previous meetings, should be introduced in Rel-15.
  The proposal for new requirement, which was under discussion but no decision was made in the previous meetings, can be discussed further.
For Rel-15 late drop (NR-NR DC and NE DC) will be further discussed after June 2019 with target timeline of Dec 2019.

## Slide 3: Requirements Applicability
Issue 1: Requirements for SA and NSA
  Proposal: All minimum performance requirements defined in Sections 5-8 are applicable to both SA and NSA unless otherwise explicitly stated in Section 9 and 10.
Issue 2: Requirements for different UE power classes
  Proposal: All minimum performance requirements defined in Sections 5-10 are applicable to all UE power classes unless otherwise stated.
Issue 3: Requirements applicable rules for FR2 Bands
  Proposal: Specify FR2 frequency band applicability rules in the TS 38.101-4
Issue 4: Test applicability in FR2 considering TE achievable SNR limitation
  Further clarify in TS 38.101-4 that for FR2 requirements “In case the required SNR is larger than the SNR upper bound that can be emulated by test system, the corresponding requirement can currently not be tested.”
  Proposal
    Option 1: SNR upper bound is derived by TE vendors for each particular setup and test case -> TE declare
    Option 2: SNR upper bound is specified by RAN4 in TR 38.810

## Slide 4: TDD requirements
      Issue 1: TDD UL/DL configuration {DDDSUU}+{DDDD} for FR1 requirements
  Proposal:
    Option 1: No introduce test case(s) for TDD DL/UL configuration: {DDDSUU}+{DDDD} under 30kHz in Rel-15
    Option 2: Introduce one additional test case for {DDDSUU}+{DDDD} for PDSCH demodulation

## Slide 5: PDSCH requirements
Issue 1: Additional test with 8 HARQ process for FDD and 16 HARQ process for TDD
  Previous agreement
    FFS whether to introduce additional requirement with 70% test point with 8 HARQ process for FDD and 16 HARQ process for TDD
      Option 1: No Test since soft buffer test has been defined (Intel, QC)
      Option 2: Introduce PDSCH demodulation tests with 70% test point with 8 HARQ processes for FDD and 16 HARQ processes for TDD
  Current options:
    Option 1: Do not define PDSCH test cases with 8 (FDD) / 16 (TDD) HARQ processes except 30% TP test cases.
    Option 2: Apply 8/16 HARQ processes for SDR requirements for FDD/TDD.
    Option 3: Introduce PDSCH demodulation tests with 70% test point with 8 HARQ processes for FDD and 16 HARQ processes for TDD
    Option 4: Apply [6]/[12] HARQ processes for SDR requirements for FDD/TDD.
  Proposal:

## Slide 6: PDSCH requirements
      Issue 2: TRS configuration for FR2
  Previous agreement
    Option 1: Do not change TRS configuration
    Option 2: 20ms with 1 slot duration and OFDM symbol indexes 5, 9
    Option 3: 40ms with 1 slot duration
    Other options are not precluded
    TRS configuration change can be applicable for one of test cases. Exact test cases is FFS.
    FFS whether to introduce configuration for normal demodulation or SDR test cases
  Proposal:
    Option 1: No change: Use 2 slots TRS configuration for Rel-15 Normal and SDR requirements (Intel, QC)
    Option 2: Replace FR2 Test 1-1 with TRS configuration: 20ms with 1 slot and OFDM symbol 6, 10 (NTT DoCoMo)
      Option 2a: 2 additional DMRS
      Option 2b: 1 additional DMRS
    Bring evaluation results for option 2 and decide among above two options in next meeting

## Slide 7: PDSCH requirements
      Issue 3: Dynamic TDD DL-UL configuration test
  Previous agreement:
    Option 1: Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s).
    Option 2: Do not define test
    Further make downselection in RAN4 #90
  Current options:
    Option 1: Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s)-both FR1 and FR2
    Option 2: Use dynamic UL/DL determination for some existing PDSCH demodulation test case(s)- FR2 only
    Option 3: Define the RAN4 performance requirements definition for dynamic TDD UL/DL configuration in Rel-16 CLI WI.
  Proposal: TBD

## Slide 8: PDSCH requirements
      Issue 4: Common parameters for PDSCH (Normal and SDR) and CSI test cases
  PDCCH parameters:
    Number of PDCCH candidates = 1
    PDCCH aggregation level = [8]
      FFS for SDR tests with following SCS/CBW combinations: 15/5, 30/5, 30/10, 30/15
        Option 1: AL4 for 15/5, 30/10, 30/15, AL1 for 30/5
        Other options are not precluded
    PDCCH DCI format 1-1
  Other
    K1 for FDD test cases = 2
    HARQ ACK/NACK Bundling = Multiplexed
    Slots for PDCCH monitoring (FR2) = each slot

## Slide 9: PDSCH requirements
      Issue 5: TCI configuration
  Previous agreement
    Only one TCI state configured for NR UE performance test cases in Rel-15( [QCL behavior Type A and TypeD (FR2 only)])
    Detailed parameters FFS
  Proposal
      UE reuses TCI information from PDCCH DM-RS (RRC + MAC CE) for PDSCH demodulation.
    Note: Current proposal contains information about general procedure for TCI configuration. Detailed parameters will be captured in corresponding Draft CRs.
TCI parameters |  | TCI state for TRS | TCI state for PDCCH DMRS | TCI state for NZP CSI-RS for CSI acquisition | TCI state for NZP CSI-RS for BM (FR2 only)
QCL info Type 1 | Reference signal | SSB index | Index of NZP CSI RS resource from TRS |  | 
 | QCL type | Type C | Type A |  | 
QCL info Type 2 (FR2 only) | Reference signal | SSB index | Index of NZP CSI RS resource from TRS |  | 
 | QCL type | Type D | Type D |  | 

## Slide 10: PDSCH requirements
      Issue 6: HARQ timing (K1 value)
 | FR1, 15 kHz, DDDSU | FR1, 30 kHz, 7D1S2U | FR1, 30 kHz, DDDSU | FR1, 30 kHz, DDDSUDDSUU
K1 value | 4 if mod(i,5) = 0 3 if mod(i,5) = 1 2 if mod(i,5) = 2 6 if mod(i,5) = 3 | 8 if mod(i,10)= 0 7 if mod(i,10)= 1 6 if mod(i,10)= 2 5 if mod(i,10)= 3 5 if mod(i,10)= 4 4 if mod(i,10)= 5 3 if mod(i,10)= 6 2 if mod(i,10)= 7 | 4 if mod(i,5) = 0 3 if mod(i,5) = 1 2 if mod(i,5) = 2 6 if mod(i,5) = 3 | 4 if mod(i,10)= 0 3 if mod(i,10)= 1 2 if mod(i,10)= 2 5 if mod(i,10)= 3 3 if mod(i,10)= 5 3 if mod(i,10)= 6 2 if mod(i,10)= 7
 | FR1, 30 kHz, SU | FR1, 30 kHz, DDSU | FR1, 30 kHz, DS1S2U | 
K1 value | 3 if mod(i,2) = 0 | 3 if mod(i,4) =0 2 if mod(i,4) =1 5 if mod(i,4) =3 | 3 if mod(i,4) =0 2 if mod(i,4) =1 3 if mod(i,4) =3 | 
 | FR2, 60kHz, DDSU | FR2, 120kHz, DDDSU | FR2, 120kHz, DDSU | FR2, 120kHz, DSUU
K1 value | 3 if mod(i,4) = 0 2 if mod(i,4) = 1 5 if mod(i,4) = 3 | 4 if mod(i,5) = 0 3 if mod(i,5) = 1 2 if mod(i,5) = 2 6 if mod(i,5) = 3 | 3 if mod(i,4) = 0 2 if mod(i,4) = 1 5 if mod(i,4) = 3 | 3 if mod(i,4) = 0 5 if mod(i,4) = 1

## Slide 11: PDSCH requirements
      Issue 7: HST requirements
        Channel model: Single tap channel model with the following parameters
        Simulation assumptions:
    Channel bandwidth and SCS:
      FDD: 10 MHz, SCS 15 kHz
      TDD: 40 MHz, SCS 30 kHz (7D1S2U, S = 6D:4S:4U)
    PDSCH mapping: Type A, Start symbol 2, Duration 12
    DMRS configuration:
      Option 1: Type 1, Single symbol, 1 additional DMRS
      Option 2: Type 1, Single symbol, 2 additional DMRS
    TRS configuration:
      Option 1: 10ms, 2 slots, offset 1
      Option 2: 20ms, 2 slots, offset 10
    FRC:
      Option 1: QPSK Rank 1 (MCS 4)
      Option 2: 16QAM Rank 1 (MCS 13)
    Baseline receiver assumption for frequency offset tracking (for initial simulation purpose only)
      Option1: TRS based on tracking
      Option2: SSB+TRS based on tracking (SSB with 20ms periodicity)
Parameter | Option 1 | Option 2
Ds | 300 m | 300 m
Dmin | 2 m | 2 m
v | 350 km/h | 300 km/h
fd | 875 Hz for 15 kHz SCS test and 1167 Hz for 30 kHz SCS test | 750 Hz for 15 kHz SCS and 30 kHz SCS tests

## Slide 12: Simulation alignment
PDSCH requirements for existing test cases will be finalized in RAN4 90bis meeting
  Requirements can be updated only in case technical issues are observed