## Slide 1: Way forward on NR PDCCH demodulation requirements
Ericsson
3GPP TSG-RAN WG4 Meeting #90
Athens, Greece, 25 February – 1 March, 2019
R4-1902406

## Slide 2: Test case 14/15 for AL16
Agreement:
  Introducing FR1 15kHz test with 4Rx AL16 (test 14)- TDL-A ULA Medium A
  MIMO correlation for FR1 30kHz test with 4Rx AL 16 (15b)
    TDL-A, ULA Medium A
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | CORESET-interleaver-size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
14 | 15 | 1_0 | 48 | 39 | 2 | 16 | Non-interleaved | 6 | NA | [TDL-A, 30ns, 10Hz] | 1x2 Low | 1x4 Medium A
15b | 30 | 1_0 | 48 | 41 | 2 | 16 | Non-interleaved | 6 | NA | [TDL-A, 30ns, 10Hz] as optional only for 4Rx | NA | 1x4 Medium A

## Slide 3: Test cases with 4Rx with interleaved CCE-to-REG mapping
Agreement:
  using bundle size =2 (test 6a,7a adopted)
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | CORESET-interleaver-size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
6a | 30 | 1_0 | 102 | 41 | 1 | 2 | Interleaved | 2 | 3 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
7a | 30 | 1_1 | 102 | 52 | 1 | 4 | Interleaved | 2 | 3 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low

## Slide 4: Test case overview (1/2)
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | CORESET-interleaver-size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
1 | 15 | 1_0 | 24 | 39 | 2 | 2 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
2 | 15 | 1_0 | 24 | 39 | 2 | 4 | Non-interleaved | 6 | NA | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
3 | 15 | 1_1 | 24 | 52 | 2 | 2 | Non-interleaved | 6 | NA | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
4 | 15 | 1_1 | 48 | 52 | 2 | 4 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
5 | 15 | 1_1 | 48 | 52 | 2 | 8 | Non-interleaved | 6 | NA | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
6a | 30 | 1_0 | 102 | 41 | 1 | 2 | Interleaved | 2 | 3 | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
7a | 30 | 1_1 | 102 | 53 | 1 | 4 | Interleaved | 2 | 3 | TDL-C, 300ns, 100Hz | 1x2 Low | 1x4 Low
8 | 30 | 1_1 | 90 | 53 | 1 | 8 | Interleaved | 6 | 3 | TDL-C, 300ns, 100Hz | 2x2 Low | 2x4 Low
9 | 120 | 1_0 | 60 | 40 | 1 | 2 | Interleaved | 2 | 3 | TDL-A, 30ns, 75Hz | 1x2 Low | NA
10 | 120 | 1_1 | 60 | 56 | 1 | 4 | Interleaved | 6 | 2 | TDL-A, 30ns, 300Hz | 1x2 Low | NA
11 | 120 | 1_1 | 60 | 56 | 1 | 8 | Interleaved | 2 | 3 | TDL-A, 30ns, 75Hz | 2x2 Low | NA

## Slide 5: Test case overview (2/2)
Test No. | SCS(KHz) | Format | CORESET RB | Payload | CORESET time duration | AL | CCE-to-REG Mapping | REG bundle size | CORESET-interleaver-size | Propagation condition | Antenna configuration with 2Rx | Antenna configuration with 4Rx
12 | 15 | 1_0 | 48 | 39 | 1 | 4 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Low
13 | 15 | 1_1 | 48 | 52 | 1 | 8 for 2Rx and 4 for 4Rx | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 2x2 Low | 2x4 Low
14 | 15 | 1_0 | 48 | 39 | 2 | 16 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | 1x2 Low | 1x4 Medium A
15 | 30 | 1_0 | 48 | 41 | 2 | 16 | Non-interleaved | 6 | NA | TDL-C, 300ns, 100Hz | 1x2 Low | NA
15b | 30 | 1_0 | 48 | 41 | 2 | 16 | Non-interleaved | 6 | NA | TDL-A, 30ns, 10Hz | NA | 1x4 Medium A
16 | 120 | 1_0 | 60 | 40 | 2 | 16 | Interleaved | 2 | 3 | TDL-A, 30ns, 75Hz | 2x2 Low | NA

## Slide 6: Way forward
RAN4 will finalize the Rel-15 PDCCH demodulation requirements for test cases listed in pages 4 and 5 in RAN4#90bis
  Requirements will not be updated after RAN4#90bis unless the technical issues remain.
For the alignment, companies are encouraged to check the noise covariance estimation granularity is same or less than the bundling size.

## Slide 7: SNR requirements derivation
Plan for deriving performance requirements (SNR points)
  Define tentative SNR requirements for the agreed test cases as much as possible
  Update TPs including SNR requirements for test cases with []
  The agreed SNR values still can be updated if more results collected from companies in future meeting or technical issues identified
SNR = average of IM results among companies +extra margin [0.5dB]
For test cases where the span among companies’ results is within [2.5dB], capture the SNR requirement with [] as above in the TP
For test cases with larger span than [2.5dB], further check the details of simulation assumption and further discuss extra margin on a case by case basis, leave TBD for the SNR requirement in the TP

## Slide 8: Summary of impairment results (1/2)
Description | Ericsson | QC | Intel | Samsung | Huawei | CATT | CMCC | MTK | STD | SPAN | AVE | Common margin | AVE+margin(0.5dB)
Test 1 2Rx | 6.5 | 8.6 | 7.5 |  | 7.4 | 7.1 |  | 7.8 | 0.7 | 2.1 | 7.5 | 0.5 | 8.0
Test 1 4Rx | 0.5 | 2.6 | 2.5 |  | 2.5 | 0.6 |  | 2.1 | 1.0 | 2.1 | 1.8 | 0.5 | 2.3
Test 2 2Rx | 1.5 | 1.6 | 0.7 |  | -0.5 | 2.1 |  | 1.4 | 0.9 | 2.6 | 1.1 | 0.5 | TBD
Test 2 4Rx | -2.2 | -1.9 | -2.5 |  | -4.5 | -2.5 |  | -2.9 | 0.9 | 2.6 | -2.7 | 0.5 | TBD
Test 3 2Rx | 6.6 | 9.1 | 7.4 |  | 6.8 | 7.2 |  | 8.4 | 1.0 | 2.5 | 7.6 | 0.5 | 8.1
Test 3 4Rx | 1.2 | 2.8 | 2.7 |  | 1.2 | 1.7 |  | 2.4 | 0.7 | 1.6 | 2.0 | 0.5 | 2.5
Test 4 2Rx | 3.7 | 5.9 | 5.2 |  | 5.0 | 4.3 |  | 5.8 | 0.9 | 2.2 | 5.0 | 0.5 | 5.5
Test 4 4Rx | -1.7 | 0.6 | 0.4 |  | -1.2 | -1.3 |  | 0.0 | 1.0 | 2.3 | -0.5 | 0.5 | 0.0
Test 5 2Rx | -2.0 | -0.8 | -2.5 |  | -3.6 | -1.4 |  | -1.8 | 1.0 | 2.8 | -2.0 | 0.5 | -1.5
Test 5 4Rx | -5.2 | -4.3 | -5.1 |  | -6.8 | -5.0 |  | -5.5 | 0.8 | 2.5 | -5.3 | 0.5 | -4.8
Test 6 2Rx | 6.8 | 6.8 | 6.8 |  | 5.7 | 5.7 | 6.0 | 5.7 | 0.6 | 1.2 | 6.2 | 0.5 | 6.7
Test 6 4Rx A | 3.9 | 2.8 | 1.9 |  | 0.9 | 1.1 | 1.2 | 1.4 | 1.1 | 3.0 | 1.9 | 0.5 | TBD

## Slide 9: Summary of impairment results (2/2)
Description | Ericsson | QC | Intel | Samsung | Huawei | CATT | CMCC | MTK | STD | SPAN | AVE | Common margin | AVE+margin(0.5dB)
Test 7 2Rx | 2.8 | 3.6 | 3.1 |  | 1.2 | 1.3 | 0.8 | 2.6 | 1.1 | 2.8 | 2.2 | 0.5 | 2.7
Test 7 4Rx A | 0.5 | 0.7 | -0.9 |  | -2.5 | -2.5 | -3.1 | -1.3 | 1.5 | 3.8 | -1.3 | 0.5 | TBD
Test 8 2Rx | -2.5 | -0.1 | -2.2 |  | -3.3 | -1.5 | -2.9 | -1.7 | 1.1 | 3.3 | -2.0 | 0.5 | -1.5
Test 8 4Rx | -5.7 | -3.4 | -4.2 |  | -6.6 | -4.7 | -6.2 | -4.8 | 1.1 | 3.2 | -5.1 | 0.5 | -4.6
Test 9 | 5.6 | 6.6 | 5.7 |  | 4.1 |  |  | 5.6 | 0.9 | 2.5 | 5.5 | 0.5 | 6.0
Test 10 | 1.2 | 3.8 | 1.7 |  | 1.0 |  |  | 2.6 | 1.2 | 2.8 | 2.1 | 0.5 | 2.6
Test 11 | -1.4 | 0.9 | -0.4 |  | -2.3 |  |  | -1.2 | 1.2 | 3.2 | -0.9 | 0.5 | -0.4
Test 12 2Rx | 3.3 | 3.7 | 3.9 |  | 3.4 | 3.8 | 4.3 | 4.4 | 0.4 | 1.1 | 3.8 | 0.5 | 4.3
Test 12 4Rx | -1.5 | 0.0 | -0.1 |  | -2.4 | -1.8 | -1.8 | -0.6 | 0.9 | 2.4 | -1.2 | 0.5 | -0.7
Test 13 2Rx AL 8 | -1.3 | -0.5 | -0.8 |  | -2.1 | 0.2 | -0.7 | -0.7 | 0.7 | 2.3 | -0.8 | 0.5 | -0.3
Test 13 4Rx AL 4 | -2.5 | -0.8 | -0.7 |  | -3.7 | -2.0 | -2.0 | -1.7 | 1.0 | 3.0 | -1.9 | 0.5 | TBD
Test 14 2Rx | -3.6 | -1.5 | -2.4 |  | -2.2 | -3.4 | -3.3 | -1.8 | 0.8 | 2.1 | -2.6 | 0.5 | -2.1
Test 14 4Rx | -4.7 | -3.6 | -3.0 |  | -7.2 | -4.3 | -6.5 | -3.1 | 1.6 | 4.2 | -4.6 | 0.5 | TBD
Test 15 2Rx | -6.0 | -3.1 | -5.2 |  | -5.6 | -3.9 | -6.6 | -4.2 | 1.2 | 3.5 | -4.9 | 0.5 | -4.4
Test 15 4Rx B | -5.8 | -3.0 | -3.3 |  | -5.0 |  | -6.2 | -4.6 | 1.3 | 3.2 | -4.6 | 0.5 | -4.1
Test 16 | -4.6 | -2.5 | -3.6 |  | -5.2 |  |  | -3.6 | 1.0 | 2.7 | -3.9 | 0.5 | -3.4