## Slide 1: 3GPP TSG-RAN WG4 Meeting #90 Athens, Greece, Feb.25 – Mar.01 2019
Huawei, …
Way forward on General part of NR BS demodulation performance
R4-1902438

## Slide 2: Background
The following WFs were approved:
  R4-1808022 Way forward on general part for NR BS demodulation requirements, RAN4#87
  R4-1809370 Way forward on general parameters for BS demodulation performance requirements, RAN4#AH1807
  R4-1811726 Way forward on general part of NR BS demodulation performance, RAN4#88
  R4-1813755 Way forward on NR BS demodulation general part, RAN4#88Bis
  R4-1816346 Way forward on NR BS demodulation general part, RAN4#89

## Slide 3: Rel-15 Work Scope
No new BS demodulation requirement, which was not discussed in the previous meetings, should be introduced in Rel-15.
Whether to introduce the NR BS demodulation requirements for HST scenario will be discussed in RAN4#90.

## Slide 4: Test Applicability - 1
Test applicability will be defined in TS 38.141-1/2 only.
Different PRACH formats with requirements defined, i.e. short sequence format A1, A2, A3, B4, C0 and C2 and long sequence format 0:
  BS is tested on all preamble formats declared to support, but just choose the smallest supported PRACH SCS per FR for each supported PRACH format(s) with short sequence if BS support multiple SCS per FR.
Test applicability for CA
  For a BS supporting UL carrier aggregation, only the CC combination with the largest aggregated bandwidth per SCS is used for test.
    Not mixed SCS CA combination to be tested for within a frequency range
    Verify the performance per CC basis
In case the required SNR is larger than the SNR upper bound that can be emulated by test system, the corresponding requirement can currently not be tested.

## Slide 5: Phase Noise
In the ideal simulation for FR2, no explicit phase noise model is required.
Company consider the phase noise impact in their submitted impairment results.