## Slide 1: WF on performance requirements of UCI Multiplexing on PUSCH
R4-1902439
Document for: Approval
3GPP TSG-RAN WG4 RAN#90
Athena, GR, 25th Feb– 1th March, 2019
Agenda: 6.14.2.2.1
Samsung, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis
  R4-1816347, WF on NR PUSCH demodulation requirements, RAN4#89

## Slide 3: Background
The WF (R4-1813942) on UCI multiplexing on PUSCH is approved:
  Specify the test cases for UCI decoding performance over PUSCH in Rel-15 by next June
  Test parameters to be discussed after Nov meeting

## Slide 4: UCI Test Scope
Specify the requirement of UCI multiplexing over on PUSCH with UL data in Rel-15
UCI payload type
  UCI only contains CSI part1 and part2

## Slide 5: Test setup
MCS: 16
Waveform: CP-OFDM
SCS/BW:
  FR1: 10MHz/30kHz; FR2: 50MHz/120kHz
Antenna configuration: 1T2R
Time domain allocation
  FR1: type A and Type B with slot-based. The requirements for type A and type B is only applicable according to the BS declaration
  FR2 type B with non slot-based
DMRS configuration
  FR1: DMRS 1+1 (2,11) for type A, DMRS (0,10) for type B
  FR2: DMRS 1+0

## Slide 6: Test setup
PTRS Configuration
  FR1: no PTRS configured
  FR2: configured K_PTRS with 2, L_PTRS with 1
Propagation condition
  FR1: TDLC300-100
  FR2: TDLA30-300
Others
  No PUCCH partition, i.e. no frequency hopping

## Slide 7: Test setup
Test metric:
  Option1: 1%BLER of UCI with CSI
  Option2: 0.1% BLER of UCI with CSI part1, 1% BLER of UCI with CSI part2
  Other options is not precluded.
  Company is encouraged to provide results for both option 1 and option 2 including BLER curve in next meeting, decision will be made based on the submitted results.

## Slide 8: UCI parameters
Number of payload:
  7 bits(part1=5bits, part2=2bits)
  One more payload size need to be added
    Option 1: [40] bits (part1 = 20 bits, part2 = 20 bits)
    Other options are not precluded
Notes: Samsung: 40bits is for CA 4 CCs case, 7 bits for single CC,
ZTE: Cross CC feedback is not mandated to support, each CC is independent
Nokia: 7 bits without CRC, test equipment vendors need to take into account: the payload need to be feedback errorless over the side channel.
Keysight: Making dependency with TE capability on this topic seems not good idea because TE vender can’t attend BS demod session all the time.

## Slide 9: UCI parameters
Test parameters:
  BetaOffsetCSI-part1 and BetaOffsetCSI-part2
    6.25
  Alpha (scaling factor)
    1

## Slide 10: Initial Simulation Assumptions, UCI over PUSCH
Parameter |  | Value | 
 |  | FR1 | FR2
General System | Transform precoding | Disabled | Disabled
 | Number of Tx | 1 | 1
 | Number of Rx | 2 | 2
 | Number of layers | 1 | 1
 | [Uplink-downlink allocation for TDD] | 30 kHz SCS: 7D1S2U, S=6D:4G:4U | 120kHz SCS: 3D1S1U, S=10D:2G:2U
 | Code block group based PUSCH transmission | Disabled | Disabled
 | MCS index | 16 | 16
 | Propagation Condition | MCS 16: TDL-C 300ns, 100 Hz | MCS 16: TDL-A 30ns, 300Hz
HARQ | he number of HARQ transmission | 1 | 1
DMRS | DMRS configuration type | 1 | 1
 | Maximum number of OFDM symbols for front loaded DMRS | 1 | 1
 | Number of additional DMRS symbols | 1 | 0
 | Number of DMRS CDM group(s) without data | 2 | 2
 | EPRE ratio of PUSCH to DMRS | -3 dB | -3 dB
 | DMRS port | 0 | 0
 | DMRS sequence generation | NID=0, nSCID =0 | NID=0, nSCID =0
Time domain resource | PUSCH mapping type | A, B | B
 | PUSCH starting symbol index | 0 | 0
 | PUSCH symbol length | 14 | 14
Frequency domain resource | Carrier frequency (GHz) | 4 | 30
 | SCS and BW | 30kHz: 10 MHz | 120kHz: 50 MHz
 | RB assignment | Full applicable test bandwidth | Full applicable test bandwidth
 | Frequency hopping | Disabled | Disabled
PTRS configuration | Frequency density (KPT-RS) | no PTRS | 2
 | Time density (LPT-RS) | no PTRS | 1
UCI | UL-SCH | With | With
 | Payload (bits) | Case 1: [csi part1= 5, csi_part2 =2] Case 2 [csi_part1=[20],csi_part2=[20]] | Case 1: [csi_part1 = 5 ,csi_part2 = 2] Case 2: [csi_part1=[20], csi_part2=[20]]
 | uci-on-pusch-scaling | 1 | 1
 | I^CSI-1 and I^CSI-2 | [6.25] for CSI | [6.25] for CSI
Test metric |  | [SNR@ 1% BLER] [0.1% BLER of UCI with CSI part1, 1% BLER of UCI with CSI part2 ] | [SNR@ 1% BLER] [0.1% BLER of UCI with CSI part1, 1% BLER of UCI with CSI part2 ]