## Slide 1: 3GPP TSG-RAN WG4 Meeting #90 Athens, Greece, Feb.25 – Mar.01 2019
Huawei, …
Way forward on NR PUCCH demodulation performance in Rel-15
R4-1902440

## Slide 2: Background
R4-1808025 Way forward on PUCCH demodulation requirements, RAN4#87
R4-1809556 Way forward for NR PUCCH demodulation performance requirements, RAN4#1807
R4-1811727 Way forward for NR PUCCH demodulation performance requirements, RAN4#88
R4-1813943 Way forward on NR PUCCH demodulation requirements, RAN4#88Bis
R4-1816348 Way forward on NR PUCCH demodulation requirements, RAN4#89

## Slide 3: PUCCH format 3 and 4
For FR2 PUCCH format 3 and 4 requirements with additional DMRS, it is agreed to introduce the requirements, but need to down prioritize it. down prioritization means the requirements for additional DMRS can be introduced in Release 15 WI (completed by June, 2019) or in TEI-15 by December,2019
If BS supports both with and without additional DMRS configuration, select the PUCCH format 3 and 4 requirements for one of with and without additional DMRS configuration for test, otherwise BS vendor tests the PUCCH format 3 and 4 requirements for the declared with or without additional DMRS configuration supporting.

## Slide 4: Time Mask for PUCCH
Background
  Further investigation is need to check the performance impact due to the time mask under the frequency hopping enabled.
  Whether frequency hopping is needed considering the time mask impact to the PUCCH performances.
Agreement
  With the frequency hopping configuration which has been chosen for the demodulation simulation, no additional impairment for the impact of transient period need to be introduced: there is no power change and so no transient period is needed in between symbols.

## Slide 5: Simulations
New simulation cases for FR2 PUCCH format 3 and format 4 with additional DMRS configured as red highlighted in next slide.

## Slide 6: Initial Simulation Assumptions
Parameters |  | PUCCH Format 0 | PUCCH Format 1 | PUCCH Format 2 | PUCCH Format 3 | PUCCH Format 4 | 
BandWidth/SCS |  | FR1: 10MHz/15kHz; 40MHz/30kHz; FR2: 100MHz/60kHz; 100MHz/120kHz |  |  |  |  | 
Antenna |  | 1T2R, 1T4R and 1T8R for FR1; 1T2R for FR2 |  |  |  |  | 
Propagation condition |  | FR1: : TDLC300-100; FR2: TDLA30-300 |  |  |  |  | 
Carrier frequency (GHz) |  | FR1: 4GHz; FR2: 30GHz |  |  |  |  | 
(#Bits, #Symbols, #PRBs) |  | (1, 1, 1) (1, 2, 1) | (2, 14,1) | (4, 1, 4) (22, 2, 9) | (16, 14, 1) (16, 4, 3) |  | (22, 14, 1)
DMRS pattern |  |  |  |  | FR1 and FR2: Without additional DMRS for all cases With additional DMRS for cases with the number of OFDM symbols more than 9 |  | 
Modulaiton |  |  |  | QPSK | QPSK |  | QPSK
initialCyclicShift |  | 0 | 0 |  |  |  | 
StartingSymbolIndex |  | 13 for 1 symbol; 12 for 2 symbols; | 0 | 13 for 1 symbol; 12 for 2 symbols; | 0 |  | 0
Index of orthogonal sequence (time-domain-OCC) |  |  | 0 |  |  |  | 
occ-Length |  |  |  |  |  |  | n2
occ-Index |  |  |  |  |  |  | n0
Test metric | DTX to Ack probability <1% | √ | √ | √ for bits <=11 | × |  | ×
 | Missed Ack probability < 1% | √ | √ | √ | × |  | ×
 | NACK2ACK < 0.1% | × | √ | × | × |  | ×
 | BLER < 1% | × | × | √ for bits >11 | √ |  | √