## Slide 1: WF on simulation assumptions for BC tolerance requirements
LG Electronics
3GPP TSG-RAN WG4 #90 Meeting
Athens, Greece, 25th Feb. – 01st March, 2019
Agenda Item: 6.7.8.3.2
Document for : Approval
R4-1902684

## Slide 2: Background
RAN Plenary agreed to specify BC tolerance requirements for UE feature 2-20 set to 0 [1]
RAN4 agreed to decide [x]-tile % and [Y] dB based on delta EIRP CDF curve
  Candidate [x]-tile % is one of set in [80%, 85%, 90%, 95%, 100%]. In addition, companies can also check other point, e.g., 60%
Agreements in AH meeting [2]
  Test point is top 50% EIRP2 points for PC3 UE
  Option3 in Test procedure [2] is baseline
  Basic principle : Test procedure and test point will be decided as package to reduce the OTA test time [3]
  The same polarization combining option will be used for both EIRP1 and EIRP2[2]
    Option 3: EIRP CDF is derived based on data vector [maximum (V-V + V-H, H-V+H-H)] cross all testing points

## Slide 3: WF on General UE RF parameters
Basic RF parameters: reuse the simulation assumptions for Peak/Spherical EIRP requirements
UE RF parameters | Unit | Value | Notes
Frequency band |  | n257/n258/n260/n261 | Antenna performance can be different
Measurement Grid | degree | 7.5 or 15 | Peak EIRP is 7.5 Spherical EIRP is 15
# of element antenna in an antenna module/set (# of panels, # of analog beam(K), etc.) |  | 4 (2 panels, # total beam: 8,16,32) | Consider switched 2 panels. These parameters will be depend on UE implementation. Other values are not precluded
Polarization |  | 2 polarization | 
Antenna location (front, back, top-side, left-side, right-side, bottom-side) |  | Left/right | combination of the lists are not precluded.
Phase Error per Antenna element(δpk ) Amplitude Error per Antenna element(δak ) | Degree/ dB | δpk ~ N(0, 2) with =[0~30] δak ~ N(0, 2) with = [0~2]dB | Other distributions are not precluded
Error in RSRP estimation(Dk ) | dB | Dk ~ N(0, [2]2) | 
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | This information is meaningful only if it’s the same with the material which covers antennas.
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | 
Display panel – Full (Y) or Partial (N) | Y/N | Y | 
Bezel Margin | mm | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability

## Slide 4: WF on measurement method for delta EIRP
Simulation Set-up : Option1 (per antenna elements)
  Set Ideal AWT(Analog Beam Weight Table) for K beams ( depend on UE implementations)
    AWT = [W1 W2 W3 … WK];
  For each P UEs ( P is number of UE to be simulated)
    Generate Tx/Rx AWT considering Phase/Amplitude error
      Tx AWT = [WT1 WT2 WT3 … WTK], K is one of [8,16,32]
        WTk = Wk * δak *exp(iδpk) where δak, δpk represent amplitude/phase error vector of each element for given k Beam and * means point-wise multiplication
      Rx AWT = [WR1 WR2 WR3 … WRK] = [W1 W2 W3 … WK]
    For Given Measure point(Q) within EIRP measurement grid
      Iterate until get statistically meaningful measurement values
        Decide UE Autonomous DL(Rx) Beam selection (EIRP1)
          Beam Index(k) = index of max(RSRP1+D1, RSRP2+D2, RSRP3+D3, … , RSRPK+DK) = index of max(A(Q, WR1)+D1, A(Q, WR2)+D2, A(Q, WR3)+D3, …, A(Q, WRK)+DK)
          EIRP1 = A(Q, WTk)
        Decide UE EIRP2:
          Size of SRS AWT is restricted by SRS-resource of M.
          SRS AWT = [WSRS_T1 WSRS_T2 WSRS_T3 … WSRS_TM] is subset of Tx AWT. How to select the subset is up to UE implementation.
          EIRP2 = max(A(Q, WSRS_T1), …, G(Q, WSRS_TM)) (Beam sweeping and Select best)
          Delta_EIRP = EIRP2 – EIRP1
  If all measurement grid points are run, get CDF of delta_EIRP
  Company should guarantee EIRP2 can fulfil Req.1 and Req.2
DK= measurement error of RSRPK
A(Q, Wk) = Composite Antenna Pattern in TS38.803 for given Q direction with Wk beam vector)

## Slide 5: WF on General UE RF parameters
Basic RF parameters: reuse the simulation assumptions for Peak/Spherical EIRP requirements
UE RF parameters | Unit | Value | Notes
Frequency band |  | n257/n258/n260/n261 | Antenna performance can be different
Measurement Grid | degree | 7.5 or 15 | Peak EIRP is 7.5 Spherical EIRP is 15
# of element antenna in an antenna module/set (# of panels, # of analog beam(K), etc.) |  | 4 (2 panels, # total beam: 8,16,32) | Consider switched 2 panels. These parameters will be depend on UE implementation. Other values are not precluded
Polarization |  | 2 polarization | 
Antenna location (front, back, top-side, left-side, right-side, bottom-side) |  | Left/right | combination of the lists are not precluded.
Phase Error per Beam (δpk ) Amplitude Error per Beam (δak ) | Degree/ dB | δpk ~ N(0, 2) with =[10~45] δak ~ N(0, 2) with = [1~3]dB | Other distributions are not precluded
Error in RSRP estimation(Dk ) | dB | Dk ~ N(0, [2]2) | 
Front cover (Plastic, Glass, Ceramic, Metal) |  | Glass | This information is meaningful only if it’s the same with the material which covers antennas.
Back cover (Plastic, Glass, Ceramic, Metal) |  | Glass | 
Side cover / Frame (Plastic, Glass, Ceramic, Metal) |  | Metal | 
Display panel – Full (Y) or Partial (N) | Y/N | Y | 
Bezel Margin | mm | 1.5 | Module can’t be placed outer edge of UE to secure mechanical reliability

## Slide 6: WF on measurement method for delta EIRP
Simulation Set-up : Option2 (per beam)
  Set Ideal AWT(Analog Beam Weight Table) for K beams ( depend on UE implementations)
    AWT = [W1 W2 W3 … WK];
  For each P UEs ( P is number of UE to be simulated)
    Generate Tx/Rx AWT considering Phase/Amplitude error
      Tx AWT with error = [WT1 WT2 WT3 … WTK]
      Rx AWT = [W1 W2 W3 … WK] = [WR1 WR2 WR3 … WRK]
      Relationship between Tx/Rx AWT : A(Q, WTk)=A(Q+ δpk, WRk) + δak . where δak, δpk represent amplitude/phase error per Beam for given k Beam
    For Given Measure point(Q) within EIRP measurement grid
      Iterate until get statistically meaningful measurement values
        Decide UE Autonomous DL(Rx) Beam selection (EIRP1)
          Beam Index(k) = index of max(RSRP1+D1, RSRP2+D2, RSRP3+D3, … , RSRPK+DK) = index of max(A(Q, WR1)+D1, A(Q, WR2)+D2, A(Q, WR3)+D3, …, A(Q, WRK)+DK)
          EIRP1 = A(Q, WTk)
        Decide UE EIRP2:
          Size of SRS AWT is restricted by SRS-resource of M.
          SRS AWT = [WSRS_T1 WSRS_T2 WSRS_T3 … WSRS_TM] is subset of Tx AWT. How to select the subset is up to UE implementation.
          EIRP2 = max(A(Q, WSRS_T1), …, A(Q, WSRS_TM)) (Beam sweeping and Select best)
          Delta_EIRP = EIRP2 – EIRP1
  If all measurement grid points are run, get CDF of delta_EIRP
  Company should guarantee EIRP2 can fulfil Req.1 and Req.2
DK= measurement error of RSRPK
A(Q, Wk) = Composite Antenna Pattern in TS38.803 for given Q direction with Wk beam vector)

## Slide 7: WF on SRS parameters
RAN1 common understanding for UL beam sweeping operation
  If UE does not configure the spatialRelationInfo from NW, then the UE can consider the UL beam sweeping.
  If UE has configure the spatialRelationInfo from NW, then the UE consider autonomous beam selection
    spatialRelationInfo contain the ID of a reference ‘ssb-Index’ or ‘csi-Rs-Index’ for SRS resource
Upper limitation of SRS-Resource
  To reduce the test time, the upper number of SRS-Resource (M) is [4] or [8] or [16] from TE
  <UplinkBeamManagement in TS38.331 v15.4.0>

## Slide 8: Reference
[1] RP-182879, “WF on Beam Correspondence,” Samsung
[2] R4-19002256, “Ad-Hoc Meeting Minutes for Beam Correspondence,” Samsung
[3] R4-1900xxxx, “Draft chairman meeting report for RAN4 #90,”
[4] R4-1900134, "on beam correspondence requirements," Intel Corporation
[5] R4-1900251, "Beam correspondence for tolerance based requirement with UE beam sweeping ," LG Electronics France
[6] R4-1900672, "FR2 Beam Correspondence, On Alternative Definition," Qualcomm Incorporated
[7] R4-1901278, "Beam Correspondence," Nokia, Nokia Shanghai Bell
[8] R4-1901315, "Beam Correspondence, remaining X and Y," Sony, Ericsson
[9] R4-1900431, “Verification of beam correspondence during initial access,” Ericsson, Sony
[10] R4-1900278, “On uplink beam sweeping based EIRP test procedure,” Ericsson, Sony
[11] R1-1900133, “On beam correspondence test procedure,” Intel Corporation
[12] R4-1900715, "Initial discussion on test procedure for beam correspondence in FR2," LG Electronics