## Slide 1: Wayforward for PC2 FDD-TDD HPUE CHTTL, China Unicom, SGS Wireless, Xiaomi
3GPP TSG-RAN WG4 Meeting #90 R4-1902452 Athens, Greece, 25th Feb – 1nd March, 2019

## Slide 2: Backgrounds
The scope of PC2 FDD-TDD including the following two cases:
  Note: for case 1 and case 2, the duty cycles of NR TDD can be different.
  RAN4 study starts from case 1, but case 2 is not precluded.
  Example band combination for this study is DC_3_n78
Some initial aspects and solutions are discussed during RAN4#90 [1]~[7]
 | EN-DC total power | LTE maximum power | NR maximum power
Case 1 | 26dBm | 23dBm | 23dBm
Case 2 | 26dBm | 23dBm | 26dBm

## Slide 3: Wayforward for PC2 FDD-TDD HPUE
For the PC2 FDD-TDD HPUE
  Consider re-using MaxUplinkDutyCycle mechanism with weighting function between LTE and NR to constrain the overall weighted Tx duty cycle
    The PC2 FDD-TDD HPUE will fallback to PC3 if the network configuration exceed the MaxUplinkDutyCycle
  How to apply the uplink duty cycle capability can be further studied
Further study the following solutions to meet the overall uplink duty cycle for the PC2 FDD-TDD HPUE, starting from case 1
  Option 1: Reduce Tx time for LTE FDD UL
    Restrict LTE FDD UL transmission by TDM patterns can be considered as the starting point for option 1
  Option 2: Reduce Tx power for LTE FDD UL
  Other options are not precluded
  Companies are encouraged to check if option 1 and option 2 are applicable in the SAR requirement
Study the Rx desense requirements for DC_3_n78, starting from case 1
  The power combinations for Rx desense requirements are agreed as follows
Rx Self-desensitization Caused by | Power Combination | UL Power Configurations (dBm) | 
 |  | LTE | NR
1 UL | Case 1 | 23 | 23
 | Case 2 | 23 | 26
2UL IMD | Case 1 | 23 | 23
 | Case 2 | 23 | 23

## Slide 4: Reference
  [1] R4-1900256 Discussion on FDD+TDD HPUE OPPO
  [2] R4-1900534 Power class 2 UE for FDD-TDD EN-DC MediaTek Inc.
  [3] R4-1901028 Discussion on PC2 EN-DC UE(1 LTE FDD band and 1 NR band) for Rel-16 vivo
  [4] R4-1901242 Discussion for EN-DC High Power UE with one LTE FDD band and 1 NR TDD band CHTTL
  [5] R4-1901321 Discussion on HPUE for inter-band EN-DC OPPO
  [6] R4-1901799 Applicable scheme to avoid regulatory limits Huawei Technologies Co., Ltd
  [7] R4-1901882 Considerations for PC2 FDD-TDD EN-DC Qualcomm Incorporated