## Slide 1: 3GPP TSG-RAN WG4 Meeting #90 Athens, Greece, 25th February – 1st March 2019
Ericsson, MediaTek, Nokia
Way forward on L1 RSRP accuracy
R4-1902565

## Slide 2: Agreement
For measurement accuracy,
  The accuracy is defined based on the single sample.

## Slide 3: Summary of SSB based L1 RSRP measurement results with single sample
Company | Absolute accuracy levels for measurement BW of SSB
Huawei | ± 5
Intel | ± 5.5
Nokia | ± 4.5
Company | Relative accuracy levels for measurement BW of SSB
Huawei | ± 3
Intel | ± 3.5

## Slide 4: Summary of CSI-RS based L1 RSRP measurement results with single sample
Company | Absolute accuracy levels for measurement BW of 24 PRBs [dB]
Huawei | ± 6
CMCC | ± 6
Intel | ± 5.5
Company | Relative accuracy levels for measurement BW of 24 PRBs [dB]
Huawei | ± 3
CMCC | ± 3
Intel | ± 3.5

## Slide 5: Way forward for L1-RSRP measurement accuacy requirements
RAN4 is to decide the minimum BW used for deriving the CSI-RS based L1-RSRP measurement accuacy based on the simulation results.
Interested companies are encouraged to provide L1-RSRP accuracy simulation results based on the simulation assumptions in this WF.

## Slide 6: Simulation assumptions for CSI-RS based L1-RSRP measurement accuracy
Parameters | Value
SCS | 15 kHz, 30 kHz, 120 kHz
Side condition (SNR) | -3 dB
Density (D) | 3
Number of samples (M) | 1 (single sample measurement)
Number of PRB | 24, 48, 96
Propagation condition | AWGN

## Slide 7: Simulation assumptions for SSB based L1-RSRP measurement accuracy
Parameters | Value
SCS | 15 kHz, 30 kHz, 120 kHz
Side condition (SNR) | -3 dB
Number of samples (M) | 1 (single sample measurement)
Propagation condition | AWGN