## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’an, China, 8th – 12th April 2019
Huawei, HiSilicon
Way forward on RRM impact of the R16 enhancement for NB-IoT
R4-1903674

## Slide 2: Group WUS
RAN4 is to discuss thoroughly at least the following topics,
  Identify impact on R15 WUS performance from R16 WUS;
  Define minimum WUS reception requirements for R16 group WUS,
    Use R15 requirements as baseline;
  Introduce serving cell measurement relaxation requirements according to R16 group WUS
    Use R15 requirements as baseline.
Regarding requirements for R16 group WUS,
  For minimum reception requirements, it is dependent on the sequence and multiplexing design;
  For serving cell relaxation requirements, reuse R15 requirements.

## Slide 3: Preconfigured UL resource
RAN4 does not define the threshold for TA change or DL/UL timing change. It is expected that network will configure proper NRSRP threshold based on UE’s original TA.
The requirements for TA acquisition at least through RACH or EDT procedures follow the ones defined for random access.

## Slide 4: Multi carrier operation
Legacy requirements defined for R14 msg3 based quality reporting apply for msg3 based quality reporting on non-anchor carriers including,
  Hypothetical NPDCCH and
  T1 and T2 and
  Report mapping and
  Reporting accuracy.
Define non-anchor carrier serving cell RRM requirements based on NRS measurement on the non-anchor carrier in TS 36.133.
RSRP/Q offset to compensate the NRS based non-anchor carrier measurements should considered.