## Slide 1: WF on NR MIMO OTA
CAICT
3GPP TSG-RAN WG4 Meeting #90bis R4-1904160
Xi’an, China, April 8th – April 12th, 2019
Agenda item: 10.2.1
Document for: Approval

## Slide 2: General part
20cm shall be set as the minimum test zone size for NR MIMO OTA test methods, both FR1 and FR2. Another test zone size larger than 20cm can be further discussed. UE vendors are encouraged to provide the input on the test zone size in the future.
Adopt Black-box approach for NR MIMO OTA testing, the physical center of the UE shall be placed in the center of test zone, the EUT shall be completely contained within the test zone size defined by respective operating band
Number of probes and placement of probes for MPAC system for FR1 and FR2 have to be standardized in the MIMO OTA SI.

## Slide 3: Channel model scaling(1)
General principle for scaling the channel models
  Rotate AoDs/ZoDs and scale to CDL-A and CDL-C using the methods in 38.901 (section 7.7.5.1) to make them fit the median values in 38.901 Table 7.5-6 for the accepted scenarios
Detailed steps on how to scale the channel models
  Adopt the procedure in contribution R4-1904197 as the baseline for channel model scaling, and provide the final channel model table next meeting.
  The values in the contribution R4-1904197 are tentatively agreed as baseline for simulation.
How to handle the mid-paths with exactly same angular parameters
  A simple dithering approach is needed, the values of angles of these clusters must be dithered by [x] degree
    This angle should be decided before next RAN4 meeting in the NR MIMO OTA reflector

## Slide 4: Channel model scaling(2)
For FR1 channel model scaling purpose, 3.5GHz is used as reference frequency as we agreed in previous RAN4 meeting.
The baseline emulated propagation environment for FR1 MIMO OTA is 2D without elevation modeling.
For FR1, how to scale the channel model to 2D:
  Set all ZoAs in the channel model to be 90o, ZoDs should retain 3D characteristics after scaling;
  The ZSA of the channel model should be set as 0o;
Companies to share the resulting channel model table in the NR MIMO OTA reflector before next RAN4 meeting. Suggested order is CDL-A with UMi and CDL-C with UMa for FR1.
Companies are encouraged to provide the analysis on the comparison between 2D and 3D channel model for further enhancement of MIMO OTA testing for FR1.

## Slide 5: Channel model parameters
  UE speed:
    FR1: 30km/h;
    FR2: 3 km/h for Indoor Office and 12 km/h for UMi
  FR2 UE Antenna Pattern for channel model generation
    Isotropic
  UE direction of travel
    For FR1, use [120]o
    For FR2, the UE direction of travel must be such that it moves in the direction of the strongest cluster with an Y degree offset, where Y is TBD, e.g. 1 deg
      Fixing the initial phases of the subpaths is not precluded

## Slide 6: Verification of the Channel Models
  For FR1 MIMO OTA channel model, same verification parameters with LTE (Power Delay Profile (PDP), Doppler/Temporal correlation, Spatial correlation, Cross-polarization, Power validation) is utilized to guarantee the channel model implementation.
  Using the correlation matrix for channel model verification is TBD
  KPI of FR2 channel model
    The same channel model parameters as FR1, e.g. PDP, Doppler, Cross-polarization, power validation and PAS similarity percentage (PSP) shall be adopted for FR2.
      The antenna assumptions for the PSP metric calculation from the reference and OTA PAS are TBD
  The procedure to validate these above parameters for FR1 and FR2 is TBD
  For system design and implementation purpose, TE vendors shall check the impact due to the increasing frequency up to 7.125GHz for FR1.

## Slide 7: Criteria of test zone size
  Criteria of defining the test zone size
    FR1: spatial correlation curve with [x%] RMS error, within the agreed 20cm test zone size (i.e. within a 10cm radius from the center) on each frequency band
      For FR1, the spatial correlation error is 2D
      A weighted RMS correlation error approach is not precluded [R4-1706668]
    For FR2, the metric is PSP in 3D
  Introducing other test zone size other than 20cm is not precluded in the future if issues were identified.

## Slide 8: NEXT actions
Make decision on Channel model tables next RAN4 meeting.
Estimation of number of probes with system layout based on the provided channel model table is encouraged.
Next meeting, it is desired to bound the RMS spatial correlation error range