## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’an, China, 8th – 12th April, 2019
Ericsson
Way forward on Rel-16 MTC RRM enhancement
R4-1904577

## Slide 2: Channel quality report in Msg3
RAN4 waits for further RAN1/RAN2 agreements on DL channel quality report work.

## Slide 3: Group WUS
RAN4 shall wait for further RAN1 progress on release 16 WUS design work to decide whether release 15 WUS requirements are reusable.
  Based on current design, it likely possible to apply Rel-15 legacy WUS requirements on Rel-16 group WUS.

## Slide 4: MPDCCH improvement on RLM
It is likely possible to achive significant MPDCCH BLER performance gain by using DMRS and CRS for MPDCCH demodulation.
RAN4 shall evaluate the MPDCCH BLER performance based on RAN1 agreement on precoder options which is currently under discussion.

## Slide 5: Preconfigured UL resource
RAN4 shall define requirements for following options to validate TA:
  Serving cell change
  Time alignment timer (TAT)
  serving cell RSRP change
PUR transmissions/resources should be not allowed during the time (T0) UE is out of synchronization in IDLE mode (e.g. between PTWs).
  Value of T0 is FFS
PUR transmissions are allowed only when maximum serving cell change is less than RSRP and received TA is less than TAmax.
  Values of RSRP and TAmax are FFS

## Slide 6: Mobility enhancement
RAN4 prioritizes the work on defining the measurement requirements for RSS based RSRP measurements for IDLE mode.
Based on the RSS based RSRP measurement performance gain, RSS is used for improving the CE level selection when multiple CE levels are configured.
For serving cell measurement relaxation, the existing NB-IoT serving cell measurement relaxation requirements (as defined in 4.6.2.1A and 4.6.2.3A in TS 36.133) are reused.