## Slide 1: WF on performance requirements of UCI Multiplexing on PUSCH
R4-1904716
Document for: Approval
3GPP TSG-RAN WG4 RAN#90b
Xi’an, China, 8th– 12th April, 2019
Agenda: 6.12.2.2.1
Samsung, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis
  R4-1816347, WF on NR PUSCH demodulation requirements, RAN4#89
  R4-1902439, WF on Performance requirement of UCI Multiplexing on PUSCH, RAN4#90

## Slide 3: Test setup
HARQ
  Number of HARQ process ：1
  RV =0

## Slide 4: UCI parameters
Number of payload:
  7 bits(CSI part1=5bits, CSI part2=2bits)
  40 bits(CSI part1= 20bit, CSI part2 =20bits)
Payload content:
  7 bits:
    [0 1 0 1 0] for CSI part1
      Other options are not precluded
    [1 0] for CSI part2
      Other options are not precluded
  40 bits: Select random payload content for CSI part1 and part2 in the (20,20) configuration
Notes: Nokia: content [0, 0]for CSI part 2 fine.
Nokia/Ericsson is fine to [1,0] for CSI part 2

## Slide 5: Test setup
Test metric:
  one metric for CSI-1 and one for CSI -2 separately
      Target SNR : 0.1% BLER for CSI-1, 1% BLER for CSI-2
Notes: Nokia: offline discuss with ZTE, it is statistic same, just
Ericsson: from test point of view, op 4 is better.
ZTE: Which one is more convenient for test need more time to think
Samsung: separate two CSI part. The decoding is different for two parts.
Ericsson: anyway need to check the whole UCI.

## Slide 6: Test Metric definition for option 3
BLER for CSI part1 is defined as
  probability of incorrectly decoding the information CSI part1 when the CSI part1 information is sent
  -#(false CSI part1) denotes the number transmission of not detect CSI part1
  -#(CSI part1) denotes the number of CSI part1 transmission
BLER for CSI part2 is defined as
  probability of incorrectly decoding the information CSI part2 when CSI part1 and CSI part2 information are sent
  -#(false CSI part2) denotes the number transmission of not detect CSI part2
  -#(CSI part2) denotes the number of CSI part2 transmission

## Slide 7: UCI parameters
Test parameters:
  BetaOffset_HARQ_ACK_Index
    11 (20)
  BetaOffsetCSI-part1_Index and BetaOffsetCSI-part2_index
    13 (6.25)
  Alpha (scaling factor)
    1
Notes: The name defined in TS 38.331.

## Slide 8: Initial Simulation Assumptions, UCI over PUSCH
Parameter |  | Value | 
 |  | FR1 | FR2
General System | Transform precoding | Disabled | Disabled
 | Number of Tx | 1 | 1
 | Number of Rx | 2 | 2
 | Number of layers | 1 | 1
 | [Uplink-downlink allocation for TDD] | 30 kHz SCS: 7D1S2U, S=6D:4G:4U | 120kHz SCS: 3D1S1U, S=10D:2G:2U
 | Code block group based PUSCH transmission | Disabled | Disabled
 | MCS index | 16 | 16
 | Propagation Condition | MCS 16: TDL-C 300ns, 100 Hz | MCS 16: TDL-A 30ns, 300Hz
HARQ | Maximum number of HARQ transmission | 1 | 1
 | RV | 0 | 0
DMRS | DMRS configuration type | 1 | 1
 | Maximum number of OFDM symbols for front loaded DMRS | 1 | 1
 | Number of additional DMRS symbols | 1 | 0
 | Number of DMRS CDM group(s) without data | 2 | 2
 | EPRE ratio of PUSCH to DMRS | -3 dB | -3 dB
 | DMRS port | 0 | 0
 | DMRS sequence generation | NID=0, nSCID =0 | NID=0, nSCID =0
Time domain resource | PUSCH mapping type | A, B | B
 | PUSCH starting symbol index | 0 | 0
 | PUSCH symbol length | 14 | 10
Frequency domain resource | Carrier frequency (GHz) | 4 | 30
 | SCS and BW | 30kHz: 10 MHz | 120kHz: 50 MHz
 | RB assignment | Full applicable test bandwidth | Full applicable test bandwidth
 | Frequency hopping | Disabled | Disabled
PTRS configuration | Frequency density (KPT-RS) | no PTRS | 2
 | Time density (LPT-RS) | no PTRS | 1
UCI | UL-SCH | With | With
 | Payload (bits) | Case 1: csi_part1= 5, csi_part2 =2 Case 2 : csi_part1=20,csi_part2=20 | Case 1: csi_part1 = 5 ,csi_part2 = 2 Case 2: csi_part1=20, csi_part2=20
 | uci-on-pusch-scaling | 1 | 1
 | I^HARQ_ACK | 11 | 11
 | I^CSI-1 and I^CSI-2 | 13 for CSI part1 and part2 | 13 for CSI part1 and part2
Test metric |  | 0.1% BLER of UCI with CSI part1, 1% BLER of UCI with CSI part2 | 0.1% BLER of UCI with CSI part1, 1% BLER of UCI with CSI part2