## Slide 1: Way forward on UE demodulation enhancement for HST
Qualcomm Inc, ...
3GPP TSG-RAN WG4 Meeting #90-Bis Xi’an, China, 8 – 12 April, 2019
R4-1904792
Document for: Approval

## Slide 2: WF on extension of demod requirements to CA
Specify HST-SFN CA requirements based on Rel.14 train speed (350km/h)
  Ericsson, Qualcomm, NTT DOCOMO, CMCC
Not Define HST-SFN CA requirements
  Intel, MTK

## Slide 3: WF on HST-SF scenario
Option 1: HST-SFN bi-directional scenario (Huawei, CMCC, Intel, NTT DOCOMO, Qualcomm, MTK)
  The following maximum Doppler shifts supported for downlink will be further evaluated considering the uplink and downlink channels together to decide a pair of maximum Doppler shift for downlink and uplink
    Agreement: companies can bring results for the following two options of maximum Doppler with MCS sweep from 12 to 16:
      Option 1: 1100Hz
      Option 2: 972Hz
Option 2: HST-SFN uni-directional scenario (Ericsson, Qualcomm)
  Maximum Doppler shift for downlink for uni-directional
    Option 1: 1250Hz (Qualcomm)
    Other options with lower values compared to above not precluded
FFS: whether both bi- and uni-directional scenario are specified or not.

## Slide 4: WF on Additional Test to be Introduced
Option 1(NTT DOCOMO): add tests for HST single tap and multi-path with 500km/h speed, only applicable to UEs without enhanced HST-SFN capability
Option 2(Qualcomm): add test for only HST single tap with 500km/h speed, only applicable to UEs without enhanced HST-SFN capability
Option 3(Intel, MTK): do not specify additional tests

## Slide 5: WF on Transmission Mode
Transmission mode for test to be added:
  TM3
    Qualcomm, Intel, MTK, Ericsson, NTT DOCOMO,CMCC
  DMRS-based TM in addition to TM3
    Huawei
      Interested companies to further discuss the potential benefits, impacts and solutions for DMRS-based transmission

## Slide 6: WF on Priority of Test Scenarios
Priority 1: TM3 under bi-directional channel with cap on Doppler shift (Qualcomm, NTT DOCOMO, CMCC, Intel, MTK)
Priority of the following scenarios to be discussed in RAN4#91 meeting. Interested companies to bring supporting documents to justify priority.
  TM3 under uni-directional channel (Ericsson, Qualcomm)
  TM9 under bi-directional channel (Huawei)

## Slide 7: WF on Simulation Assumptions
Simulation assumptions for Priority 1 scenario (previous slide) to be finalized in RAN4#91 meeting
  Interested companies to propose simulation assumptions for
    Maximum Doppler shift
    MCS
    Bi-directional channel parameters
    Other parameters not precluded