## Slide 1: Way forward on R16 NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #90bis
Xi’an, China, 8 – 12 Apr, 2019
R4-1904827
Document for: Approval

## Slide 2: Agreements on DC-based handover
DC-based handover involving cells with different SCS is feasible, depending on UE capability of supporting different SCS.
  Note: extra UE complexity can be expected even for the UE which can support multiple SCS in serving cell.
DC-based handover in FR2 is not feasible and will be further studied in this work item.

## Slide 3: Agreements on RACH-less handover
RAN4 confirms the feasibility of RACH-less handover in FR1 with zero TA or same TA between source and target cells
  For both intra and inter-frequency scenarios
  For both synchronous and asynchronous deployment
  With same or different SCS in source and target cells
Feasibility of RACH-less in FR2 is FFS.
Interested companies are encouraged to provide analysis on RACH-less handover with different TA