## Slide 1: WF on known cell condition for PSCell FR2
R4-1904845
Document for: Approval
3GPP TSG-RAN WG4 RAN#90bis
Xi’an, China, 8th – 12th Apr, 2019
Agenda: 6.10.7.3.1
Nokia, Nokia Shanghai Bell

## Slide 2: Background
For PScell addition, PSCell in FR1 is known if it has been meeting the following conditions:
  During the last 5 seconds before the reception of the NR PSCell configuration command:
    the UE has sent a valid measurement report for the NR PSCell being configured and
    One of the SSBs measured from the NR PSCell being configured remains detectable according to the cell identification conditions specified in section 9.3 of TS 38.133 [50],
  One of the SSBs measured from NR PSCell being configured also remains detectable during the NR PSCell configuration delay according to the cell identification conditions specified in section 9.3 of TS 38.133 [50].

## Slide 3: PSCell Addition Procedure
To enable addition of a PSCell:
  Network configures UE to measure inter-frequency measurements
  UE report inter-frequency measurements (candidate PSCell).
  Networks configure UE to add PSCell.
  UE access PSCell via PRACH
When a PSCell is added 3 different cases exist:
  target PSCell and Tx beam both remain the same
  target PSCell remains the same, but Tx beam has changed
  target PSCell has changed

## Slide 4: PSCell Scenarios
PSCell and Tx beam is unchanged:
PSCell is unchanged and Tx beam is changed:
PSCell is changed:

## Slide 5: Way Forward
Define:
  Known PSCell (scenario 1 – fully known)
  Unknown PSCell (scenario 3 – fully unknown)
PSCell is known if:
  If during the period equal to [X ms]:
    the UE has sent a valid measurement report for the cell, and
    measurement report includes Index
    the cell remains detectable according to the cell identification conditions
  The SSB measured during the period equal to [Y ms] also remains detectable during the PSCell addition delay according to the cell identification conditions specified in section 9.2 and 9.3.
An added PSCell can be regarded as unknown if the added PSCell is not known
  When a candidate PSCell is unknown cell, additional UE measurements are expected.

## Slide 6: Way Forward
Define requirements for partially known PSCell:
  Tx beam has changed
  Rx beam has changed
For scenario 2:
  PSCell is unchanged but Tx beam (Index) has changed:
    This would add an additional delay assuming UE would need at least 1 SSB reception in PSCell Index detection.
For scenario 1&2:
  PSCell is unchanged but UE Rx beam has changed:
    Allow a sweep on UE side decide which Rx beam to use assuming PSCell is unchanged.

## Slide 7: Way Forward
PSCell Delay in FR2 is defined similar as for FR1:
  From when PSCell is added
  Untill UE sends PRACH on PSCell
Agreements:
Focus on Case 1 in Slide #3
Reuse the agreement for SCell activation on known/unknown conditions for Power Class 1
  FFS for UE supporting Power Class 2/3/4