## Slide 1: WF on improving EN-DC configuration tables in 38.101-3
Nokia, Nokia Shanghai Bell
R4-1904912

## Slide 2: Agreements in online session
Agreement: Remove the whole tables in 5.2 while the information about SUO column is included in the table for two bands in 5.5.
Agreement: Remove columns for LTE CA and NR CA from the tables in 5.5
Agreement: Go with band combination basis approach by clarifying some restriction rule to use certain UL configurations.

## Slide 3: Removal of section 5.2B
Background: During online discussion it was agreed to remove the tables in clause 5.2 and SUO information is transferred into clause 5.5B.
However tables in clause 5.2 have also notes which have essential information such as mandatory simultaneous Rx/Tx capability.
Agreement: All notes from tables in clause 5.2 are transferred into clause 5.5B to corresponding Tables.

## Slide 4: Common band combination based grouping
DC_5A_n261A DC_5A_n261B DC_5A_n261C DC_5A_n261D DC_5A_n261E DC_5A_n261F DC_5A_n261G DC_5A_n261H DC_5A_n261I DC_5A_n261J | DC_5A_n261A DC_5A_n261D DC_5A_n261E DC_5A_n261F DC_5A_n261G DC_5A_n261H DC_5A_n261I DC_5A_n261J
DC_5A_n261(2A) DC_5A_n261(3A) DC_5A_n261(4A) DC_5A_n261(D-G) DC_5A_n261(D-H) DC_5A_n261(D-I) DC_5A_n261(D-O) | DC_5A_n261A DC_5A_n261(2A) DC_5A_n261(3A) DC_5A_n261(4A)
AGREEMENTS:
Grouping of EN-DC configurations is done based on common band combination
In case E-UTRA or/and NR has non-contiguous CA it will be on a separate row compared to cases when EN-DC configuration has only single carrier or contiguous CA operation

## Slide 5: Clarification on uplink support
Background:
Clarify in specification that valid uplink configurations are such that uplink does not have more carriers than downlink and
UL types should be consistent within a row, i.e. There should not be a mixture of contiguous and non-contiguous UL CA within a row (once NC UL CA is defined)
Agreement:
Text to be added prefereably to general section of 5.5B:
  If multiple UL DC configurations are indicated with multiple DL DC configurations, only UL DC configurations with the same or a lower number of carriers in the same fallback group are valid UL configurations
As an example DC_5A_n261C is not a valid uplink configuration for DC_5A_n261A

## Slide 6: The sequence of the EN-DC combinations
AGREEMENT:
DC configurations should be sorted by LTE band combination, then NR band combination
LTE combintions should be sorted by the first band number, then the first bandwidth character, then the second band number, then the second bandwidth character and so on
The same sort order should be applied for the NR part, there combinations with () should be sorted alphanumerically within the brackets after the contiguous combinations
Example:
DC_1A_n77A
DC_1A_n77C
DC_1C_n77A
DC_1C-2A_n77A
DC_41A-42A_n79A
DC_41A-42C_n79A
DC_41C-42A_n79A
DC_41C-42C_n79A
DC_41C-42C_n257A
DC_41C-42C_n257M
DC_41C-42C_n257(2A)
DC_41C-42C_n257(2A-2O)
DC_41C-42C_n257(8A)
DC_41C-42C_n257(D-G)