## Slide 1: WF on PC2 EN-DC (1 LTE TDD band + 1 NR TDD band)
CMCC, vivo, OPPO, CATT
3GPP TSG-RAN WG4 Meeting #90-bis R4-1904977
Xi’an, China, 8 – 12 April, 2019

## Slide 2: Background
In RAN#82 meeting, WID on Power Class 2 UE for EN-DC (1 LTE TDD band +1 NR TDD band) were approved [1]. The objective of the work item is to specify the RF requirements for Power Class 2 EN-DC (1 LTE band +1 NR band with 1Tx).
RAN4 need to specify UE Tx duty cycle requirements sufficient to prevent exceeding local regulatory limits such as SAR for inter-band PC2 EN-DC UE.
The following inter-band EN-DC were approved to support PC2 HPUE for 5G NR:
EN-DC configuration | Uplink EN-DC configuration
DC_39A-n41A | DC_39A-n41A
DC_39A-n79A | DC_39A-n79A
DC_41A-n79A | DC_41A-n79A

## Slide 3: Agreements
Introducing a new signaling which indicates that the NR maxUplinkDutyCycle capability corresponds to LTE UL/DL configuration and it is a per band combination capability
The values range of NR maxUplinkDutyCycle for PC2 inter-band EN-DC are from [20]% to 100% and the default value for NR uplink duty cycle can be specified according to different TDD configurations as following
LTE UL/DL Configuration (Uplink duty cycle) | 0 (60%) | 1 (40%) | 2 (20%) | 3 (30%) | 4 (20%) | 5 (10%) | 6 (50%)
Default value for NR maxUplinkDutyCycle (10% as granularity) | [40]% | [60]% | [80]% | [70]% | [80]% | [90]% | [50]%

## Slide 4: References
[1] RP-182877 New WID on Power Class 2 UE for EN-DC (1 LTE band +1 NR band). CMCC
[2] R4-1903024 SAR requirements for PC2 EN-DC (1 LTE TDD band + 1 NR TDD band). CMCC
[3] R4-1900468 Discussion on SAR requirement for EN-DC PC2 UE. CATT
[4] R4-1900257 Discussion on TDD inter-band NSA HPUE. OPPO
[5] R4-1903245 Further discussion on SAR requirement for EN-DC PC2 UE. CATT
[6] R4-1903054 Discussion on TDD inter-band NSA HPUE SAR. OPPO
[7] R4-1904660 Discussion on maximum duty cycle for TDD EN-DC HPUE. vivo