## Slide 1: WF for EN-DC FDD-TDD High Power UE CHTTL, China Unicom, SGS Wireless...
3GPP TSG-RAN WG4 Meeting #90bis R4-1904982 Athens, Greece, 25th Feb – 1nd March, 2019

## Slide 2: Backgrounds
The scope of PC2 FDD-TDD including the following two cases:
  Note: for case 1 and case 2, the duty cycles of NR TDD can be different.
  RAN4 study starts from case 1, but case 2 is not precluded.
  Example band combination for this study is DC_3_n78
A Wayforward R4-1902452 is agreed in RAN4#90
  Further aspects are discussed. [1]~[7]
 | EN-DC total power | LTE maximum power | NR maximum power
Case 1 | 26dBm | 23dBm | 23dBm
Case 2 | 26dBm | 23dBm | 26dBm

## Slide 3: Wayforward for PC2 FDD-TDD HPUE
Wayforward for RAN4#91:
Target on concluding a solution to solve SAR issue in RAN4#91, the solutions provided in this meeting can be further studied
  Study the feasibility of reporting combined maximum duty cycle capability between LTE and NR
  Study the feasibility solving SAR issue by only reporting one overall maximum duty cycle capability
  Study the feasibility of TDM patterns based on NR TDD configuration requested by operators as well as existing LTE TDD configurations
  UE centric solution can be further studied, including combining with network centric solution
Other solutions are not precluded
Background from last WF R4-1902452:
Further study the following solutions to meet the overall uplink duty cycle for the PC2 FDD-TDD HPUE, starting from case 1
  Option 1: Reduce Tx time for LTE FDD UL
    Restrict LTE FDD UL transmission by TDM patterns can be considered as the starting point for option 1
  Option 2: Reduce Tx power for LTE FDD UL
  Other options are not precluded

## Slide 4: Reference
  [1] R4-1903055 Discussion on NSA FDD-TDD HPUE SAR solutions OPPO
  [2] R4-1903296 Discussion on solutions for EN-DC FDD-TDD High Power UE CHTTL
  [3] R4-1903434 Further consideration on HPUE for inter-band FDD-TDD EN-DC OPPO
  [4] R4-1903631 Initial comparison of two option solutions to avoid HPUE exceeding SAR requirement China Unicom
  [5] R4-1903966 Increasing the configured EN-DC power for FDD-TDD (PC3 and PC2) Ericsson
  [6] R4-1904522 Further consideration on FDD+TDD HPUE Huawei, HiSilicon
  [7] R4-1904619 SAR mitigation for PC2 FDD-TDD EN-DC in FR1 Qualcomm Incorporated