## Slide 1: Simulator scenarios and assumptions for simulator alignment purpose
Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting RAN4#90bis R4-1905106
Xi’An, China, 8th April – 12th April 2019
Agenda: 8.5.1
Document for: Approval

## Slide 2: Background
In RAN#82, a WID on Integrated Access and Backhaul for NR (IAB) was approved in RP-182882
Among the objectives of the work item, RAN4 is tasked to define RF requirements for both backhaul (BH) and access links of an IAB-node including requirements for co-existence (e.g. ACLR, ACS)
In RAN4 #90bis meeting discussion started on simulation scenarios and assumptions for the purpose of simulator alignment

## Slide 3: Proposal on simulation scenario (1)
Impact of IAB network to a 5G NR network shall be analysed and new simulation results are needed
We propose to simulate the following scenario:
  Victim Network: Micro layer 5G NR network in hexagonal grid with 19 tri-sectorial sites operating access
  Aggressor Network: Non-collocated micro layer IAB network in hexagonal grid with 19 tri-sectorial sites operating backhauling
  Frequency range: FR2
Simulation methodology for creating victim network does not change compared to consolidated methodology
Simulation methodology for creating IAB aggressor network is proposed in slide 5

## Slide 4: Proposal on simulation scenario (2)
Figure 1: Simulation scenario for uncoordinated operation

## Slide 5: Proposal on simulation methodology for creating aggressor IAB network
Adopt the following simulation steps for creating the aggressor IAB network:
Aggressor IAB nodes are dropped in hexagonal grid
  100% grid shift from victim network
Choose the central site as donor site
  All three sectors of that site become donor sectors
Create network topology based on RSRP metric
  Children IAB nodes associate to parent IAB nodes based on coupling loss.
  Associations are made assuming a single element (no beamforming) at both children and parents IAB nodes.
Once network topology is formed, activate randomly N links subject to the following conditions:
  Each parent can only schedule one child at a time
  Half duplex constraint at IAB nodes: each IAB node can transmit/receive to/from only one other IAB node
  The value N of active backhauling links cannot be determined a-priori because it depends on the network topology
BF weights are adjusted to point to the LOS direction between communicating IAB nodes

## Slide 6: Proposal on simulation assumptions
Victim Network Parameters (5G access network) |  | Aggressor Network Parameters (IAB backhaul network) | 
Layout | Urban Micro layer: Hexagonal Grid with 19 tri-sectorial sites | Layout | Urban Micro layer: Hexagonal Grid with 19 tri-sectorial sites Number of IAB-donors (): 1 site (3 sectors) Number of tri-sectorial IAB-nodes is: 19 –
Wrap-around | Yes | Wrap-around | Yes
Inter-site distance (ISD) | 200m | Inter-site distance (ISD) | 200m
Topology formation | N.A. | Topology formation | Parent-node RSRP as input to the IAB-node parent-node selection.
Carrier frequency | 30GHz | Carrier frequency | 30GHz (Adjacent channel)
Duplex mode | TDD | Duplex mode | TDD
System bandwidth | 400MHz | System bandwidth | 400MHz
Large-scale channel parameters | Micro-to-Micro: UMi-Street canyon (hUE =10m). | Large-scale channel parameters | Micro-to-Micro: UMi-Street canyon (hUE =10m) The path loss for links between the IAB-node and candidate serving IAB-nodes/donors is determined based on N =3 independent large-scale channel realizations (taking into account LOS/NLOS probability and shadow fading). The realization that results in the minimum pathloss between the IAB-node and the associated serving IAB-node/donor is selected.
gNB Tx power | 33dBm | IAB node Tx power | 33dBm
gNB antenna configurations | 16x8 Antenna Array Vertical and Horizontal element spacing: | IAB node antenna configurations | 16x8 Antenna Array Vertical and Horizontal element spacing:
gNB antenna height | 10 m | IAB node antenna height | 10 m
gNB antenna element gain | 3dBi | IAB node antenna element gain | 3dBi
gNB receiver noise figure | 10dB | IAB node receiver noise figure | 10dB
Victim Network Parameters (5G access network) |  | Aggressor Network Parameters (IAB backhaul network) | 
Layout | Urban Micro layer: Hexagonal Grid with 19 tri-sectorial sites | Layout | 
Wrap-around | Yes | Wrap-around | Yes
Inter-site distance (ISD) | 200m | Inter-site distance (ISD) | 200m
Topology formation | N.A. | Topology formation | Parent-node RSRP as input to the IAB-node parent-node selection.
Carrier frequency | 30GHz | Carrier frequency | 30GHz (Adjacent channel)
Duplex mode | TDD | Duplex mode | TDD
System bandwidth | 400MHz | System bandwidth | 400MHz
Large-scale channel parameters | Micro-to-Micro: UMi-Street canyon (hUE =10m). | Large-scale channel parameters | Micro-to-Micro: UMi-Street canyon (hUE =10m) The path loss for links between the IAB-node and candidate serving IAB-nodes/donors is determined based on N =3 independent large-scale channel realizations (taking into account LOS/NLOS probability and shadow fading). The realization that results in the minimum pathloss between the IAB-node and the associated serving IAB-node/donor is selected.
gNB Tx power | 33dBm | IAB node Tx power | 33dBm
gNB antenna configurations |  | IAB node antenna configurations | 
gNB antenna height | 10 m | IAB node antenna height | 10 m
gNB antenna element gain | 3dBi | IAB node antenna element gain | 3dBi
gNB receiver noise figure | 10dB | IAB node receiver noise figure | 10dB