## Slide 1: Modification for filler bits option 10
Huawei, HiSilicon
3GPP TSG-RAN WG4 #90BIS Meeting
Xi’an, China, 08th – 12th April, 2019
Agenda Item: 6.8.3.3
Document for : Information
R4-1905120

## Slide 2: Option 10
2 symbols (control region)
12 symbols
(PDSCH)
(PDSCH 2)
(PDSCH 1)
(PDSCH)
(PDSCH C)
(PDSCH C)

## Slide 3: Design guideline
Keep designs as similar for FR1 and FR2
Minimize changes as much as possible
Use RNTI as basis to map PDSCH in slot
Boosting test models require some additional work for the different mappings

## Slide 4: Basic ideas
1) Associate RNTI number to default PDSCH properties in a new table
2) determine modifications for TM1.1 (3.1)
3) determine modifications for TM2
4) determine modifications for TM1.2 (TM3.2. TM3.3)
5) determine RNTI usage
PDCCH
RNTI = 2 starts on third symbol, same EPRE as PDCCH, 3 RBs wide
RNTI = 0 or 1, starts on first symbol, same EPRE as PDCCH

## Slide 5: Modify / Add Table 4.9.2.3.2-1 in 38.141-1, 38.141-2
Test model |  | Number of users
NR-FR1-TM1.1 | 2 for PRBs located in RB#0-2 0 for remaining PRBs | 2
NR-FR1-TM1.2 | 0 for boosted PRBs 1 for de-boosted PRBs 2 for PRBs located in RB#0-2 | 3
NR-FR1-TM2 | 2 for all PRBs | 1
NR-FR1-TM2a | 2 for all PRBs | 1
NR-FR1-TM3.1 | 2 for PRBs located in RB#0-2 0 for remaining PRBs | 2
NR-FR1-TM3.1a | 2 for PRBs located in RB#0-2 0 for remaining PRBs | 2
NR-FR1-TM3.2 | 0 for QPSK PRBs 1 for 16QAM PRBs 2 for PRBs located in RB#0-2 | 3
NR-FR1-TM3.3 | 0 for 16QAM PRBs 1 for QPSK PRBs 2 for PRBs located in RB#0-2 | 3
Test model |  | Number of users
NR-FR1-TM1.1 | 2 for PRBs located in RB#0-2 0 for remaining PRBs | 2
NR-FR1-TM1.2 | 0 for boosted PRBs 1 for de-boosted PRBs 2 for PRBs located in RB#0-2 | 3
NR-FR1-TM2 | 2 for all PRBs | 1
NR-FR1-TM2a | 2 for all PRBs | 1
NR-FR1-TM3.1 | 2 for PRBs located in RB#0-2 0 for remaining PRBs | 2
NR-FR1-TM3.1a | 2 for PRBs located in RB#0-2 0 for remaining PRBs | 2
NR-FR1-TM3.2 | 0 for QPSK PRBs 1 for 16QAM PRBs 2 for PRBs located in RB#0-2 | 3
NR-FR1-TM3.3 | 0 for 16QAM PRBs 1 for QPSK PRBs 2 for PRBs located in RB#0-2 | 3

## Slide 6: TM1.1/3.1 modification
Parameter | Value
# of QPSK PDSCH PRBs | NRB - 3
Ratio of PDSCH EPRE to PDCCH EPRE | 0 dB
Starting RB for DSCH PRBs | 3
Modulation of PRBs with nRNTI=2 | QPSK?
PDCCH
PDSCH RNTI=2
PDSCH RNTI=0

## Slide 7: TM2 modification
PDCCH
PDSCH RNTI=2
No spec change except to change RNTI usage
PDSCH RNTI=2
PDSCH RNTI=2

## Slide 8: Boosting TMs
Shift RBG notion by 3 RBs.
Consequence is locations must be specified
  Actual boosted ratio changes
Use resource allocation type 1 for the physical layer mapping
P=2
old
Option 10
Legend
PDCCH
RNTI=2
RNTI=0
RNTI=1

## Slide 9: TM1.2 (similar ideas for other TMs)
Parameter | Value
Percent of QPSK PDSCH PRBs boosted (target) | x=40%
# of QPSK PDSCH RBGs which are boosted | , where P is determined from table 5.1.2.2.1-1 from TS 38.214 [18], configuration 1 column using NRB-3 for BWP size
Level of boosting (dB) | 3
Locations of PDSCH RBs which are boosted | [3+Pk, …, 3+P(k+1)-1] where k= and
# of QPSK PDSCH PRBs which are deboosted | 
Level of deboosting (dB) | 
nRNTI = 2 | 
Ratio of PDSCH EPRE to PDCCH EPRE | 0 dB
# of RBs | 3
Modulation | QPSK
Parameter | Value
Percent of QPSK PDSCH PRBs boosted (target) | x=40%
# of QPSK PDSCH RBGs which are boosted | 
Level of boosting (dB) | 3
Locations of PDSCH RBs which are boosted | 
# of QPSK PDSCH PRBs which are deboosted | 
Level of deboosting (dB) | 
nRNTI = 2 | 
Ratio of PDSCH EPRE to PDCCH EPRE | 0 dB
# of RBs | 3
Modulation | QPSK

## Slide 10: Reference Documents
[1] R4-1903984, “Further discussion on NR TM configurations,” ZTE
[2] R4-1903985, “draft CR to TS38.141-01 on NR FR1 test model(Section 4.9.2) ,” ZTE
[3] R4-1903987, “draft CR to TS38.141-02 on NR FR2 test model(Section 4.9.2) ,” ZTE
[4] R4-1904077, “Further Aspects towards NR Test Model Design,” Ericsson
[5] R4-1904078, “Draft CR to TS 38.141-1: Section 4.9.2.2 NR FR1 Test Models,” Ericsson
[6] R4-1904079, “Draft CR to TS 38.141-1: Section 4.9.2.3 Data content of physical channels and signals,” Ericsson
[7] R4-1904080, “Draft CR to TS 38.141-2: Section 4.9.2.3 Data content of physical channels and signals,” Ericsson

## Slide 11: Discussion

## Slide 12: Boosting TMs (idea 1)
If P>2
  Replace 3 RBs of first RGB with PDSCH RNTI=2
If P=2
  Replace first RBG and half of second RBG with PDSCH RNTI=2
  Determine boosting
P=2
P=4
old
Option 10
Option 10
old
Legend
PDCCH
RNTI=2
RNTI=0
RNTI=1

## Slide 13: Boosting TMs (idea 2)
Shift RBG notion by 3 RBs.
Consequence is locations must be specified
  Actual booed ratio changes
P=2
P=4
old
Option 10
Option 10
old
Legend
PDCCH
RNTI=2
RNTI=0
RNTI=1