## Slide 1: WF for UE requirement type study within the 7 -24 GHz
Huawei, HiSilicon
R4-1905197
3GPP RAN4 WG Meeting #90bis Xi’an, China, April 8 – 12, 2019

## Slide 2: Background
The UE RF requirement type within 7-24GHz is discussed from the RF component performance, potential Architecture and testability perspevtives
  [1] is proposed to define UE RF requirement with overlapping approach: 7.125-12GHz with FR1 like implementation, 12 - 24.25 GHz with FR2 like implementation, 10 – 14 GHz accommodating both implementations.
  [2] is proposed to define ‘X’ within 7-24GHz for FR1 type extension, possible RF architecture and different UE type is considered when discussing on FR2 type extension.
  [3] is proposed to define 7.125-10GHz UE RF requirement as conducted type, frequency higher than 10GHz is for further study
  Existing performance of connector and probe technology for conducted test is provided in [4], up to 12GHz can be tested with conducted type is shown in the paper.

## Slide 3: WF on UE RF requirement type for 7-24 GHz
Study on frequency range applicable for conducted type and OTA type
Study the feasibility on UE RF requirement type from following perspectives:
  RF architecture and UE type
  System performance imapct on RF requirements,e.g. ACLR
  Antenna size volume
  PA average output power with applicable power consumption for UE
  Filter with different type,e.g. LTCC, LC, SAW.
  Testability on conducted type and OTA type
  Other perspectives is not preclued
It is encouraged to provide RF component performance data within 7-24GHz for UE in the next meeting

## Slide 4: Reference
[1] R4-1903513 ” 7.125 - 24.25GHz Frequency Range from a UE Perspective”, Skyworks
[2] R4-1903058 ”Views on FR1 boundary frequency in the 7-24 GHz frequency range” , Apple
[3] R4-1904481 ”Discussion On 7-24GHz UE RF requirement”, Huawei, HiSilicon
[4] R4-1903994 ” On performance of existing RF connector and probe technology”, LGE