## Slide 1: Way forward on R16 NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #90bis
Xi’an, China, 8 – 12 Apr, 2019
R4-1902869
Document for: Approval

## Slide 2: Agreements on DC-based handover
DC-based handover involving cells with different SCS is feasible, depending on UE capability of supporting different SCS.
  Note: extra UE complexity can be expected even for the UE which can support multiple SCS in serving cell.
DC-based handover in FR2 is not considered in this work item, unless the source and target cells are collocated (i.e. UE can use same Tx/Rx beam for both target and source cells) and UE has the QCL information.

## Slide 3: Agreements on make-before-break handover
Feasibility of make-before-break handover will be investigated based on assumption that UE will stop connection with source cell before preamble transmission to target cell.

## Slide 4: Agreements on RACH-less handover
RAN4 confirms the feasibility of RACH-less handover in FR1 with zero TA or same TA between source and target cells
  For both intra and inter-frequency scenarios
  For both synchronous and asynchronous deployment
  With same or different SCS in source and target cells
RACH-less handover to target cell in FR2 is possible, e.g. UE is provided with multiple UL grants which are associated with different directions.